## Slide 1: Modeling of once-through steam generators
William Davidsen
Supervisor: Sigurd Skogestad, IKP
Co-supervisor: Lucas F. Bernardino, SINTEF
Source: https://www.sintef.no/en/projects/2024/demo-cotsg/

## Slide 2: Introduction
Reduce GHG emissions from NCS
Main contributor: Gas turbines
Improve turbine efficiency by introducing a steam cycle (utilize flue gas energy)
Weight and space limitations on offshore installations

## Slide 3: System description
Add bottoming cycle to increase efficiency
Main focus on the once through steam generator (OTSG)

## Slide 4: Method
Discretization
Mathematical formulation
Model implementation

## Slide 5: General procedure
Discretization
Mathematical formulation
Model implementation
Discretization
Volume and area equally distributed
Assumptions
  perfect mixing
  No heat loss
  No thermal resistance

## Slide 6: Mathematical formulation
Discretization
Mathematical formulation
Model implementation
Mass and energy balances
Different equations for each phase
Simplifying assumptions
  Ideal gas
  Constant Cp
  Constant UA
  Homogenous flow

## Slide 7: Model implementation
Discretization
Mathematical formulation
Model implementation
Implementation: Matlab/Casadi
Solver: Idas/Sundials
Main c Switching of equations
Two switching points: Dew and bubble point
Can use vapor quality to detect switching points
Casadi built in if-else to evaluate symbolic variables

## Slide 8: Simulations
Constants and inlet conditions based on Zotică (2020)[1]
Steady state simulations
  Nominal operating point
Dynamic simulations
  Steps in relevant disturbances
  Shows switching of equations
Step in
[1} Cristina Zotică, Lars O. Nord, Jenö Kovács and Sigurd Skogestad. Optimal operation and control of heat to power cycles: A new perspective from a systematic plantwide control approach. URL: https://www.sciencedirect.com/science/article/pii/S0098135419311342

## Slide 9: Challenges & future work
Initialization issues
Noise in m and p
Heat transfer issues
Implement steam turbine and other units
Add control elements
Set desired geometry