## Slide 1: Advanced process control – A new beginning
Sigurd Skogestad
Department of Chemical Engineering
Norwegian University of Science and Technology (NTNU)
Trondheim
19th IFAC Symposium on Control, Optimization and Automation in Mining, Mineral and Metal Processing (IFAC MMM 2022)
August 15-17, 2022
Montreal, Canada
Thanks to: Adriana Reyes-Lúa, Cristina Zotică, Dinesh Krishnamoorthy, Krister Forsman

## Slide 2
Trondheim
Arctic circle
Geiranger fjord
Trondheim

## Slide 3: About Sigurd Skogestad
•1955: Born in Flekkefjord, Norway
• 1956-1961: Lived in South Africa
•1974-1978: MS (Siv.ing.) studies in chemical engineering at NTNU
•1979-1983: Worked at Norsk Hydro co. (process simulation)
•1983-1987: PhD student at Caltech (supervisor: Manfred Morari)
•1987-present: Professor of chemical engineering at NTNU
• 1994-95: Visiting Professor UC Berkeley
• 2001-02: Visiting Professor UC Santa Barbara
•1999-2009: Head of ChE Department, NTNU
•2015-..: Director SUBPRO (Subsea research center at NTNU)
Non-professional interests:
mountain skiing (cross country)
orienteering (running around with a map)
grouse hunting
1973

## Slide 5
Advanced process control - a new beginning
Sigurd Skogestad, NTNU, Norway
Abstract (for short version, delete the parts in red)
Control engineers rely on many tools, and although some people may think that in the future there will be one general universal tool that solves all problems, like economic model predictive control (EMPC), this is not likely to happen. The main reason is that the possible benefits of using more general tools may not be worth the increased implementation costs (including modelling efforts) compared to using simpler "conventional" advanced process control (APC) solutions. In particular, this applies to process control, where each process is often unique. In addition, for a new process, a model may not be available, so at least for the initial period of operation a conventional scheme must be implemented. Control is about implementing optimal operation in practice under varying conditions (disturbances, prices, etc.). Most people think that on-line optimization (RTO) is needed to achieve this, but in many cases it’s possible to put the optimization into the control layer using the magic of feedback.
Since its introduction in the 1940’s, about 80 years ago, conventional advanced process control (APC) has largely been overlooked by the academic community, yet it is still thriving in industrial practice, even after 40 years with model-based multivariable control (MPC). So it is safe to predict that conventional APC (including PID control) will not be replaced by MPC, but will remain in the toolbox along with MPC. Thus, it is time to give conventional APC a “new beginning” in terms of strengthening its theoretical basis and training engineers and students on how to use it in an effective manner.
Conventional APC includes the standard control elements that industry commonly uses to enhance control when simple single-loop PID controllers do not give acceptable control performance. Examples of such control elements are cascade control, selectors, split range control, input or valve position control (VPC), multiple controllers (and MVs) for the same CV, and nonlinear calculation blocks. The goal of this talk is to take a systematic view on how to design a conventional APC system. The starting point is usually optimal steady-state economic operation. The process may have many manipulated variables (MVs) for control (typically valves), but usually most of these are used to control “active” constraints, which are the constraints which optimally should be kept at their limits at steady state. For the remaining unconstrained degrees of freedom, we should look for self-optimizing variables, which are measured variables for which the optimal values depend weakly on the disturbances.
The starting point is then to design a good control system for the normal (nominal) operating point, preferably based on single-loop PID controllers where each manipulated variable (MV) which is not optimally at a constraint is paired with a controlled variable (CV). To handle interactions, disturbances and nonlinearity, one may add cascade control and calculation blocks.
However, during operation one may reach new (active) constraints, either on MVs or CVs, which may be easily observed from measurements of the potential constraints. Since the number of degrees of freedom doesn’t change, we will need to give up the control of another variable, which will either by another constraint (on CV or MV) or an unconstrained CV (self-optimizing variable). The key is then to know which variable give up, and in many cases we may determine this based on physical insight, and implement it using conventional APC elements. A key new observation is that there are only four cases of switching and these may be handled by using standard APC control elements. For CV-CV switching we use selectors (overrides), for MV-MV switching we use split range control or similar, for simple CV-MV switching (where the two variables are already paired) we don’t need to do anything (except for including anti-windup in the controller) and for complex CV-MW switching we need to combine CV-CV and MV-MV switching.
The main disadvantage with conventional APC compared to MPC is that it is based on single-loop controllers, so one needs to pair outputs (CVs) with inputs (MVs). For most processes this works well, but for more complex cases with many constraint switches one may get significant benefits and simplifications with MPC. Other cases where MP may offer significant benefits compared to conventional APC is for interactive processes and for cases with known future disturbances
In summary, optimal economic operation may in many cases be achieved by use of simple conventional APC elements, but there is a lack of understanding, both in industry and academia, on how such control systems should be designed. The presentation offers a new beginning in terms of providing a systematic approach.
Bio
Sigurd Skogestad received his Ph.D. degree from the California Institute of Technology, Pasadena, USA in 1987. He has been a full professor at Norwegian University of Science and Technology (NTNU), Trondheim, Norway since 1987. He is the principal author, together with Prof. Ian Postlethwaite, of the book "Multivariable feedback control" published by Wiley in 1996 (first edition) and 2005 (second edition). His research interests include the use of feedback as a tool to make the system well-behaved (including self-optimizing control), limitations on performance in linear systems, control structure design and plantwide control, interactions between process design and control, and distillation column design, control and dynamics. His other main interests are mountain skiing (cross country), orienteering (running around with a map) and grouse hunting. He is a Fellow of the American Institute of Chemical Engineers (2012) and IFAC (2014).

## Slide 6: “The goal of my research is to develop simple yet rigorous methods to solve problems of engineering significance”

## Slide 7: Outline
Introduction: Why do we need control?
Control: The two approaches to control
  Centralized: “One big controller”. Model predictive control (MPC) and EMPC
  Decomposed: PID, Conventional advanced Process control (APC)
Conventional APC elements
Using conventional APC to handle Optimization – with changing active constraints
  Many examples
  PID-control, Selectors, Split range control
Conclusion

## Slide 8
How should we use the inputs u (valves)?
How use measurements y?
What should we control? and why?
Where do we start?
etc.
etc.
Tennessee Eastman challenge problem (1991)
How design a control system for a complete plant?
Notes: 8

## Slide 9: Control is about implementing optimal operation
Given process plant
Want to Maximize profit P => Minimize cost J=-P [$/s]
  J = cost feed + cost energy – value products
    Excluding fixed costs (capital costs, personell costs, etc)
Subject to satisfying constraints on
    Products (quality)
    Inputs (max, min)
    States
Degrees of freedom = manipulated variables (MVs) = inputs u
What is Optimal operation?

## Slide 10
In theory: Centralized controller is always optimal (e.g., EMPC)
Objectives
Present state
Model of system
Approach:
  Model of overall system
  Estimate present state
  Optimize all degrees of freedom
Process control:
  Excellent candidate for centralized control
Problems:
  Model not available
  Objectives = ?
  Optimization complex
  Tuning
  Not robust (difficult to handle uncertainty)
  Slow response time
(Physical) Degrees of freedom, u= valve positions
CENTRALIZED
OPTIMIZER

## Slide 11: In practice: Hierarchical decision system based on time scale separation
Degrees of freedom, u= valve positions

## Slide 12: Notation
MV = Manipulated Variable = Input (u)
CV = Controlled Variable = Output (y)
DV = Disturbance Variable (d)
Process
MV
CV
DV
Controller
CV
MV
DV

## Slide 13: Main objectives control
ARE THESE OBJECTIVES CONFLICTING?
IS THERE ANY LOSS IN ECONOMICS?
Usually NOT
  Different time scales
    Stabilization fast time scale
  Stabilization doesn’t “use up” any degrees of freedom
    Reference value (setpoint) available for layer above
    But it “uses up” part of the time window
Economics: Implementation of optimal operation (changing setpoint)
Regulation: Stable (non-drifting) operation (around given setpoint)

## Slide 14: Hierarchical structure: Degrees of freedom unchanged
No degrees of freedom lost as setpoints y2s replace inputs u as new degrees of freedom for control of y1
G
CPID
y2s
u
y2
y1
u=Original DOF
y2s=New DOF
Cascade control:

## Slide 15: Two ways of decomposing the control system
Vertical (hierarchical; cascade)
Based on time scale separation
Decision: Selection of CVs that connect layers
Horizontal (decentralized)
Usually based on distance
Decision: Pairing of MVs and CVs with layers
CV1
CV2

## Slide 16: Control layers
Sometimes divided in two
Supervisory (“advanced”) control:
  Follow set points for CV1 from economic optimization layer
  Switch between active constraints (change CV1)
  Look after regulatory layer (avoid that MVs saturate, etc.)
  Implementation:
  Alternative 1: APC: “Advanced control” based on ”simple elements”
  Alternative 2: MPC: Model predictive control
Regulatory control (PID):
  Stable operation (CV2)
CV = controlled variable
PROCESS
(day)

## Slide 17: Supervisory control: Conventional APC vs. MPC
Need both in our toolbox
Conventional APC («advanced regulatory control»):
  More general than most people think
  In many cases it’s all you need
  But: May get complex for larger problems
  But: Cannot handle all cases
  Need something before you consider a MPC project
MPC needed for more complex problems
  Main problem MPC: Need dynamic model
  Costly to implement and maintain
  Requires experts

## Slide 18: Conventional advanced process control (APC)
Also called: Advanced regulatory control (ARC)
«Advanced» is a relative term: When single-loop PID is not sufficient.
Common APC elements:
  Cascade control
  Feedforward control / Ratio control
  Decoupling
  Selectors
  Split range control (SRC)
  Multiple controllers for same CV
  Valve (input) position control (VPC)
Can handle constraint changes

## Slide 19
Standard control element | Solution to task | Input | Output
E1. Linear feedback controller (PID) with anti-windup | T1 | CV | MV
E2. Cascade control. | T2 | CV1, CV2 | MV
E3. Feedforward control | T3 | DV | MV
E4. Decoupling element | T4 | MVd | MV
E5. Ratio control | T3, T4 | SP, DV or MV | MV
E6. Nonlinear element | T5 | u (scalar) | y=f(u)
E7. Calculation block | T2, T3, T4, T5 | u | y=f(u)
E8. Split-range control | TS1. TS4 | CV | MV1, MV2, …
E9. Multiple controllers for the same CV | TS1, TS4 | CV | MV1, MV2, …
E10. Valve (input) position control (VPC) | T6, TS1, TS4 | CV=MV1 | MV2
E11. Selector | TS2, TS4 | CV1, CV2, … (MV1, MV2, …) | MV
E12. Gain scheduling | T5 | CV | MV
E13. Simple dynamic element | T11 | u | y (=u static)
E14. Soft sensor (static calculation block) | T12 | u | CV=f(u)
Standard APC control elements

## Slide 20: Conventional «Advanced» process control (APC)
  Extensively used by industry
    Has been around since 1930’s
    Present form: Since 1960’s
    Supported by all control vendors (Honeywell, Yokogawa, ABB, etc.)
  Literature
    Industry: Book by Donald Eckman (1945) and books by Greg Shinskey (1967-1981)
    Almost completely ignored by academic researchers (except Luyben case studies)
  Problem for engineers: Lack of theory and design methods
  Main fundamental limitation: Based on single-loop (need to choose pairing)

## Slide 21
Alan Foss (“Critique of chemical process control theory”, AIChE Journal,1973):
The central issue to be resolved ... is the determination of control system structure. Which variables should be measured, which inputs should be manipulated and which links should be made between the two sets? There is more than a suspicion that the work of a genius is needed here, for without it the control configuration problem will likely remain in a primitive, hazily stated and wholly unmanageable form. The gap is present indeed, but contrary to the views of many, it is the theoretician who must close it.
Some academic interest:
Stephanoplous, Morari, Skogestad
Balchen, Åstrøm, Hägglund
Notes: 21

## Slide 22: Rest of the talk
Show how to use simple control elements for optimal operation under changing constraints

## Slide 23: MV-CV Pairing Two main rules
“Pair-close rule”
  The MV should have a large, fast, and direct effect on the CV.
“Input saturation rule”
  Pair a MV that may saturate with a CV that can be given up (when the MV saturates)
Process
MV
CV
DV

## Slide 24: Changing active constraints and APC Two main cases
MV-MV switching
  Need many MVs to cover whole steady-state range
  Use only one MV at a time
  Three options: 1. Split range control, 2. Different setpoints, 3. Valve position control (VPC)
CV-CV switching («override»)
  Must select between CVs
  Only one option: Many controllers with Max-or min-selector
Plus the combination. CV-MV switching (because MV saturates)
3. Simple: CV can be given up (follow «input saturation rule»)
  Don’t need to do anything (except anti-windup in controller)
4. Complex: CV cannot be given up
  Combine MV-MV switching (three options) with CV-CV switching (selector)
Process
Process
Process
Process
Adriana Reyes-Lua and Sigurd Skogestad, Systematic Design of Active Constraint Switching Using Classical Advanced Control Structures, Ind.Eng.Chem.Res, 2020

## Slide 25: MV-MV switching
Need several MVs to cover whole steady-state range (because primary MV may saturate)
Note that we only want to use one MV at the time.
Three main solutions for “selecting the right MV”:
  Alt.1: A. (Standard) Split-range control (SRC) (one controller)
  B. Generalized SRC (many controllers)
  Alt.2 Many controllers with different setpoints
  Alt.3 Valve position control
In addition: MPC
Which is best? It depends on the case!
* Adriana Reyes-Lua Cristina Zotica, Sigurd Skogestad, «Optimal Operation with Changing Active Constraint Regions using Classical Advanced Control,, Adchem Conference, Shenyang, China. July 2018 ,
Process
A. Reyes-Lúa and S. Skogestad. “Multi-input single-output control for extending the operating range: Generalized split range control using the baton strategy”. Journal of Process Control 91 (2020)

## Slide 26: Example MV-MV switching
Break and gas pedal in a car
MV-MV switching

## Slide 27: Split range control: Donald Eckman (1945)
MV-MV switching

## Slide 28
Alt. 1A. Split-range control (SRC)
MV-MV switching
C – same controller for all inputs (u1, u2)
But can get different gains by adjusting the slopes in the SR-block
v = internal signal
A. Reyes-Lúa, C. Zotica, K. Forsman, S. Skogestad, Systematic design of split range controllers,
12th IFAC Symposium on Dynamics and Control of Process Systems, Including Biosystems (DYCOPS), Florianópolis, Brazil, 2019.

## Slide 29
MVs:
AC (expensive cooling)
CW (cooling water; cheap)
HW (hot water, quite cheap)
Electric heat, EH (expensive)
y=T
Example: Room heating/cooling with 4 MVs
Alt. 1A. Split-range control (SRC)
MV-MV switching
d=Tamb
CPI – same controller for all inputs (one integral time)
But get different gains by adjusting slopes α in SR-block

## Slide 30
Alt. 1B. Generalized SRC (Baton strategy: multiple independent controllers)
Disadvantages Alt. 1A. Standard Split-range control (SRC):
Must use same integral/derivative time for all MVs
Does not work well when constraint values change (SR-block problem)
MV-MV switching
y=T
A. Reyes-Lúa and S. Skogestad. “Multi-input single-output control for extending the operating range:
Generalized split range control using the baton strategy”. Journal of Process Control 91 (2020)
d=Tamb
All four controllers need anti-windup

## Slide 31
Alt. 1B. Generalized SRC (Baton strategy: multiple independent controllers)
Disadvantages Alt. 1A. Standard Split-range control (SRC):
Must use same integral/derivative time for all MVs
Does not work well when constraint values change (SR-block problem)
MV-MV switching
y=T
A. Reyes-Lúa and S. Skogestad. “Multi-input single-output control for extending the operating range:
Generalized split range control using the baton strategy”. Journal of Process Control 91 (2020)
d=Tamb
All four controllers need anti-windup

## Slide 32: Simulation of standard and generalized SRC
Generalized split range control:
Different (smaller) integral times for each input
Gives faster settling for most inputs
A. Reyes-Lúa and S. Skogestad. “Multi-input single-output control for extending the operating range:
Generalized split range control using the baton strategy”. Journal of Process Control 91 (2020)
MV-MV switching

## Slide 33: What about Model Predictive control (MPC)?

## Slide 34: Comparison of Generalized SRC and MPC
Responses
MPC: Similar response to standard SRC
MPC: Faster initially, uses several input simultanously
MPC: Slower settling
Disadvantage MPC:
Complex: Requires full dynamic model
Does not use on input at a time
Uses both heating and cooling at the same time
  See at t=300 min (not optimal economics)
A. Reyes-Lúa and S. Skogestad. “Multi-input single-output control for extending the operating range:
Generalized split range control using the baton strategy”. Journal of Process Control 91 (2020)
MV-MV switching

## Slide 35
y=T
Disadvantages Alt. 1A Standard Split-range control (SRC):
Must use same integral time for all MVs
Does not work well when constraint values change
C1
C2
C3
C4
Ts1=23oC
Ts2=Ts1-1C=22oC
Ts3=Ts1-2C=21oC
Ts4=Ts1-3C=20oC
Advantages Alt. 2 :
Simple to implement (no logic)
Controllers can be tuned independently
Switching by feedback: Do not need to know constraint values
Disadvantage Alt. 2: Setpoint not constant
  Can be an advantage (gives energy savings for room heating)
  Fix: Use master controller on T (with setpoint Ts=22c) that resets the setpoint Ts1 (but keeps differences)
d=Tamb
MV-MV switching
Alt. 2. Multiple controllers with different setpoints
A. Reyes-Lúa, S. Skogestad, Multiple-input single-output control for extending the steady-state operating range—Use of controllers with different setpoints, Processes, 2019

## Slide 36
A Reyes-Lua, S Skogestad. Multiple-Input Single-Output Control for Extending the Steady-State Operating Range - Use of Controllers with Different Setpoints. Processes 7 (12), 941, 2019
Comparison of Alternatives 1 (SRC) and 2 (different setpoints)
d=Tamb
y=T
MV-MV switching

## Slide 37: Alt. 3. Input (valve) position control (VPC)
Advantage: Always control output y with same input (u1=MV1)
  Good if tight control of CV is important and cannot be achieved with u2=MV2
When u1 approaches saturation: Use u2 to control u1 (VPC)
  Disadvantages: Ecomomic loss because we cannot use full range for u1
  Example: With electric heat (u1=EH) to control temperature (y=T) we will use some heat also in summer
VPC
MV-MV switching

## Slide 38: CV-CV switching: Use selectors (only* option!)
Many CVs paired with one MV.
But only one CV controlled at a time.
Use: Max or Min selector
Sometimes called “override”
Selector is generally on MV (compare output from many controllers)
Process
Note: Selectors are logic blocks
>
MAX
=
HS
=
<
MIN
=
LS
=
*Selectors may be implemented in other ways, for example, using «if-then»-logic.
*In some cases a max- and min- selector in series may be replaced by a saturation element

## Slide 39: Furnace control
TC
u=Fuel gas
Flue gas
Process fluid (water)
Air
T1s = 500C
TC
T2max=700C
y1=T1
u1
u2
u=min(u1,u2)
Input (MV)
u = Fuel gas flowrate
Output (CV)
y1 = process temperature T1
(desired setpoint or max constraint)
y2 = furnace temperature T2
(max constraint)
Rule: Use min-selector for constraints that are satisfied with a small input
CV-CV switching
u = input = manipulated variable (MV)
y = output = controlled variable (CV)
MIN
with safety constraint
y2=T2
HP steam

## Slide 40: Furnace control with cascade (selector on CV)
TC
u=Fuel gas
Flue gas
Process fluid
Air
T1s = 500C
TC
T2max
MIN
y1=T1
y2=T2
u1
u2
CV-CV switching
T2s

## Slide 41: Design of selector structure
Rule 1 (max or min selector)
Use max-selector for constraints that are satisfied with a large input
Use min-selector for constraints that are satisfied with a small input
Rule 2 (order of max and min selectors):
If need both max and min selector: Potential infeasibility
Order does not matter if problem is feasible
If infeasible: Put highest priority constraint at the end
“Systematic design of active constraint switching using selectors.”
Dinesh Krishnamoorthy , Sigurd Skogestad. Computers & Chemical Engineering, Volume 143, (2020)
CV-CV switching

## Slide 42: Valves have “built-in” selectors
A min-flow (z=0) gives a “built-in” max-selector (to avoid negative flow)
A max-flow (z=1) gives a “built-in” min-selector
So it’s not necessary to add these as selector blocks (but it will not be wrong).
Another way to see this is to note that a valve works as a saturation element
CV-CV switching

## Slide 43: Example: Optimal operation of distillation column. Top product valueable
Always control xD at constraint
(valueable product) to
avoid «product give-way»
May overpurity bottom to get more of the valuable product
Avoid flooding using constraint on DP
CV-CV switching

## Slide 44: Example: Adaptive cruise control
CV-CV switching

## Slide 45: Challenges selectors
Standard approach requires pairing of each active constraint with a single input
  May not be possible in complex cases
Stability analysis of switched systems is still an open problem
  Undesired switching may be avoided in many ways:
    Filtering of measurement
    Tuning of anti-windup scheme
    Minimum time between switching
    Minimum input change
CV-CV switching

## Slide 46: CV-MV switching (because of constraint on MV)
Simple CV-MV switching
  Don’t need to do anything if we paired the MV with a CV that can be given up
Complex CV-MV switching
  This is a repairing of loops (CV-MV switching)
  Need to combine MV-MV switching with CV-CV-switching
The CV-CV switching always uses a selector
As usual, there are three alternatives for the MV-MV switching:
  Split range control (block /\): Has problems because limits may change
  Different setpoints for level. Actually, may have additional advantages
  Valve position control («long loop»). avoids repairing.
  + Shinskey-alternative

## Slide 47: Anti-surge control
F0
y=F
u=FR
FC
Fsp=Fmin
MAX
umin=0
MAX-block to avoid negative flow.
Not needed because the input (valve) has «built-in» selector, u ≥ 0.
Simple CV-MV switching
We satisfy the input saturation rule:
«When the MV (u) saturates, control of the CV (y) can be given up»

## Slide 48: Anti-windup
All the controllers shown need anti-windup to «stop integration» during periods when the control action (vi) is not affecting the process:
  Controller is disconnected (because of selector)
  Physical MV (ui) is saturated
Anti-windup using back-calculation. Typical choice for tracking constant, KT=1
KT,i
Selector or
saturation

## Slide 49: Example: Furnace control
TC
u=Fuel gas
Flue gas
Process fluid
Air
T1s = 500C
TC
T2max=700C
LS
y1=T1
y2=T2
uA
uB
u=min(uA,uB)
Furnace control : Cannot give up control of y1=T1. What to do?
Inputs (MV)
u = Fuel gas flowrate
u2 = Process flowrate
Output (CV)
y1 = process temperature T1
(with desired setpoint)
u2
MIN
Complex CV-MV switching

## Slide 50: Cannot give up controlling T1 Solution: Cut back on process feed (u2) when T1 drops too low
TC
u=Fuel gas
Flue gas
Process fluid
Air
T1s = 500C
TC
T2max=700C
LS
y1=T1
y2=T2
uA
uB
u=min(uA,uB)
TC
T’1s = T1s-5C=495C
u2
TC
Using Input-input switching
Inputs (MV)
u = Fuel gas flowrate
u2 = Process flowrate
Output (CV)
y1 = process temperature
(with desired setpoint)
Note: Standard Split Range Control (Alt. 1) is not good here.
Could be two reasons for too little fuel
  Fuel is cut back by override (safety)
  Fuel at max,
So don’t know limit for MV1 to use in SRC-block.
Complex CV-MV switching
u = input = manipulated variable (MV)
y = output = controlled variable (CV)
MIN

## Slide 51: Use Alt. 2: Two controllers
TC
u=Fuel gas
Flue gas
Process fluid
Air
T1s = 500C
TC
T2max=700C
LS
y1=T1
y2=T2
uA
uB
u=min(uA,uB)
Inputs (MV)
u = Fuel gas flowrate
u2 = Process flowrate
Output (CV)
y1 = process temperature
(with desired setpoint)
TC
T’1s = T1s-5C=495C
u2
Complex CV-MV switching
u = input = manipulated variable (MV)
y = output = controlled variable (CV)
MIN
  Solution: Two controllers with different setpoints

## Slide 52
Alt. 4. Shinskey. Flooded condenser,
y1
y2
u2
u1
Two controllers (TC for y3, PC for y1) are in some cases competing for the same input (u1), but PC wins because of the smart use of anti-windup back to TC, which stops TC from working (integrating) when the input from PC is non-zero
Complex CV-MV switching + CV-CV switching (Alt. 4)
Comment: Alt.2 with two controllers (PC) works fine here and is simpler,
See next page.
y3
Normally: Use u1 to control y3, and u2 to control y1
When y2 reaches min: Must use to u2 to control y2, and since y1 cannot be given up we must do a repairing of loops where y3 is given up and u1 is used to control y1

## Slide 53: Examples: Important insight
Many problems: Optimal steady-state solution always at constraints
In this case optimization layer may not be needed
  if we can identify the active constraints and control them using selectors

## Slide 54: Systematic design of simple advanced controllers (APC)
First design simple control system for nominal operation
  With single-loop PID control we need to make pairing between inputs (MVs) and outputs (CVs):
  Should try to follow two rules
    «Pair close rule» (for dynamics).
    «Input saturation rule»:
Process

## Slide 55: Systematic design of simple advanced controllers (APC)
Then make a list of possible new contraints that may be encountered (because of disturbances, parameter changes, price changes)
Reach constraint on new CV
  Simplest: Find an unused input (simple CV-MV switching)
  Otherwise: CV-CV switching using selector (may involve giving up a CV-constraint or a self-optimizing CV)
Reach constraint on MV (which is used to control a CV)
  Simplest (If we followed input saturation rule):
    Can give ip controlling the CV (Simple CV-MV switching)
    Don’t ned to do anything
  Otherwise (if we cannot give up controlling CV)
    Simplest: Find an unused input
      MV-MV switching
    Otherwise: Pair with a MV that already controls another CV
      Complex CV-MV switching
      Must combine MV-MV and CV-CV switching
Is this always possible? No, pairing inputs and outputs may be impossible with many constraints.
May then use MPC instead

## Slide 56
Disturbance
F2 [m3/s]
Example : Level control
LC
SP
FC
F1,m
F1,s
F1 [m3/s]
MV1 = z1 (inflow valve position)
MV2 = z2 (outflow valve position) (likely to saturate)
CV1 = F1 (inflow): Should be controlled at setpoint F1,s (if possible)
CV2 = level: must always be controlled (at some SP)
Problem: outflow-valve may saturate at fully open (z2=1) and then we lose level control
Note: We did not following the “input saturation rule” which says:
Pair MV that may saturate (z2) with CV that can be given up (F1)
z2
z1
Nomimal design with “pair-close” rule
Process

## Slide 57
Disturbance
LC
Nominal design with Reverse pairing (follows “input saturation rule”):
FC
SP
F1,m
F2,s
BUT with Reverse pairing: Get “long loop” for flow control
In addition: loose control of y2= level if z1 (F1-valve) saturates
F1 [m3/s]
F2 [m3/s]
«long loop»
This gives simple CV-MV switching (if z2 saturates at fully open)
«Long loop» = Works through other loops

## Slide 58
Disturbance
LC
FC
SP-L
F1,m
F1,s
Alternative solution: Follow “Pair close”-rule and use Complex CV-MV switching.
When z2 saturates at max, use the other MV (z1) for level control and give up controlling F1
Get: “Bidirectional inventory control”
LC
SP-H
MIN
F1 [m3/s]
F2 [m3/s]
Avoid long loop for control of F1
Works both when F1-valve or F2-valve saturate at open
Overall: seems to be the best solution
LC
Using
MV-MV
switching
This is complex CV-MV switching

## Slide 59
Disturbance
LC
FC
SP-L
F1,m
F1,s
Recommended: Two controllers
SP-L = low level setpoint
SP-H = high level setpoint
LC
SP-H
MIN
F1 [m3/s]
F2 [m3/s]
Use of two setpoints is good for using buffer dynamically!!
Alternative solution: Follow “Pair close”-rule and use Complex CV-MV switching.
When z2 saturates at max, use the other MV (z1) for level control and give up controlling F1
Get: “Bidirectional inventory control”
This is complex CV-MV switching

## Slide 60: Generalization of bidirectional inventory control
Reconfigures automatically with optimal buffer management!!
F.G. Shinskey, «Controlling multivariable processes», ISA, 1981, Ch.3
Cristina Zotica, Krister Forsman, Sigurd Skogestad ,»Bidirectional inventory control with optimal use of
intermediate storage», Computers and chemical engineering, 2022
,
Max flow:
Fs=∞

## Slide 61
F0=1
F2=1
F3=1
F1=1
1
=∞
=∞
=∞

## Slide 62
F0=1
F2=1
F3=1
F1=0.5
1
=∞
=∞
0.5

## Slide 63
F0=0.5
F2=1
F3=1
F1=0.5
1
0.5
=∞
=∞

## Slide 64
F0=0.5
F2=0.5
F3=1
F1=0.5
1
0.5
=∞
=∞

## Slide 65
F0=0.5
F2=0.5
F3=0.5
Fully open
1
=∞
=∞
=∞

## Slide 66
F0=1
F2=1
F3=1
F1=1
1
=∞
=∞
Challenge: Can MPC be made to do his? Optimally reconfigure loops and find optimal buffer?
YES. Give unachievable high setpoints on all flows

## Slide 67
Extension . Bidirectional inventory control with minimum flow for F2
Max flow:
Fs=∞
IC
min
max
F2min
Level M (medium) in Unit 2 is the new «normal low» level.
M should be large to keep F2>F2min for a temporary drop in F1
M may be set by the operators (because they may know about expected stops)
Note: The order of selectors is important
Gets complicated…… but not sure if MPC can be made to work
M
F0
F1
F2
F3
Fs
16 July 2022

## Slide 68: Implementing optimal operation Summary
Most people think
  You need a detailed nonlinear model and an on-line optimizer (RTO) if you want to optimize the process
  You need a dynamic model and model predictive control (MPC) if you want to handle constraints
  The alternative is Machine Learning
No! In many cases you just need to measure the constraints and use PID control
  «Conventional advanced process control (APC)»
How can this be possible?
  Because optimal operation is usually at constraints
  PID-controllers can be used to identify and control the active constraints
  For unconstrained degrees of freedom, one often have «self-optimizing» variables
This fact is not well known, even to control professors
  Because most APC-applications are ad hoc
  Few systematic design methods exists
Today APC (ARC) and MPC are in parallel universes
  Both are needed in the control engineer's toolbox

## Slide 69: Conclusion
Put optimization into the control layer
  It’s much faster and more effective
Conventional Advanced process control (APC) works very well in many cases
  Optimization by feedback
    Self-optimizing control
    Active constraint switching
  Need to pair input and output.
    Advantage: The engineer can specify directly the solution
    Problem: May not be possible for complex cases
  Need model only for parts of the process (for tuning)
  Conventional APC: A new beginning needed in terms of developing theory and design methods

## Slide 70
Optimal centralized
Solution (EMPC)
Sigurd (me)
Academic process control community fish pond
Simple solutions that
work (selector, PID++)