## Slide 1: SIMPLE RULES FOR ECONOMIC PLANTWIDE CONTROL
Simple Rules for Economic Plantwide Control, PSE & ESCAPE 2015
Vladimiros Minasidisa, Sigurd Skogestada, Nitin Kaisthab aDept. of Chemical Engineering, Norwegian University of Science and Technology, Trondheim, Norway bDept. of Chemical Engineering, Indian Institute of Technology, Kanpur, India
Notes: The thematic content of the series:
1 Facts
Revenue from the last two years; Localization; History and surroundings
2 Research
Six strategic areas; Three Centres of Excellence; Laboratories; Cooperation with SINTEF;
3 Education and student activities
Study areas and programmes of study; Quality Reform; Further- and continuing education; Internationalization
4 Innovation and relationships with business and industry
Innovative activities; Agreements with the public and private sectors
5 Dissemination
Publications, events and the mass media
Museum of Natural History and Archaeology, NTNU Library
6 Organization and strategy
Board and organization; Vision, goal and strategies;
For more on terminology, see www.uhr.no/informasjon/index.htm (“terminologiliste”)
See also www.ntnu.no/intersek/english_matters/ (”Selected administrative terms with translations”)

## Slide 2: OUTLINE
INTRODUCTION
PROCEDURE FOR ECONOMIC PLANTWIDE CONTROL
REACTOR-SEPARATOR-RECYCLE CASE STUDY
PRACTICAL RULES
DYNAMIC SIMULATIONS
CONCLUSIONS

## Slide 3: HOW TO DESIGN THE CONTROL SYSTEM FOR A COMPLETE PLANT ?
NEED A SYSTEMATIC APPROACH
Famous critique article on process control by Foss (1973):
The central issue to be resolved ... is the determination of control system structure. Which variables should be measured, which inputs should be manipulated and which links should be made between the two sets?
There is more than a suspicion that the work of a genius is needed here, for without it the control configuration problem will likely remain in a primitive, hazily stated and wholly unmanageable form. The gap is present indeed, but contrary to the views of many, it is the theoretician who must close it.

## Slide 4: MAIN OBJECTIVES FOR A CONTROL SYSTEM
Economics: Implementation of close-to-optimal economic operation
Regulation: Stable operation
ARE THESE OBJECTIVES CONFLICTING?
Usually NOT
  Different time scales
    Stabilization fast time scale
  Stabilization doesn’t “use up” any degrees of freedom
    Reference value (setpoint) available for layer above
    But it “uses up” part of the time window (frequency range)

## Slide 5
PRACTICAL OPERATION: HIERARCHICAL STRUCTURE
Manager
Process engineer
Operator/RTO
Operator/”Advanced control”/MPC
PID-control
u = valves
Our Paradigm
CV1

## Slide 6
Decompose the structural decisions into two parts:
Top-down part, which attempts to find a slow-time-scale supervisory control structure that achieves a close-to-optimal economic operation.
Figure 1: Typical control hierarchy in a chemical plant
ECONOMIC PLANTWIDE CONTROL PROCEDURE

## Slide 7
Decompose the structural decisions into two parts:
Top-down part, which attempts to find a slow-time-scale supervisory control structure that achieves a close-to-optimal economic operation.
Bottom - up part, that aims to design a stable and robust fast-time-scale regulatory control structure, which stabilizes the plant and follows the setpoints from the supervisory layer.
Figure 1: Typical control hierarchy in a chemical plant
ECONOMIC PLANTWIDE CONTROL PROCEDURE

## Slide 8
Top Down
    Step S1: Define operational objectives (optimal operation)
      Cost function J (to be minimized)
      Operational constraints
    Step S2: Identify degrees of freedom (MVs) and optimize for expected disturbances
    Step S3: Select primary controlled variables CV1 (economic CVs)
    Step S4: Where to set the production rate? (TPM)
Bottom Up
    Step S5: Regulatory / stabilizing control (PID layer)
      What more to control CV2 (stabilizing CVs)?
      Pairing of inputs and outputs
    Step S6: Supervisory control (MPC layer)
    Step S7: Real-time optimization (Do we need it?)
ECONOMIC PLANTWIDE CONTROL STEPWISE PROCEDURE (Skogestad, 2004)

## Slide 9: ECONOMIC PLANTWIDE CONTROL
Top-down part (mainly steady-state): :
Step S1: Define the operational objectives (economics) and constraints.
  Identify
    A scalar cost function J
      J = cost feed + cost energy – value products
    operational constraints
    disturbances d and their ranges
Two main cases (modes/regions) depending on market conditions:
  Mode 1. Given feedrate
  Mode 2. Maximum production (max feedrate)

## Slide 10: ECONOMIC PLANTWIDE CONTROL
Top-down part (mainly steady-state): :
Step S2: Determine the degrees of freedom and find the steady-state optimal operation.
  Must optimize for the range of expected disturbances d
  Requires a rigorous model (usually steady-state)
  POTENSIALLY VERY TIME CONSUMING
  Main goal: Identify the ACTIVE CONSTRAINTS

## Slide 11: ECONOMIC PLANTWIDE CONTROL
Top-down part (mainly steady-state): :
Step S3: Select primary (economic) controlled variables (CV1)
  Identify the candidate measurements ym and from these select a set CV1 (one CV for each steady-state degree of freedom):
    Control the active constraints!
    For the remaining unconstrained degrees of freedom:
    Control “self-optimizing” variables
Figure 1: Typical control hierarchy in a chemical plant

## Slide 12: “Self-optimizing” variables: Controlled variables (CV1), which when kept at constant setpoint, indirectly achieve close-to-optimal operation in spite of unknown disturbances
Minimize the need for re-optimization

## Slide 13: Famous example – Marathon runner:
d
ny
ym
H
CV2s
CV1s
CV1
Objective: Minemise J=T
Any self-optimizing variable to control ?
CV1 = Hym ?
CV1 = Speed?
Disturbance (d) = hill
Candidate measurements (ym): speed, heart rate, …
CV=speed
J=T
d=hill
CVopt
Loss

## Slide 14: Famous example – Marathon runner:
d
ny
ym
H
CV2s
CV1s
CV1
CV1 = Hym ?
CV1 =
Disturbance (d) = hill
Candidate measurements (ym): speed, heart rate, …
CV=heart
rate
J=T
d=hill
CVopt
Objective: Minemise J=T
Any self-optimizing variable to control ?
SELF-OPTIMIZING VARIABLE:

## Slide 15: ECONOMIC PLANTWIDE CONTROL
Top-down part (mainly steady-state):
Step S4: Select the location of throughput manipulator (TPM)
  Q: Where should the plant’s “gas pedal” (TPM) be located ?
    Usually one for each plant
    The location of the TPM is a dynamic issue but has an economic impact
  A: Often located at the feed, but
    to maximize throughput (Mode 2), should be located close the production bottleneck
    to avoid “snowballing”, locate inside recycle loop

## Slide 16: ECONOMIC PLANTWIDE CONTROL
Bottom-up part (mainly dynamic):
Step S5: Select the control structure for the Regulatory Control layer
  Q1: What variables (CV2) should be controlled to stabilize the plant operation ?
  A1: Select “drifting” process variables CV2 = H2ym that need to be controlled to ensure safe and stable operation e.g. inventories, pressures, temperatures.
  Q2: How should CV2 be controlled (pairing)?
  A2: Controllability analysis
Figure 1: Typical control hierarchy in a chemical plant

## Slide 17: ECONOMIC PLANTWIDE CONTROL
Bottom-up part (mainly dynamic):
Step S6: Select the control structure for the Supervisory (Advanced) Control layer
  How should the economic controlled variables CV1 be controlled ?
  (MVs: Setpoints CV2s to regulatory layer)
  Two alternatives:
  Multivariable controller (e.g. MPC)
  Mix of various “advanced” controllers including PID, selectors, feedforward…

## Slide 18: ECONOMIC PLANTWIDE CONTROL
Bottom-up part (mainly dynamic):
Step S7: Select the control structure for the Process Optimization layer (RTO)
  How should the optimal setpoints for CV1 be updated ?
  A good choice of controlled variables (CV1) may remove the need for this layer.
Figure 1: Typical control hierarchy in a chemical plant

## Slide 19: REACTOR-SEPARATOR- RECYCLE CASE STUDY (Luyben)
Feed F0 contains mostly A.
Reactor (CSTR)
  1st order A -> B reaction
  Constant temperature
Separator (distillation column)
  Distillate D (mostly A ): recycled back to CSTR.
  Bottom product B (mostly B )
  22 stages
  Constant pressure
  Constant relative volatility
Reactor-separator-recycle process
F0
B
D

## Slide 20: CASE STUDY: Step S1
Definition of optimal operation:
Given feedrate (Mode 1)
  J = cost feed + cost energy – value products J = cF F0 + cV VB – cB B
  Since F0 = B is given, this simplifies to min J = VB
Reactor-separator-recycle process

## Slide 21: CASE STUDY: Step S1
Definition of optimal operation:
Given feedrate (Mode 1)
  J = cost feed + cost energy – value products J = cF F0 + cV VB – cB B
  Since F0 = B is given, this simplifies to min J = VB
Operational constraints
  MR ≤ 2800 kmol
  VB ≤ 50 kmol/min
  xB ≤ 0.0105 (max. 1.05% A in product)
Reactor-separator-recycle process

## Slide 22: CASE STUDY: Step S2
Step S2: Determine the degrees of freedom and find the steady-state optimal operation.
Given pressure and reactor temperature:
6 dynamic manipulated variables (valves)
uD = {F0, VB, D, B, F, LT}
MD and MB have no steady-state effect and need to be controlled
Steady state and given feed:
3 steady-state degrees of freedom
  Step S3: Must find 3 economic variables to control (CV1)
  ???
Reactor-separator-recycle process

## Slide 23: 11 Practical rules (to HELP with THE REMAINING Steps)
“Plantwide control for dummies”

## Slide 24: PRACTICAL RULES for Step S3
Rule 1: Control the active constraints
  In general, process optimization is required to determine the active constraints.
  but a good engineer can often guess the active constraints.
Step S3: Selection of economic CV1

## Slide 25: PRACTICAL RULES for Step S3
Rule 1: Control the active constraints
  In general, process optimization is required to determine the active constraints.
  but a good engineer can often guess the active constraints
Rule 1A: The purity constraint of the valuable product is always active and should be controlled.
  To maximize valuable product and avoid product “give away”.
Step S3: Selection of economic CV1

## Slide 26: CASE STUDY
Rule 1: Control the active constraints
Rule 1A: The purity constraint of the valuable product is always active and should be controlled.
Case study: Both MR (max) and xB (purity valuable product) are active.
Need to find one more CV1
Reactor-separator-recycle process
Practical rules for Step S3: Selection of economic CV1
J=VB
u = LT
Unconstrained optimum

## Slide 27: PRACTICAL RULES for Step S3
Rule 2: (for remaining unconstrained steady-state degrees of freedom, if any): Control the “self-optimizing” variables.
  The two main properties of a good “self-optimizing” variable are:
    Ιts optimal value is insensitive to disturbances
      so F = ΔCV1,opt /Δd is small
    Ιt is sensitive to the plant inputs (= “flat optimum”)
      so the process gain G = ΔCV1/Δu is large
Step S3: Selection of economic CV1

## Slide 28: PRACTICAL RULES for Step S3
Rule 2: (for remaining unconstrained steady-state degrees of freedom, if any): Control the “self-optimizing” variables.
  The two main properties of a good “self-optimizing” variable are:
    Ιts optimal value is insensitive to disturbances (such that F = ΔCV1,opt /Δd is small)
    Ιt is sensitive to the plant inputs (so the process scaled gain G = ΔCV1/Δu is large).
The following rule combines the two desired properties:
Rule 2A: Select the set CV1 such that the “ratio” G-1F is minimized.
  This rule is often called the “Maximum scaled gain rule”.
Step S3: Selection of economic CV1

## Slide 29: CASE STUDY: Self-optimizing variables
Rule 2: (for remaining unconstrained steady-state degrees of freedom, if any): Control the “self-optimizing” variables.
  The two main properties of a good “self-optimizing” variable are:
    Ιts optimal value is insensitive to disturbances (such that F = ΔCV1,opt /Δd is small)
    Ιt is sensitive to the plant inputs (so the process scaled gain G = ΔCV1/Δu is large).
The following rule shows how to combine the two desired properties:
Rule 2A: Select the set CV1 such that the ratio G-1F is minimized.
  This rule is often called the “Maximum scaled gain rule”.
Practical rules for Step S3: Selection of economic CV1
“Sensitive variables” (with large scaled gain):
Some good candidates for CV1,SOC : {LT/F , xD}.

## Slide 30: PRACTICAL RULES for Step S3
Rule 3: (for remaining unconstrained steady-state degrees of freedom, if any): Never try to control the cost function J (or any other variable with min or max at the optimal point).
  The cost function J has no sensitivity to the plant inputs so G = 0, (which violates Rule 2A)
Step S3: Selection of economic CV1

## Slide 31: PRACTICAL RULES for Step S3
Rule 3: (for remaining unconstrained steady-state degrees of freedom, if any): Never try to control the cost function J (or any other variable with min or max at the optimal point).
  The cost function J has no sensitivity to the plant inputs at the optimal point and so G = 0, which violates Rule 2A.
  Potential infeasibility :
Step S3: Selection of economic CV1
J
u

## Slide 32: CASE STUDY
Rule 3: (for remaining unconstrained steady-state degrees of freedom, if any): Never try to control the cost function J (or any other variable that reaches a min or max at the optimal point).
Case study: Do not keep VB constant (but may be used as a TPM)
Practical rules for Step S3: Selection of economic CV1

## Slide 33: PRACTICAL RULES for Step S4
Rule 4: Locate the TPM close to the process bottleneck.
  This is to be able to maximize the production rate (Mode 2)
  Gives a simpler transition between mode 1 (given feed) and mode 2
  (Process bottleneck is defined as the last constraint to become active when increasing the throughput rate.)
Rule 5: (for processes with recycle) Locate the TPM inside the recycle loop.
  This is to avoid “overfeeding” the recycle loop = “snowballing” (Luyben)
Step S4: Location of throughput manipulator (TPM)

## Slide 34: CASE STUDY
Rule 4: Locate the TPM close to the process bottleneck.
Rule 5: (for processes with recycle) Locate the TPM inside the recycle loop.
According to Rules 4 and 5 the best candidate for TPM location is VB.
Practical rules for Step S4: Location of throughput manipulator (TPM)

## Slide 35: PRACTICAL RULES for Step S5
Rule 6: Arrange the inventory control loops (for level, pressures, etc.) around the TPM location according to the radiation rule (Georgakis)
  This ensures “local consistency” i.e. all inventories are controlled by their local in or outflows.
Step S5: Structure of regulatory control layer
TPM
TPM
TPM

## Slide 36: PRACTICAL RULES for Step S5
Rule 7: Select “sensitive/drifting” variables as controlled variables CV2 for regulatory control.
  Typically include inventories (levels and pressures), reactor temperature, or a sensitive temperature in a distillation column.
Step S5: Structure of regulatory control layer

## Slide 37: PRACTICAL RULES for Step S5
Rule 8: Economically important active constraints (CV1) should be selected as CVs (CV2) in the regulatory layer.
  Economic variables CV1 are generally controlled in the supervisory layer.
  But moving CV1 to a faster layer may ensure tighter control with a smaller back-off.
Step S5: Structure of regulatory control layer

## Slide 38: PRACTICAL RULES for Step S5
Rule 9: (“Pair-close” rule): The pairings should be selected such that, effective delays and loop interactions are minimal.
Step S5: Structure of regulatory control layer

## Slide 39: PRACTICAL RULES for Step S5
Rule 10: Avoid using MVs that may optimally saturate (at steady state) to control CVs in CV2.
  The reason is that we want to avoid re-configuring the regulatory control layer.
  To follow this rule, one needs to consider also other regions of operation than the nominal.
Step S5: Structure of regulatory control layer

## Slide 40: CASE STUDY
Rule 7: Select “sensitive/drifting” variables as controlled variables CV2 for regulatory control.
  Typically include inventories (levels and pressures), reactor temperature, or a sensitive temperature in a distillation column
Rule 6: Arrange the inventory control loops (for level, etc.) around the TPM location according to the radiation rule.
Rule 8: Economically important active constraints (CV1) should be selected as CVs (CV2) in the regulatory layer
Rule 9: (“Pair-close” rule): The pairings should be selected such that, effective delays and loop interactions are minimal.
Rule 10: Avoid using MVs that may optimally saturate (at steady state) to control CVs in CV2.
Practical rules for Step S5: Structure of regulatory control layer

## Slide 41: PRACTICAL RULES for Step S6
Rule 11: MVs that may optimally saturate (at steady state) should be paired with the subset of CV1 that may be given up.
  This rule applies for cases when we use decentralized control in the supervisory layer and we have changes in active constraints
  The idea is to avoid reconfiguration of loops.
  This rule should be considered together with Rule 10.
Step S6: Structure of supervisory control layer

## Slide 42: CASE STUDY
Practical rules for Step S6: Structure of supervisory control layer
Two remaining degrees of freedom
  LT
  F
Have two remaining variables to control (CV1):
  Active constraint xB
  Self-optimizing variable xD

## Slide 43: CASE STUDY: Final control structure

## Slide 44: DYNAMIC SIMULATIONS
Initially the TPM is ramped to achieve 40% increase in fresh feed (F0), starting at 400 min till 600 min.
Later the TPM is ramped down to its original value, starting at 1800 min till 2000 min.
Important dynamic issue: TPM location

## Slide 45: Proposed structure: TPM at reboiler duty (VB)

## Slide 46: Alternative structure: TPM at feed (F0)

## Slide 47: Alternative structure: TPM at the product stream – B

## Slide 48: Alternative structure: TPM at the reactor effluent – F
Needs longer ramping time to be feasible

## Slide 49: Alternative structure: TPM at the recycle stream – D

## Slide 50: RESULTS: TPM at feed – F0
Figure 5:
TPM at the feed – F0. Self-optimizing CV – LT/F.

## Slide 51: RESULTS: TPM at the product stream – B
Figure 14:
TPM at the product stream – B. Self-optimizing CV – LT/F.

## Slide 52: Alternative structure: TPM at the product stream – B
Figure 12:
TPM at the product stream – B. LT- constant.

## Slide 53: RESULTS: TPM at feed – F0
Figure 3:
TPM at the feed - F0. LT – constant.

## Slide 54: RESULTS: TPM at the reactor effluent – F
Figure 4:

## Slide 55: RESULTS: TPM at the reactor effluent – F
Figure 6:

## Slide 56: RESULTS: TPM at reboiler’s steam supply – VB
Figure 6:
TPM at reboiler’s steam supply – VB. LT – constant.

## Slide 57: RESULTS: TPM at reboiler’s steam supply – VB
Figure 8:
TPM at reboiler’s steam supply – VB. Self-optimizing CV – LT/F.

## Slide 58: RESULTS: TPM at the recycle stream – D
Figure 9:
TPM at the recycle stream – D. LT – constant.

## Slide 59: RESULTS: TPM at the recycle stream – D
Figure 11:
TPM at the recycle stream – D. Self-optimizing CV – LT/F.

## Slide 60: CONCLUSIONS
SYSTEMATIC APPROACH TO PLANTWIDE CONTROL:
Define the cost function and operational constraints
Determine the active constraints
  possibly based on process insight
Find CV1’s for each steady-state degree of freedom:
  active constraints
  + "self-optimizing" unconstrained variables.
Determine the TPM location
Determine the structure of the control layers (pairing)
11 practical rules

## Slide 61: ECONOMIC PLANTWIDE CONTROL
SUMMARY AND REFERENCES
The following paper summarizes the procedure:
  S. Skogestad, “Control structure design for complete chemical plant”, Computers and Chemical Engineering, 28 (1-2), 219-234 (2004).
The following paper updates the procedure:
  S. Skogestad, “Economic plantwide control”, Book chapter in V. Kariwala and V.P. Rangaiah (Eds), Plant-Wide Control: Recent Developments and Applications”, Wiley (2012).
There are many approaches to plantwide control as discussed in the following review paper:
  T. Larsson and S. Skogestad, “Plantwide control: A review and a new design procedure”, Modeling, Identification and Control, 21, 209-240 (2000).
More information:
  http://www.nt.ntnu.no/users/skoge/plantwide