## Slide 1
An autonomous approach for driving systems towards their limit: an intelligent adaptive anti-slug control system for production maximization
Vinicius de Oliveira
Johannes Jäschke
Sigurd Skogestad
Department of Chemical Engineering,
NTNU, Trondheim, Norway
Two-phase pipe flow
(liquid and vapor)
Slug (liquid) buildup

## Slide 2
Outline
Explaning the slugging problem
Overview of the proposed method
    The autonomous supervisor layer
    The robust and adaptive control layer
Results
  How does the method perform in practice?
  How does it handle major disturbances?
  What if we use a bad baseline controller?

## Slide 3
The big picture

## Slide 4: The slug cycle

## Slide 5: The slug cycle (video)
Experiments performed by the Multiphase Laboratory, NTNU

## Slide 6: Slug cycle (stable limit cycle)
p1
p2
z

## Slide 7: Problems caused by severe slugging
Large disturbances in the separators
  Causing poor separation performance
  Can cause total plant shutdown  production losses!
  Increase flaring.
Large and rapid variation in compressor load
Limits production capacity (increase pressure in pipeline)

## Slide 8: How to avoid slugging?

## Slide 9: Avoid slugging: 1. Design change to avoid slugging
p1
p2
z
Expensive

## Slide 10: Minimize effect of slugging: 2. Build large slug-catcher
Most common strategy in practice
p1
p2
z
Expensive

## Slide 11: Avoid slugging: Close valve (but increases pressure)
p1
p2
z
Problematic for aging fields  increased pressure limits production
No slugging when valve is closed

## Slide 12: Avoid slugging: ”Active” feedback control

## Slide 13: Anti slug control: Full-scale offshore experiments at Hod-Vallhall field (Havre,1999)

## Slide 14: Problems with current anti-slug control systems
Tend to become unstable (oscillating) after some time
  Inflow conditions change
  Require frequent retuning by an expert  costly
Ideal operating point (pressure set-point) is unknown
  If pressure setpoint is too high  production is reduced
  If pressure setpoint is too low  system may become unstable

## Slide 15
Motivation
We want to increase valve opening
But larger openings = worse controllability
The lager the valve opening the more difficult it is to stabilize the system
      Controller gets more sensitive to uncertainties
      Process gain is reduced

## Slide 16
Our proposed autonomous control system
  Setpoint change is key for the adaptation to work well
Robust adaptive control
Plant
Autonomous supervisor
Periodically checks the stability of the system
Reduces setpoint if control loop is working fine

## Slide 17
How does it work?

## Slide 18
Adaptive control based on adaptive augmentation
Relies on state-of-the-art output feedback adaptive control techniques
     Very successful in the aerospace industry

## Slide 19
Adaptive control design
Open-loop system dynamics
Uncertainty model
control effectiveness uncertainty. Affects the process gain
state-dependent nonlinear uncertainty. Affects poles and zeros
matrix of unknown coefficients
vector of Lipschitz basis functions

## Slide 20
Adaptive control design
Define reference model
Output Feedback Adaptive Laws
Robust baseline + adaptive output feedback
     computed using your favorite method (PID, , LQG/LTR, …)
Feedback term to improve transient dynamics

## Slide 21
How does it perform in practice?

## Slide 22
2009-2013: Esmaeil Jahanshahi, PhD-work supported by Siemens
Experimental mini-rig
3m
its dynamical behavior is quite similar to that of much larger rigs
water+air mixture

## Slide 23
Experimental Results
Baseline controller tuned for Z=30%
Linearized mechanistic or simple empirical models can be used
  Note: our models agree very well with experiments

## Slide 24
Autonomous supervisor and adaptive LTR controller
Safely operates at very large valve openings

## Slide 25
Autonomous supervisor and adaptive LTR controller
Adaptation gains

## Slide 26
Oops, Big disturbance!
Emulates a ‘gas-to-oil’ ratio change over 60%

## Slide 27
Large change in the operating conditions
Supervisor quickly detects major disturbance
Moves to safer operating point
Adaptive control stabilizes under new operating conditions

## Slide 28
What happens if the baseline controller is poorly tuned?

## Slide 29
Poorly tuned PI control as baseline: Adaptation is OFF

## Slide 30
Poorly tuned PI control as baseline: Adaptation is ON
  Supervisor quickly detects major disturbance
Desired closed-loop performance is recovered!

## Slide 31
Comparison
Case | Mean valve opening | ISE
Bad baseline + adaptation OFF | 38,45 % | 6,2
Bad baseline + adaptation ON | 50,42% | 0,76
Good baseline + adaptation ON | 53,23% | 0,64
Large is good
Small is good

## Slide 32
Take home message
Our 2-layered anti-slug control system works very well in practice
The interaction between the two layers create a very nice synergy:
        Setpoint changes triggered by the supervisor makes the adaptation work well
        A well functioning adaptive control makes it possible to safely operate at large valve openings, thus maximizing production

## Slide 33
Take home message
    Expected benefits
    Stable and safe operation in a wide range of conditions
    Reduced need for control tuning
    Reduced workload on operators
    Increased production

## Slide 34
Thank you for your attention
`
    “A robust adaptive control system is key for reliable autonomous operation”

## Slide 35
Olga simulation
`
loopshaping vs. Adaptive LTR