## Slide 1: Production optimization using simple control loops
Dinesh Krishnamoorthy* and Sigurd Skogestad
NTNU, Trondheim, Norway
SUBPRO
SUBSEA PRODUCTION AND PROCESSING
*Also with Equinor (20%)

## Slide 2
Why did we start SUBPRO?
    Improve academic basis in selected subsea areas
    Provide the basis for future industrial innovation
43 PhD students/Postdocs in 8-year period
    12 completed PhD/postdoc projects
    16 ongoing PhD/Postdoc projects (as of April 2019)
    15 Planned new projects
21 Professors from three NTNU departments
    Chemical Engineering
    Geoscience and Petroleum
    Mechanical and Industrial Engineering
About 20 Master students every year
Annual budget: 3.5 million Euro
SUBPRO: Center for research-based innovation on subsea production and processing. 2015 - 2023
SUBPRO
7 Partners (2019):

## Slide 3
Project structure, 2015 – March 2019
SEPARATION - PROCESS CONCEPTS Prof. Hugo Jakobsen
Compact separation concepts
Characterization of fluid particle breakup in turbulent flow
H2S and hydrate control
Membranes for gas dehydration *
Membrane testing for gas dehydration
Mechanistic modeling of droplet breakage
SEPARATION – FLUID CHARACTERIZATION Prof. Johan Sjöblom/ Prof. Gisle Øye
Modeling of coalescence*
Wax crystallization and inhibition*
Produced water quality and
Injectivity*
Sequential separation*
Influence of production and EOR chemicals on produced water quality
SYSTEM CONTROL
Prof. Sigurd Skogestad
Ass. Prof. Johannes Jäschke
Control for extending component life
Estimation of un-measured variables*
Adaptive control of subsea processes
Modelling and* multivariable control of subsea processes
Dynamic simulation model library*
Production optimization
2 New PhDs late 2019
Automatic control of subsea separation
Enhanced virtual flow metering
Experimental validation of methods for optimizing remaining Useful Life
FIELD ARCHITECTURE
Prof. Sigbjørn Sangesland
Subsea gate box
Field development concepts *
Multiphase booster models
Methods for minimizing cost and risk in subsea field development
Condition based maintenance models*
RELIABILITY, AVAILABILITY, MAINTENANCE AND SAFETY (RAMS)
Prof. Mary Ann Lundteigen
New safety and control philosophy for subsea systems *
Reliability and availa-bility assessment in subsea design*
Optimizing condition monitoring
Safety 4.0 Demonstrating safety of novel subsea technologies
5 RESEARCH AREAS
30 PROJECTS
16 ongoing projects
* 12 completed projects
2 associated projects
Machine learning for production and process optimization
SUBPRO
Petrobras
Schlumberger
Technip FMC
«Did you copy our slides?»
Production optimization under uncertainty
Adriaen
Timur
Allyne
Otavio
Dinesh
Himanshu

## Slide 4: What are the challenges with Advanced Production optimization?
Technological limitations
Human aspects (probably the most important !)
SUBPRO

## Slide 5: Human aspects
Corporate culture
Technical Competence
Talent and knowledge number one barrier for adopting advanced technologies1
1Report from McKinsey & Company, Nov 2017
SUBPRO

## Slide 6: Technological limitations
Complex systems – lack of good models
Large chunks of data are discarded
Numerical robustness and computational issues
SUBPRO

## Slide 7: Maintenance
Special report on Process Control Sept 2006
SUBPRO

## Slide 8: Current needs of the industry
Need simple tools that do not require:
  Complex models
  Heavy data pre-processing
  Solving computationally intensive problems online
  Major overhaul of hardware or software infrastructure
  Frequent update and maintanence by expert engineers
SUBPRO

## Slide 9: Supervisory control layer
Alternative implementations:
Model predictive control (MPC)
Classical advanced control structures (PID, selectors, etc.)
RTO

## Slide 10: Model predictive control (MPC)
Can include constraints explicitly
If lack of DOF to meet control specifications:
  Conventional: Use weights
    (Partially) give up variables with small weights in objective function.
  Use two-stage MPC with constraint priority list:
    Stage 1. Check for steady-state feasibility and give up low-priority constraints if needed Stage 2. Solve conventional dynamic MPC

## Slide 11: Classical “Advanced control” structures
Cascade control (measure and control internal variable)
Feedforward control (measure disturbance, d)
    Including ratio control
Change in CV: Selectors (max,min)
Extra MV dynamically: Valve position control (=Input resetting =midranging)
Extra MV steady state: Split range control (+2 alternatives)
Multivariable control (MIMO)
    Single-loop control (decentralized)
    Decoupling
    MPC (model predictive control)
Extensively used in practice, but almost no academic work
CV = controlled variable (y)
MV = manipulated variable (u)

## Slide 12: Do we really need real-time optimization?
Often not!
We often know or can guess the active constraints
  Example: Assume it’s optimal with max. light ends in oil product (TVP).
  No need to have a complex dynamic model with energy balance and thermodynamics to find the optimal cooling
  Just use a PI-controller
    CV = flash temperature
    MV = cooling

## Slide 13: Systematic procedure for economic process control
Start “top-down” with economics (steady state):
Step 1: Define operational objectives (J) and constraints
Step 2: Optimize steady-state operation
Step 3: Decide what to control (CVs)
  Step 3A: Identify active constraints = primary CV1.
  Step 3B: Remaining unconstrained DOFs: Self-optimizing CV1 (find H)
Step 4: Where do we set the throughput? TPM location
Then bottom-up (dynamics):
Step 5: Regulatory control
  Control variables to stop “drift” (sensitive temperatures, pressures, ....)
Finally: Make link between “top-down” and “bottom up”
Step 6: “Advanced/supervisory control”
    Control economic CVs: Active constraints and self-optimizing variables
    Look after variables in regulatory layer below (e.g., avoid saturation)
Step 7: Real-time optimization (Do we need it?)
S. Skogestad, ``Control structure design for complete chemical plants'',
Computers and Chemical Engineering, 28 (1-2), 219-234 (2004).
CV1
CV2
Process
MVs
RTO

## Slide 14: Simple feedback controllers
No need for additional software development
Easy to commission
Easy to understand and maintain
Within the framework of safety and automation system (SAS)
Has been in use for several decades
SUBPRO

## Slide 15: Optimization with PI-controller
max y
s.t. y ≤ ymax
u ≤ umax
Example: Drive as fast as possible to Belo Horizonte (u=power, y=speed, ymax = 100 km/h)
Optimal solution has two active constraint regions:
  y = ymax  speed limit
  u = umax  max power
Note: Positive gain from MV (u) to CV (y)
Solved with PI-controller
  ysp = ymax
  Anti-windup: I-action is off when u=umax
s.t. = subject to
y = CV = controlled variable
ysp = ymax
PI
Active constraint control using PI-controller

## Slide 16: Optimization with PI-controller
The example:
Optimal operation: Switch between CV constraint and MV saturation
A simple PI-controller was possible because we followed the pairing rule:
  «Pair MV that saturates with CV that can be given up»
CV-MV switching

## Slide 17: Simple feedback controllers + logics
SUBPRO
CV-CV switching

## Slide 18: Switching between active constraints
1. Output to Output (CV - CV) switching (SIMO)
  Selector
2. Input to output (CV – MV) switching
  Do nothing if we follow the pairing rule: «Pair MV that saturates with CV that can be given up»
3. Input to input (MV – MV) switching (MISO)
  Split range control
  OR: Controllers with different setpoint value
  OR: Valve position control (= midranging control)
We are working on providing systematic procedures for the design of such control strategies

## Slide 19: The less obvious case: Unconstrained optimum
u: unconstrained MV
What to control? y=CV=?
  Self-optimizing variable
J
uopt
Jopt

## Slide 20: The ideal “self-optimizing” variable is the gradient, Ju
c =  J/ u = Ju
  Keep gradient at zero for all disturbances (c = Ju=0)
Unconstrained degrees of freedom
u
cost J
Ju=0
Ju<0
Ju<0
uopt
Ju
0
Problem: Usually no measurement of gradient
For Parallel units, optimal operation happens when gradients are equal
Notes: 20

## Slide 21
w_gl1
w_oil
w_gas
w_gl3
w_glN
w_gl2
Gas-lift optimization problem
How to optimally allocate the gas lift using simple PI controllers?
That is: Have N gas lifts (MVs). What should we control?
Limited gas lift supply
Gas processing constraint
Unconstrained operation

## Slide 22: Gas lift performance curves
Marginal Gas-lift-to-oil ratio (mGOR)
SUBPRO

## Slide 23
w_gl1
w_oil
w_gas
w_gl3
w_glN
w_gl2
Gas-lift optimization problem
Case 1: Limited Gas Lift supply
SP: 0
SP: 0
SP: 0
CV:mGOR2–mGOR1
CV:mGOR3–mGOR1
CV:mGORN–mGOR1
SP: w_gl_max
a
a
a
a
+

## Slide 24
w_gl1
w_oil
w_gas
w_gl3
w_glN
w_gl2
Gas-lift optimization problem
SP: 0
SP: 0
SP: 0
CV:mGOR2–mGOR1
CV:mGOR3–mGOR1
CV:mGORN–mGOR1
SP: w_gas_max
CV:w_gas
a
a
a
a
Case 2: Gas processing contraint

## Slide 25: Gas lift performance curves
Marginal Gas-lift-to-oil ratio (mGOR)
SUBPRO

## Slide 26
w_gl1
w_oil
w_gas
min select
Ctrl 1
Ctrl 2
Ctrl 3
SP: 0
Marginal GL-oil-ratio Controllers
SP: 0
SP: 0
w_gl3
w_glN
w_gl2
Gas-lift optimization problem
All 3 Cases combined

## Slide 27: Results

## Slide 28: Conclusion
Optimal operation using simple controller structures
Logics to switch between different operating regions
Beneficial for brownfield and late-life fields
Thank you !
SUBPRO
SUBSEA PRODUCTION AND PROCESSING