## Slide 1: An overview and evaluation of approaches for online process optimization
Sigurd Skogestad, Dinesh Krishnamoorthy
Department of Chemical Engineering
Norwegian University of Science and Technology, Trondheim, Norway
SUBPRO SUBSEA PRODUCTION AND PROCESSING
“Steady-state real-time optimization using transient measurements”, D. Krishnamoorthy, B. Foss, S. Skogestad, Comp. Chem. Eng.. 115, 34-45 (2018)
“A Feedback RTO strategy using Transient Measurements”, D. Krishnamoorthy, E. Jahanshahi, S. Skogestad, Ind.Eng.Chem.Res. (submitted 2018), Also ESCAPE Graz, 2018
“On combining extremum seeking control and self-optimizing control.” Straus. J, Krishnamoorthy, D., and Skogestad, S., J. Proc. Control (under revision, 2018).
AMCEDS workshop, Shanghai, 23 July 2018

## Slide 2
Trondheim
Arctic circle

## Slide 3: Outline
Introduction.
Why is traditional static RTO not used much?
Alternative approaches
  Dynamic RTO
  Hybrid RTO
  Feedback RTO
  Self-optimizing control
  Extremum seeking control
Case studies
  Gas lift, CSTR, Ammonia reactor

## Slide 4: Hierarchical decision system
Manager
Process engineer
Operator/RTO
”Advanced control”/MPC
PID-control
u = valves
min J (economics)
hour
Setpoint control
(+ look after other variables)
minute
Stabilize + avoid drift
second
Focus of this talk

## Slide 5: Real time optimization (RTO)
Process Model
Process constraints
Optimal decision variables
Economic Model

## Slide 6: Traditional static RTO
D. E. Seborg, D. A. Mellichamp, T. F. Edgar, F. J. Doyle III, Process dynamics and control, John Wiley & Sons, 2010.
Most common in commercial RTO
Steady-state models
Two-step approach
  “Data reconciliation”:
    Steady-state detection
    Update model parameters, disturbances (feed), constraints
  Re-optimize to find new optimal steady state
Data reconciliation

## Slide 7: Traditional static RTO
Minimize static economic cost
Steady-state wait time – fundamental limiting factor
Process operates sub-optimally for long periods of time
  Frequent disturbances
  Long settling times

## Slide 8: Why is traditional static RTO not commonly used?
Cost of developing and updating the model structure (costly offline model update)
Wrong value of model parameters and disturbances (slow online model update)
Not robust, including computational issues
Frequent grade changes make steady-state optimization less relevant
Dynamic limitations, including infeasibility due to (dynamic) constraint violation
It may seem that reasons 2, 4, and 5 suggest towards dynamic optimization.
However, except reason 4, static optimization may be close to the economic optimum, at a much lower computational cost.
In expected order of importance:
«wait time»

## Slide 9: Traditional static RTO: Long steady-state wait time
Challenges with steady-state detection
Erroneously accept transient data as stationary data
Large chunks of data discarded
Câmara MM, Quelhas AD, Pinto JC. Performance Evaluation of Real Industrial RTO Systems. Processes. 2016, 4(4).

## Slide 10: How to address steady-state wait time?
OBVIOUS: DYNAMIC RTO

## Slide 11: Dynamic real-time optimization (DRTO)
Uses all (transient) data
Dynamic models
Dynamic optimization is computationally intensive
Closely related to economic MPC
optimization

## Slide 12: Economic MPC ~ Dynamic RTO
Centralized “All-in-one” optimizer
Higher sampling rates
Hierarchical layers with time scale separation
Lower sampling rates
MPC/PID

## Slide 13: Dynamic RTO has problems
Slow and not robust
  Dynamic optimization is computationally expensive - even with today’s computing power
  Numerical issues, convergence problems
Mixed-integer variables
  Still an open problem, especially for dynamic problems

## Slide 14: How to address problems with dynamic RTO?
  Hybrid RTO
  Feedback based RTO

## Slide 15: Hybrid RTO
Dynamic Estimation
+
Static Optimization
Krishnamoorthy, D., Foss, B. and Skogestad, S., 2018. Steady-State Real-time Optimization using Transient Measurements. Computers and Chemical Engineering, Vol 115, p.34-45.

## Slide 16: CASE STUDY: Gas lift
Main objective: Max oil prod.
Constraint: Max Gas capacity
Main disturbance (d): GOR variation
Reservoir
GOR = Gas/Oil ratio in feed (reservoir)
MV1
MV2
Notes: s.t.
max┬(𝑤_𝑔𝑙 )⁡ $_𝑜 ∑▒𝑤_𝑝𝑜 −$_𝑔𝑙 ∑▒𝑤_𝑔𝑙 −$_𝑓𝑙 𝑤_𝑓𝑙
s.t.
∑▒𝑤_𝑝𝑔 ≤𝑤_𝑔^𝑚𝑎𝑥+𝑤_𝑓𝑙

## Slide 17: Disturbance: GOR variation

## Slide 18: Typical measured data (pressures and flowrates)

## Slide 19: GOR estimation - using “data reconciliation” (traditional static RTO)
Problem: Steady-state wait time for data reconciliation

## Slide 20: GOR estimation – using extended Kalman filter (DRTO & HRTO)

## Slide 21: Oil and gas rates
SRTO = traditional static RTO
HRTO = hybrid RTO
DRTO = dynamic RTO

## Slide 22: Results
Chart: 
| SRTO | HRTO | DRTO
Integrated Profit | 1.8256 | 2.7019 | 2.7509
Chart: Computation Time [s]
| SRTO | HRTO | DRTO
avg. time | 0.0184 | 0.0199 | 0.9025
max time | 0.0223 | 0.0282 | 3.3631

## Slide 23: Why is traditional static RTO not commonly used?
Cost of developing and updating the model structure (costly offline model update)
Wrong value of model parameters and disturbances (slow online model update)
Not robust, including computational issues
Frequent grade changes make steady-state optimization less relevant
Dynamic limitations, including infeasibility due to (dynamic) constraint violation
It may seem that reasons 2, 4, and 5 suggest towards dynamic optimization.
However, except reason 4, static optimization may be close to the economic optimum, at a much lower computational cost.
In expected order of importance:

## Slide 24
MV2: Setpoint provided to tracking controller
Actual MV move by setpoint tracking controller
Dynamic limitations – not a big issue
SRTO = traditional static RTO
HRTO = hybrid RTO
DRTO = dynamic RTO

## Slide 25: Discussion of Hybrid RTO
Addresses steady-state wait time issue
But Need to maintain two models – Static and Dynamic
  But not a big problem

## Slide 26: Advantage of steady-state optimization (SRTO & HRTO)
Computation time
Avoids causality issue
Allows optimization on decision variables other than the MVs
  Simplifies the optimization
  Slower time scale (choose slow varying variables as decision variables)

## Slide 27: Alternative feedback-based approaches
New: Feedback RTO (faster computation)
Self-optimizing Control (SOC) (no online model update needed)
Extremum-seeking control (model free). Closely related:
  Evolutionary control (60’s)
  Hill-climbing (Shinskey)
  NCO-tracking

## Slide 28
Hybrid RTO
Feedback RTO
Feedback RTO: Replace steady-state optimization by feedback control
Krishnamoorthy, D., Jahanshahi, E. and Skogestad, S., 2018. A feedback real-time optimization strategy, Ind. Eng. Res. Chem (submitted).

## Slide 29
Feedback RTO

## Slide 30
CSTR case study
Economou, C. G.; Morari, M.; Palsson, B. O. Internal model control: Extension to nonlinear system. Industrial & Engineering Chemistry Process Design and Development 1986, 25, 403–411.
Ye, L.; Cao, Y.; Li, Y.; Song, Z. Approximating Necessary Conditions of Optimality as Controlled Variables. Industrial & Engineering Chemistry Research 2013, 52, 798–808.

## Slide 31
Comparison of RTO approaches: MV
t = 400 s, d1: Increase CAin
t = 1400 s, d2: Increase CBin
closer look
SRTO = traditional static RTO
HRTO = hybrid RTO
DRTO = dynamic RTO
New method = Feedback RTO

## Slide 32
Comparison of RTO approaches
Chart: Computation time
| Feedback RTO | SRTO | HRTO | DRTO
 | 0.004 | 0.007 | 0.01 | 0.14
Chart: Integrated Loss
| Feedback RTO | SRTO | HRTO | DRTO
 | 248.07 | 342.38 | 257.97 | 247.68
2
4
3
1
248.1
342.3
257.1
247.1

## Slide 33
Feedback RTO - Other case studies
Evaporator process1
Gas lift wells2
Ammonia reactor3
Krishnamoorthy, D., Jahanshahi, E. and Skogestad, S., Control of steady-state gradient for an Evaporator process, PSE Asia (Submitted 2019)
Krishnamoorthy, D., Jahanshahi, E. and Skogestad, S., 2018. Gas-lift Optimization by Controlling Marginal Gas-Oil Ratio using Transient Measurements (in-Press), IFAC OOGP, Esbjerg, Denmark
Bonnowitz, H., Straus, J., Krishnamoorthy, D., and Skogestad, S., 2018. Control of the Steady-State Gradient of an Ammonia Reactor usingTransient Measurements, Computer aided chemical engineering, Vol.43, p.1111-1116 (ESCAPE 28)

## Slide 34
Self-optimizing control
Self-optimizing control is when we can achieve an acceptable loss with constant setpoint values for the controlled variables

## Slide 35
Challenges SOC:
Nonlinearity
Need new SOC variables for each active constraint region
  Similar to multiparametric optimization and lookup tables
Local approximation: c = Hy.
Need detailed steady-state model to find optimal H
  Nullspace method
  Exact local method
Must reoptimize for each expected disturbance
But calculations are offline
Self-optimizing control (SOC)

## Slide 36
CSTR case study
Krishnamoorthy, D., Jahanshahi, E. and Skogestad, S., 2018. A feedback real-time optimization strategy, Ind. Eng. Res. Chem (submitted).
Feedback RTO («new method»)
Self-optimizing control

## Slide 37: Why is traditional static RTO not commonly used?
Cost of developing and updating the model structure (costly offline model update)
Wrong value of model parameters and disturbances (slow online model update)
Not robust, including computational issues
Frequent grade changes make steady-state optimization less relevant
Dynamic limitations, including infeasibility due to (dynamic) constraint violation

## Slide 38
Challenges with structural uncertainty
Structural mismatch / unmodelled disturbances
  Model simplification
  Lack of knowledge
Modifier Adaptation
Model-free RTO approaches

## Slide 39
Model-free methods
Extremum seeking control
NCO-tracking
Hill-climbing control

## Slide 40
Serious challenges with model free methods
Needs cost measurement
Need additional perturbations
Steady-state limitation
Very slow convergence

## Slide 41
Fix: ESC/RTO + Self-optimizing control
Self-optimization control is always complementary
Can combine with
  Extremum-seeking control
  Traditional Static RTO
Straus. J, Krishnamoorthy, D., and Skogestad, S., 2018. On combining extremum seeking control and self-optimizing control. J. Proc. Control (under revision).

## Slide 42
Case study: Ammonia Reactor
Objective: Maximize extent of reaction
Response to disturbance in inlet mass flow rate
Bonnowitz, H., Straus, J., Krishnamoorthy, D., and Skogestad, S., 2018. Control of the Steady-State Gradient of an Ammonia Reactor usingTransient Measurements, Computer aided chemical engineering, Vol.43, p.1111-1116 (ESCAPE 28)

## Slide 43: Why is traditional static RTO not commonly used? Some alternatives
Cost of developing and updating the model structure (costly offline model update)
 Fix: model free methods, like extremum-seeking
2. Wrong value of model parameters and disturbances (slow online model update)
 Fix: DRTO, HRTO, self-optimizing control (fastest)
Not robust, including computational issues
 Fix: Feedback RTO, self-optimizing control
Frequent grade changes make steady-state optimization less relevant
 Fix: Dynamic RTO (DRTO) or EMPC
Dynamic limitations, including infeasibility due to (dynamic) constraint violation
 Fix: DRTO, EMPC

## Slide 44: Summary/Comparison on next slide
Red box = bad
green box = good
No box = neutral

## Slide 46: Proposal : Combine RTO with other approaches
ESC / modifier adaptation layer: make RTO approach the real optimum .
SOC layer: make optimization faster, reduce wait time for model update and online optimization

## Slide 47: Conclusion
Extremum seeking control/
Modifier adaptation
Self-optimizing control
(in MPC/PID layer)
Real-time optimization
(SRTO/DRTO/HRTO)
Process
d
u
cs
Ju,s
J
y
Measurements
H
y
y
c
Slow (hour)
Extremely slow (days)
Fast (minute)
Model free
RTO:
Detailed model
(online)
SOC:
Detailed model
(offline)
Thank you !
SUBPRO SUBSEA PRODUCTION AND PROCESSING
J
Gradient estimator
Ju