## Slide 1: Surrogate models for process optimization
Sigurd Skogestad, Julian Straus
Department of Chemical Engineering
Norwegian University of Science and Technology (NTNU)
Trondheim, Norway
Shenzen, 30 July 2018

## Slide 2: Abstract
Process optimization using commercial simulators is time consuming and unreliable. We generate surrogate models from simulations and
because simulations are time consuming it’s important to reduce the number of simulations (“samples”). The surrogate model is combined with the exact mass balances to avoid that the surrogate models needs to “learn” that mass is conserved. To make the surrogate model cover relevant operating conditions (which usually also means that strongly nonlinear regions are avoided) it’s important to select proper independent variables, and here we use ideas form control theory, including self-optimizing control. The work is based on the PhD thesis of Julian Straus (2018).

## Slide 3
Trondheim
Arctic circle

## Slide 4: Outline
Introduction / Motivation
Process knowledge incorporation  Grey box model
Independent variable reduction using partial least squares regression
Independent variable transformation using self-optimizing variables
Ammonia reactor case study
Conclusion

## Slide 5: 1. Introduction / Motivation
Plantwide control of an industrial ammonia plant
Need first to find optimal operation as function of disturbances
Steady-state simulation using HYSYS
    Complicated to converge and optimize

## Slide 6: Surrogate model
Detailed models often computationally expensive
Surrogate models reduce computation load
Surrogate model: Simple input (u)-output (y) representation
u
g’
model
y

## Slide 7: Ammonia reactor section
Example process: Ammonia synthesis process with 5 chemical components
Reactor section:
Inputs (u):
Disturbances, Here
connection variables (z)
Decision variables
3 split ratios, ui
Outputs (y):
Here, connection
variables (z)

## Slide 8: Whole ammonia synthesis process
u2
d2
(2) Reaction
z1,2
= y1,2
u1
d1
(1) SynGas MakeUp
Feed
d3
u3
(3) Separation/ Refrigeration
z3,1
= y3,1
z2,3
= y2,3
NH3

## Slide 9: Optimization of integrated process
  Original (steady-state) optimization problem:
  Split original model g into n submodels gi
  Obtain surrogate submodels gi’
  Combine surrogate models to overall model through connection variables
  Optimize new problem
  Straus, J., Skogestad, S.. Minimizing the complexity of surrogate models for optimization. Comput. Aided Chem. Eng., 38, 289-294, 2016.

## Slide 10: Develop surrogate model
Procedure:
Design of
Experiments
Simulation using
Detailed Model
Surrogate Model
Fitting
Adaptive sampling
Model
Validation

## Slide 11: Choice of surrogate model structure
Model structure depends on
  Application
  Required accuracy
Common surrogate model structures :
  Artificial neural networks
  Kriging models
  Regression models based on a set of basis functions
This work: Combine surrogate models with process knowledge to get grey-box model
 New model structure
 Reduces number of sampling points and gives consistency

## Slide 12: 2. Process knowledge incorporation I
Process knowledge:
  Mass balances
  Chemical reaction
How to incorporate this?
  Mass balances with extent of reaction x

## Slide 13: Process knowledge incorporation II
Auxiliary dependent variables (yaux)
Grey box model:
Surrogate
Model
Material Balances
yaux
u
y

## Slide 14: Process knowledge incorporation III
Sample regions which occur in practice
Feed around stoichiometric ratio:
Varying ratio
1000
2000
1800
1600
1400
1200
350
400
450
500
550
600
650
Individual
800

## Slide 15: 3. Independent variable reduction using partial least square (PLS) regression
“Curse of dimensionality”: Number of independent variables u (including disturbances) can be prohibitively high
PLS regression identifies new latent input variables (uk’)
  Straus, J. and Skogestad, S.. Variable reduction for surrogate modelling. In Proceedings of Foundations of Computer-Aided Process Operations 2017, Tucson, AZ, USA, 2017
PLS Dimension
Reduction
u’
Surrogate
Model
u
Material Balances
yaux
y

## Slide 16: Example: Ammonia process 1
Reaction section of an ammonia synthesis loop
  7 connection (feed) variables
  3 manipulated variables
  3 dependent variables
Grey box model structure
u
PLS variable
transformation
Surrogate model
Mass balances
PLS Dimension
Reduction
u’
Surrogate
Model
u
Material Balances
yaux
y
nS2
nS1
Thx
Surrogate model: 3-layer cascade-forward neural network with 3, 5, and 5 hidden neurons
Sampling points: 2 point regular grid + 5000 LHS points  6024 points
Notes: Comment to Sigurd: Subscript i dropped for sake of simplicity

## Slide 17: Results: Model error (Outlet Pressure)
1
2
3
4
5
6
7
8
9
max
[%]
0.00
0.25
0.20
0.15
0.10
0.05
0.30
3.50
0.73
0.46
Number of latent variables nu‘
0.000
0.025
0.020
0.015
0.010
0.005
0.030
1
2
3
4
5
6
7
8
9
[%]
Number of latent variables nu
0.856
0.191
0.056
Conclusion: Use 4 latent variables

## Slide 18: 4. Independent variable transformation using self-optimizing variables
We have “extra” degree of freedom (H): Change independent variables from u to
Main objective: Simpler response surface
Corresponding “control” structure:
H
K
Model
g(x,z,u,d)
u
d
y
c
-
x
cs
z
  Straus, J. and Skogestad, S.. Surrogate model generation using self-optimizing variables. Under review Comp. Chem. Eng. 2018.

## Slide 19: Illustrating example – Rosenbrock function
Rosenbrock function
Self-optimizing variable
Corresponding surrogate model:
  Second order terms instead of fourth order.

## Slide 20: Calculation of self-optimizing variables
Find measurement combinations Hi that have minimum loss (here: minimum model error) when disturbances occur
Include connection variables z in disturbances
Change of variables from u to c via self-optimizing control idea:
d
u
Model
g(x,z,u,d)
y
z

## Slide 21: 5. Case study: Ammonia reactor 2
Initial independent variables:
  Connection variable (Feed)
  Manipulated variables
Dependent variables
Cost function
Surrogate model: Cubic spline
Sampling points: 4 point regular grid  625 points

## Slide 22: Case study: Ammonia reactor
Local SOC variables for each of the 3 beds
Four variable combination tested
  IN: Inlet temperatures (3*1)
  IN-OUT: Inlet and outlet temperatures (3*2)
  OPT1: Best single SOC-temperature per bed (3*1)
  OPT2: Best two SOC-temperatures per bed (3*2)
SOC = self-optimizing control

## Slide 23: Results self-optimizing variables: Max. and average error
8 K
1.5 K
In
In-Out
Opt 1
Opt 2
0.0
1.0
0.8
0.6
0.4
0.2
1.2
max
[K]
0.00
0.15
0.12
0.09
0.06
0.03
0.18
[K]
Outlet Temperature Tout
4.35 %
0.74 %
In
In-Out
Opt 1
Opt 2
0.0
0.5
0.4
0.3
0.2
0.1
0.6
max
[%]
0.00
0.10
0.08
0.06
0.04
0.02
0.12
[%]
Extent of Reaction x

## Slide 24: Further SOC advantages
Allow simple mapping in neighbourhood of complicated regions
  Limit cycles
  Reactor extinction
Undesirable region not mapped
Limit cycles
SOC = self-optimizing control

## Slide 25: 6. Conclusion / Further work
Surrogate models useful in process systems engineering
Include process knowledge  Grey box model
Dimensionality reduction through variable transformations
  PLS
  Self-optimizing control  simpler surface
Thank you !

## Slide 27: Some previous work in PSE
Substitution of computational expensive models
  Eason, J. P. and Biegler, L. T.. A trust region filter method for glass box/black box optimization. AIChE J., 62 (9) 3124–3136, 2016.
  Cozad, A., Sahinidis, N. V., and Miller, D. C.. Learning surrogate models for simulation-based optimization. AIChE J., 60 (6) 2211–2227, 2014.
Solving integrated processes
  Straus, J., Skogestad, S.. Minimizing the complexity of surrogate models for optimization. Comput. Aided Chem. Eng., 38, 289-294, 2016.
And many more