## Slide 1: Optimal operation* of distillation columns using simple control structures
Sigurd Skogestad, NTNU, Trondheim
EFCE Working Group on Separations, Gøteborg, Sweden, June 2019
*Optimal in the meaning of economics or sustainability

## Slide 2: Distillation is part of the future
It’s a myth that distillation is bad in terms of energy
Better operation and control can save energy
Integrated schemes can save energy and capital
  Divided-wall / Petlyuk columns

## Slide 3: «Distillation is an inefficient process which uses a lot of energy»
This is a myth!
By itself, distillation is an efficient process.
It’s the heat integration that may be inefficient.
Yes, it can use a lot of energy, but it provides the same energy at a lower temperature
  Difficult separations (close-boiling): use a lot of energy -- but well suited for heat pumps
  Easy separations: Use little energy

## Slide 4: Typical distillation Case
Example 8.20 from Skogestad (2008)
Energy efficiency is only 5% (with no heat Integration)
Thermodynamic efficiency is 63%

## Slide 5
V
z
Qc
Qr
King’s formula:
(binary, feed liquid, constant α,
Infinite* no. Stages, pure products)
*Actual energy only 5-10% higher
Qr = reboiler duty [W]

## Slide 6: Ideal separation work
Minimum supplied work (for any process)
Ws,id= ΔH - T0ΔS
Assume ΔH=0 for the separation. Minimum separation work
Ws,id= - F T0 ΔS
Separation of feed into pure products
This is a negative number so the minimuim separation work Ws,id is positive!

## Slide 7
V
z
Qc
Qr
Ws
(g)
(g)
(l)
Low p
High p
(g)
Distillation with heat pump
Minimum work (Carnot)
Tc
TH

## Slide 8: Thermodynamic efficiency for conventional distillation
Thermodynamic Efficiency = Ideal work/Actual work:
Note that T0 drops out

## Slide 9: Thermodynamic efficiency Special case: Binary, constant α
King's formula
Ideal binary mixture (Claperyon equation) + no pressure drop. King shows:
So
Note that λ drops out
Binary

## Slide 10: Thermodynamic efficiency of binary close-boiling mixtures (
Comment: Above 50% for z from 0.2 to 0.8
Peak efficiency is -ln0.5 = 0.693 at z=0.5

## Slide 11: Thermodynamic efficiency of binary distillation
High efficiency at small z for easy separations with large α
Reason: Must evaporate light component to get it over top
z = fraction light component in feed

## Slide 12
Note: Non-ideality does not necessarily imply lower thermodynamic efficiency
King (1971)

## Slide 13: Why is it not perfect – where are the losses?
Irreversible mixing loss at every stage.
Largest losses in the middle of each section – where the bulk separation takes place
Small losses at the high-purity column ends

## Slide 14: Reversible binary distillation
Reversible binary distillation

## Slide 15: HIDiC (Heat Integrated Distillation Column)
I don’t believe in HIDiC.
Too complicated, too much investment, not enough savings

## Slide 16: Distillation is unbeatable for high-purity separations
Operation: Energy usage essentially independent of product purity
Capital: No. of stages increases with log(impurity)
Fenske: Nmin = ln S / ln α
Actual: N 2.5 Nmin
Separation factor:

## Slide 17: OPERATION

## Slide 18: Economics and sustainability for operation of distillation columns Is there a trade-off?
No, not as long as the column is operated in a region of constant (optimal) stage efficiency
Yes, if we operate at too high or too load so that the stage efficiency drops

## Slide 19: Can save a lot of energy by improved control
Especially by avoiding over-refluxing

## Slide 20: Acknowledgement
Ivar Halvorsen, NTNU (20%) and SINTEF (80%)

## Slide 22: Thermodynamic efficiency for conventional distillation
Use heat pumps for reboiler and condenser. Ideal work with surroundings at T0 (Carnot):
Assume feed liquid and constant molar flows so
Thermodynamic Efficiency = Ideal work/Actual work: