## Slide 1: Distillation is part of the future
Mamaia, Romania, Sept. 2019
Sigurd Skogestad, NTNU

## Slide 2
Abstract. Distillation is the most important separation process for liquids and it is an important part of the future of the chemical industry.
Some highlights of the talk:
Introduction: Importance of reflux
It’s a myth that distillation is bad in terms of energy
  Distillation is actually a thermodynamically efficient process
  Distillation is an ideal separation process if one has surplus heat.
Distillation is unbeatable for high-purity separations
Integrated schemes can save energy and capital
  Divided-wall / Petlyuk columns
For autonomous and energy-efficient batch distillation try multivessel distillation with closed operation
Azeotropes can be broken by using extractive agent and especially by making use of liquid-liquid splits
Better operation and control can improve quality and productivity
  It’s a myth that distillation columns are so slow
  Beware of using too much integral action in your controller

## Slide 3: Outline
Introduction. Importance of reflux
Myth about distillation being inefficient
Distillation unbeatable for high-purity separations
Integrated schemes. Divided-wall / Petlyuk
Multivessel batch distillation
Adding a component to break azeotropes
Control: Myth about slow response

## Slide 4: 1. Introduction
1512
Water distillation. 1483
1545
1593

## Slide 5
1972
What’s wrong?

## Slide 6: Batch distillation in wikipedia (2019)
L
D
V
Note: 1. Has column (multistage)
2. Has reflux

## Slide 7: Good design
Packed column (about 10 stages)
Adjustable reflux

## Slide 8: Strange design

## Slide 9: Good design for tuica
No column, no reflux
1 theoretical stage

## Slide 10: Vapor-liquid equlibrium for ethanol-water
X1: Mole fraction ethanol (1) in liquid
Y1: in vapor
.
Large activity cofficient:
Ethanol really does not like water
And water does not like ethanol
-> low-boiling azeotrope
100 C
78.4 C
78.1 C

## Slide 11: McCabe-Thiele
X1: Mole fraction ethanol (1) in liquid
Y1: in vapor
X=0.07 (14.5 vol%)
1 stage: Y=0.35 (55 vol%)
2 stages: Y=0.60 (77 vol%)
1
2
Infinite stages: Azeotrope at Y=0.92 (96 vol%)
3 stages: Y=0.70 (84 vol%)
3
.

## Slide 12: Finite reflux
X1: Mole fraction ethanol (1) in liquid
Y1: in vapor
.
Diagonal: reflux ratio is infinite
Blue line: reflux ratio is L/D=5
Red line: reflux ratio is zero (L=0)
3 stages: Y=0.675 (82 vol%)
1
2
3
3 stages: Y=0.35 (55 vol%)

## Slide 13: Reflux gives strange effects
With fixed product rate (D):
Must increase heat in the bottom to get lower temperature

## Slide 14: 2. «Distillation is an inefficient process which uses a lot of energy»
This is a myth!
By itself, distillation is an efficient process.
It’s the heat integration that may be inefficient.
Yes, it can use a lot of energy (heat), but it provides the same energy as cooling at a lower temperature

## Slide 15: Thermodynamic (exergy) efficiency for conventional distillation
Thermodynamic Efficiency =
Ideal work for the separation/Actual work:
Approximate for

## Slide 16: Thermodynamic efficiency of binary close-boiling mixtures (
Comment: Above 50% for z from 0.2 to 0.8
Peak efficiency is -ln0.5 = 0.693 at z=0.5
α = relative volatility
z = feed composition (mole fraction light component)

## Slide 17: Thermodynamic efficiency of binary distillation
High efficiency at small z for easy separations with large α
Reason: Must evaporate light component to get it over top
z = fraction light component in feed
α = relative volatility

## Slide 18
Note: Non-ideality does not necessarily imply lower thermodynamic efficiency
King (1971)

## Slide 19: Why is it not perfect – where are the losses?
Irreversible mixing loss at every stage.
Largest losses in the middle of each section – where the bulk separation takes place
Small losses at the high-purity column ends

## Slide 20: 3. Distillation is unbeatable for high-purity separations
Operation: Energy usage essentially independent of product purity
  Kings’s formula: +
Capital: No. of stages increases only with log(impurity)
Fenske: Nmin = ln S / ln α
Actual: N 2.5 Nmin
Separation factor:
α = relative volatility

## Slide 21: 4. Integrated / complex schemes can save energy and capital

## Slide 22: Divided wall columns: starting to catch on
1940’s: first patent
1960’s: Thermodynamic analysis (Petlyuk)
1984: First implementation (BASF)
2005: BASF has about 50 divided wall columns
2019: Several hundreds
  also in Japan, South Africa, China ...

## Slide 23: Typical sequence: “Direct split”
A,B,C,D,E,F
A
F
B
C
D
E

## Slide 24: 3-product mixture
A+B+C
A+B
A
B
C
1. Direct split
A+B+C
A+B
A
B
C
B+C
A+B+C
A
B
C
B+C
3. Combined
(with prefractionator)
2. Indirect split

## Slide 25: Towards the Petlyuk column
A+B
A
B
C
B+C
A+B+C
A
A+B
B
C
B+C
liquid split
vapor split
5. Petlyuk
30-40% less energy
A+B+C
A+B
A
B
C
B+C
4. Prefractionator
+ sidestream column
A+B+C
3.

## Slide 26: 4-product mixture
A,B,C,D
A
B
C
D
A – methanol
B – ethanol
C – propanol
D – butanol
Direct optimal extension of Petlyuk ideas requires two divided walls.
Will look for something simpler
Conventional sequence with 3 columns

## Slide 27
Montz
GC – Chemicals Research and Engineering Dividing Wall Columns
Off-center Position of the Dividing Wall
≈
≈

## Slide 28: 4-product mixture: Kaibel column
A+B
A
B
D
C+D
ABCD
C
D
ABCD
A
B (pure!)
C (pure!)
Alternative 3-column
sequence
Kaibel: 1 column!! More then 50% capital savings
Also saves energy (but maybe not exergy)
A – methanol
B – ethanol
C – propanol
D – butanol

## Slide 29: Control of Kaibel column
Prefractionator:
  Close 1 “stabilizing” temperature loop
Main column
  Close 3 “stabilizing” temperature loops
Close a “stabilizing” temperature
(profile) loop for each split
D

## Slide 30
H=6m
D=5cm
F
S1
S2
B
D

## Slide 31: 5. For autonomous and energy-efficient batch distillation try multivessel distillation with closed operation

## Slide 32
Closed Operation of Multivessel Batch Distillation: Experimental Verification Bernd Wittgens and Sigurd Skogestad. AIChE Journal. 46 (6), pages 1209-1217 (June 2000)
Closed operation of batch distillation
Multivessel
Two-vessel

## Slide 34: 6. Azeotropes can be broken by adding extractive component and especially by making use of liquid-liquid splits

## Slide 35
Acetic acid
Water
N-butyl-actate
60% acetic acid
cooling
Solvent recovery. Explosives plant, Norway

## Slide 36
oppstart i starten av desember 2018 (startet med 100% syre i kolonna)
Temp plate 1
Temp plate 10 (Sp=95,5)
Temp plate 15
Temp plate 20
Damppådrag
Temp plate 5
Flow BuAC
Nivå dekanter
Temp plate 35 (Sp = 117)
Temp plate 45
Temp plate 40

## Slide 37
02 feb. 2019. Siste kjøring før rep av kolonne
Temp plate 1
Temp plate 10 (Sp=95,5)
Temp plate 15
Temp plate 20
Damppådrag
Temp plate 5
Flow BuAC
Nivå dekanter
Temp plate 35 (Sp = 117)
Temp plate 45
Temp plate 40

## Slide 38
20 feb. 2019. Første oppstart (after Koch-Glitch repair)
Temp plate 1
Temp plate 10 (Sp=95,5)
Temp plate 15
Temp plate 20
Damppådrag
Temp plate 5
Flow BuAC
Nivå dekanter
Temp plate 35 (Sp = 117)
Temp plate 45
Temp plate 40
P = 100 min
Controller integral time for temperature loop = 10 minutes

## Slide 39: Slow oscillations were caused by too slow control
Tray 10 temperature controlled using butyl-acetate reflux: Integral time (taui) = 10 minutes.
TOO MUCH INTEGRAL ACTION!
Sigurd’s formula*: Increase Kc*taui by factor f = 0.1*(P/taui0)^2 = 0.1*(100/10)^2 = 10.
Problem solved by increasing integral time to 50 minutes.
*Sigurd Skogestad. ''Simple analytic rules for model reduction and PID controller tuning''
J. Process Control, vol. 13 (2003), 291-309

## Slide 40
Drift juni 2019, 8 timers periode
Temp plate 1
Temp plate 10 (Sp=95,5)
Temp plate 15
Temp plate 20
Damppådrag
Temp plate 5
Flow BuAC
Nivå dekanter/kolonne
Temp plate 35 (Sp = 117)
Temp plate 45
Temp plate 40
Temp AcOH feed kolonne
feed kolonne
Discharge kolonne
Temp dekanter

## Slide 41: 7. Better operation and control can improve quality and productivity
S. Skogestad, “The dos and don'ts of distillation columns control”,
Chemical Engineering Research and Design (Trans IChemE, Part A), 85 (A1), 13-23 (2007).

## Slide 42: Myth of slow control
Let us get rid of it!!!
Compare manual (“perfect operator”) and automatic control for typical column:
    40 stages,
    Binary mixture with 99% purity both ends,
    relative volatility = 1.5
  First “one-point” control: Control of top composition only
  Then “two-point” control: Control of both compositions

## Slide 43: Myth about slow control One-point control
“Perfect operator”: Steps L directly to
correct steady-state value
(from 2.70 to 2.74)
Disturbance
in V
Want xD constant
Can adjust reflux L

## Slide 44: Myth about slow control One-point control
“Perfect operator”: Steps L directly
Feedback control: Simple PI control
Which response is best?
Disturbance
in V
CC
xDS

## Slide 45: Myth about slow control One-point control

## Slide 46: Myth about slow control Two-point control
“Perfect operator”: Steps L and V directly
Feedback control: 2 PI controllers
Which response is best?
CC
xDS: step up
CC
xBS: constant
V
L

## Slide 47: Myth about slow control Two-point control
V
L

## Slide 48: Myth about slow control
Conclusion:
Experience operator: Fast control impossible
  “takes hours or days before the columns settles”
BUT, with feedback control the response can be fast!
  Feedback changes the dynamics (eigenvalues)
  Requires continuous “active” control
Most columns have a single slow mode (without control)
  Sufficient to close a single loop (typical on temperature) to change the dynamics for the entire column

## Slide 49: Conclusion
Distillation is important
Distillation is unbeatable (in some cases)
Distillation is fun
Distillation is complex yet simple
Distillation is part of the future