## Slide 1: Distillation modelling and control
Webinar, Malaysia, April 2021
Sigurd Skogestad, NTNU

## Slide 2: Sigurd Skogestad
1955: Born in Norway
1978: MS (Siv.ing.) in chemical engineering at NTNU
1979-1983: Worked at Norsk Hydro co. (distillation)
1987: PhD from Caltech (supervisor: Manfred Morari)
  Thesis: “Studies om robust control of distillation columns”
1987-present: Professor of chemical engineering at NTNU
  42 Phd students graduated (9 with distillation in title of thesis)
1999-2009: Head of Department
2015- : Director SUBPRO
200+ journal publications
Book: Multivariable Feedback Control (Wiley 1996; 2005)
Book: Chemical and energy process engineering (CRC Press, 2008)
  1989: Ted Peterson Best Paper Award by the CAST division of AIChE
  1990: George S. Axelby Outstanding Paper Award by the Control System Society of IEEE
  1992: O. Hugo Schuck Best Paper Award by the American Automatic Control Council
  2006: Best paper award in Computers and chemical engineering.
  2011: Process Automation Hall of Fame (US)
  2012: Fellow of American Institute of Chemical Engineers (AIChE)
  2014: Fellow of International Federation of Automatic Control (IFAC)
  2019: Best paper award at the ESCAPE 2019 Symposium (Eindhoven)
  2019: Computing in chemical engineering award from the American Institute of Chemical Engineers

## Slide 3
Arctic circle
Geiranger fjord
Trondheim
Midnight sun
NTNU

## Slide 4
Abstract. Distillation is the most common separation process in the chemical industry. The aim of the webinar is to educate academia and industry of some of the complexities of a very important problem, which is on how to operate conventional single columns in the best way.
Some highlights of the talk:
1. Distillation as a separation process (In spite of claims to the contrary
it's an efficient process; it's the heat integration that may be inefficient)
2. Modelling (in principle it's simple using an equilibrium stage model, but the thermodynamics (VLE) may be
difficult to model and there are many coupled equations)
3. Dynamics (there is one dominant slow mode related to the holdup of light
and heavy key components in the column)
4. Optimal operation (minimize energy usage and maximize recovery subject to
satisfying purity specifications)
5. Control, single-loop and MPC
(stabilize the column and keep the operation close to optimal, preferably
using a simple control structure)
The focus will be on the two last issues, but it should be noted that an accurate
steady-state model is often needed to address issues of optimal operation and
control.

## Slide 5: Details
1. Distillation as a separation process
- In spite of many claims it's an efficient separation process from a thermodynamic point of view.
- It uses heat. Qin at reboiler, About same Qout in top
- It's the heat integration that may be inefficient
i- It's unbeatable for high-purity separatioons
2. Modellering
- Relatively simple. Stage model OK
- Thermo (VLE) is main problem
- Shortcut models
3. Dynamics
- One slow mode
4. Optimal operationa:
1. satisfy specs,
2. eaximize valueable product (recovery)
3. save energy
Some simple rules:
- Always control expensive product spec.
- Sometimes overpurify other end (trade-off between recovery and energy; need model, steady-state OK)
- In many cases the whole process needsw to be modelled (recycle). The column may not have clear specs!
How about just saving energy?
Avoid overpurification of valueable product. Just wastes energy AND gives less product!
Note: If enough stages, then overpurification does not cost much..
5. Control
- Interesting process! Many options,
- 5x5, TPM location
- LV
- Good candidate for MPC.
- But single-loop also OK

## Slide 6: Outline
1. Introduction / Distillation as a separation process
2. Modelling
3. Dynamics
4. Optimal operation
5. Control

## Slide 7: 1. Basis: Difference in boiling points (volatility)
Liquid
x
y
Gas (vapor)
Relative volatility:
Example. iso-pentane (L) – pentane (H).
Boiling points: 28 oC(L) and 36.2 oC(H)
L – light component
H – heavy component
I.J. Halvorsen and S. Skogestad, ``Distillation Theory'', In: Encyclopedia of Separation Science. Ian D. Wilson, Academic Press, 2000, pp. 1117-1134.

## Slide 8
1545
1593
Batch distillation with no reflux (-> N=1)
2020

## Slide 9
Continuous distillation with reflux (L)
V
L
stage 1

## Slide 10: When use distillation?
Liquid mixtures with difference in boiling point
Unbeatable for high-purity separations
    Essentially same energy usage independent of purity!
    Number of stages increases only as log of impurity!
      Fenske: Nmin = ln S / ln α
Well suited for scale-up
        Columns with diameters over 15 m
Examples of unlikely uses of distillation:
        High-purity silicon for computers (via SiCl3 distillation)
        Water – heavy-water separation (boiling point difference only 1.4oC)
Close-boiling mixture (α close to 1)
Need a lot of energy (heat)
and many stages

## Slide 11: «Distillation is an inefficient process»
This is a myth!
By itself, distillation is an efficient process
  Typically, thermodynamic efficiency >50%
It’s the heat integration that may be inefficient.
  Yes, it can use a lot of energy (Qr=heat), but it provides ~ the same energy as cooling (Qc) at a lower temperature

## Slide 12: Thermodynamic efficiency of distillation
Separation into pure components
Plot is for liquid feed, binary mixture
z = fraction light component in feed
α = relative volatility
Plot from I.J. Halvorsen.
Ref: S. Skogestad, Chemical and Energy process engineering, CRC Press, 2009, pp. 224
Ref: C.J. King, Separation processes, McGraw-Hill, 1971, 1980

## Slide 13: 2. Simple to model. Equilibrium stage concept
VLE: “Relative volatility model”
Usually most important!
Activity coefficient (e.g. UNIFAC)
Or: Equation of state (e.g. SRK, PR)
Mi
VLE = Vapor-Liquid Equlibrium
Francis weir formula:

## Slide 14: 2. Simple to model. Equilibrium stage concept
VLE: “Relative volatility model”
Usually most important!
Activity coefficient (e.g. UNIFAC)
Or: Equation of state (e.g. SRK, PR)
Mi
Modelling. Adjusting parameters
VLE. May need experimental data
Stages (N)
  Use steady-state model
  Match steady-state compositions and temperature profiles
    Adjust N to get theoretical stages in each section (also for packed column)
    Tray column: Can use Murphee efficiency. I use bypass on V and/or L
Holdup Mi. Match with dynamic data for compositions
  Typical column holdup, ML = ΣMi
  Tray column: 10% of column volume
  Packed column: 5% of column volume
Liquid dynamics: Make step in L and see how long it takes for change to reach bottom
  Francis weir formula: θL ≈ (2/3) ML / L

## Slide 15: 3. Dynamics
Example . Propylene-propane (C3-splitter, column D)
N = 110 theoretical stages
ΔTB=5.6K
 = 1.12 (relative volatility at 15 bar)
Purities: 99.5% propylene (top) and 90% propane (bottom)
Assume constant molar flows
L/D = 19, D/F = 0.614

## Slide 16: External flow change Propylene-propane. Simulated composition response. Increase reflux 0.4% (L = +0.05,  D=-0.05) with V constant:
XD
XB
2000 min
Xfeed stage
6 min
L
V

## Slide 17
Increase in L +0.05
feed stage

## Slide 18: External flow change. Propylene-propane. Simulated composition response with detailed model. Increase boilup (V: +0.05, D: +0.05) with L constant
Opposite of increase in L!
Xfeed stage
XB
XD
V
L

## Slide 19
What happens if we increase both L and V at the same time?
Then D and B are constant
Internal flow change
V
L

## Slide 20: Internal flow change. Propylene-propane. Simulated composition response with detailed model. Increase both L and V by same amount ( V =  L = +0.05)
Very small effect
feed stage

## Slide 21
Increase both L and V by same amount (V = L = +0.05) (D=B=0)
Very small effect! Note axis: Have “blown up” to see details
0.9950
0.9951
XD
XB
Xfeed stage
0.100
0.0998
0.0992
Both products get purer.
Response for xB a bit “strange”
(with very large overshoot)
because it takes some time for
L to reach the bottom

## Slide 22: External and Internal Flows
Large effect on composition (large “gain”)
One products get purer – the other less pure
Small effect on composition (small “gain”)
Both products get purer or both less pure
Steady–state composition profiles (column A)
COMP
COMP
0
0
stage
External flows
Internal flows (10X)
 L =  B = -  D = (-0.1, -0.01, 0, 0.01, 0.1)
 V= L = (1, 0, -1).  B= D=0
Column A: N=40, α=1.5, xD & xB: 99%, L/D= 5.4
«ILL-CONDITIONED INTERACTIVE PROCESS». Problem for control?

## Slide 23: Liquid flow dynamics are essential for control
Liquid flow dynamics ”break” the initial two-way interaction between top and bottom.
  Want to close one loop (temperature or composition) with closed-loop time constant faster than the liquid flow dynamics
S. Skogestad, “Dynamics and control of distillation columns - A tutorial introduction”, Trans IChemE, Part A (Chemical Engineering Research and Design), 75, Sept. 1997, 539-562

## Slide 24: Nonlinearity
Use logarithmic compositions
S. Skogestad, ``Dynamics and Control of Distillation Columns - A Critical Survey‘’, IFAC-symposium DYCORD+'92, Maryland, Apr. 27-29, 1992.
Reprinted in Modeling, Identification and Control, Vol. 18, 177-217, 1997.

## Slide 25
S. Skogestad, “Dynamics and control of distillation columns - A tutorial introduction”, Trans IChemE, Part A (Chemical Engineering Research and Design), 75, Sept. 1997, 539-562
With logarithmic compositions

## Slide 26: Conclusion dynamics
Dominant first order response – often close to integrating from a control point of view
Liquid flow dynamics decouples the top and bottom on a short time scale, and make control easier
Logarithmic transformations linearize the response

## Slide 27: 4. Optimal operation distillation column
Dynamic degrees of freedom (with given F): 5
Steady state (control levels and pressure): 2 degrees of freedom (e.g. L,V)
Optimal operation: Minimize cost J subject to satisfying constraints
Cost to be minimized (economics)
  J = - P where P= pD D + pB B – pF F – pV V
Constraints
  xD, impurity < max
  xB, impurity < max
  Column capacity (flooding): V < Vmax, etc.
value products
cost energy (heating+ cooling)
cost feed

## Slide 28: Expected active constraints distillation
Valueable product: Purity spec. always active
  Avoid product “give-away”
  (“Sell water as methanol”)
  Saves energy
Control implications:
  1. Control valueable product at spec.
    Control D at 0.5% water
  2. Overpurify other end to reduce loss
    Control B with methanol < 2%
    Overpurifying may not cost much energy (V) if enough stages
    If “few” stages: May be optimal to operate at max energy (V) to minimize loss of valuable product
valuable
product
methanol
+ max. 0.5%
water
cheap product
(byproduct)
water
+ max. 2%
methanol
methanol
+ water

## Slide 29: 5. Control
S. Skogestad, “The dos and don'ts of distillation columns control”,
Chemical Engineering Research and Design (Trans IChemE, Part A), 85 (A1), 13-23 (2007).

## Slide 30: Two objectives for control
Have 5 dynamic degrees of freedom
Stabilize (avoid drift)
  Levels (MD, MB, pressure)
  Temperature profile («level of heavy component»)
  NOTE: Temperature setpoint can be used as degree of freedom for composition control
Optimize operations
  Normally control product compositions (xD, xB)

## Slide 31: Issues distillation control
The “configuration” problem (pairings for level and pressure)
  Which are the two remaining degrees of freedom?
    e.g. LV-, DV-, DB- and L/D V/B-configurations
The temperature control problem
  Which temperature (if any) should be controlled?
Composition control problem
  Control two, one or no compositions?
TC
Ts
TC
L
V

## Slide 32: Stabilize temperature profile (“level of heavy component”)
LIGHT
HEAVY
F
D
B
TC
Temperature sensor should be located at «sensitive» stage (with high gain)
Typically in middle of top or bottom section

## Slide 33: Which stage? Binary column
slope closely correlated with steady state gain
STAGE
TEMPERATURE PROFILE

## Slide 34: Multicomponent column
Slope NOT correlated with steady-state gain
TEMPERATURE PROFILE
Conclusion: Temperature slope alone OK only for binary columns

## Slide 35: Which configuration? Level control top: Use L or D?
Seems almost impossible to control level with D (small range because need D>0)
LC
D (small)
L (large)
VT (large)
FORTUNATELY:
Tight level control is NOT important
Fast inner temperature loop gives indirect level control!
Conclusion: Recommend using D (and B) for level control!!
Gives LV-configuration
However, for large L/D (>5):
Would like to use D because L is most effective for composition control

## Slide 36: Conclusion configurations
Normally use LV-configuration
because it is
  simplest
  level tunings do not matter for column behavior
  can get smooth variations in product rates D and B
Usually add temperature loop using L or V
  Especially for difficult separations with large L and V
  Gives indirect level control
  Breaks interactions
LV-configuration

## Slide 37: LV-configuration with temperature loop and dual composition control
CC
LV
TC
Ts
xB
CC
xD
Inner fast T-loop should be in the «important» end
  The figure above is when bottom composition is most important
Temperature sensor should be located at «sensitive» stage.
FAST

## Slide 38: Myth of slow control
Let us get rid of it!!!
Compare manual (“perfect operator”) and automatic control for column A:
    40 stages,
    Binary mixture with 99% purity both ends,
    relative volatility = 1.5
    L/D = 5.4
  First “one-point” control: Control of top composition only
  Then “two-point” control: Control of both compositions
S. Skogestad, “Dynamics and control of distillation columns - A tutorial introduction”, Trans IChemE, Part A (Chemical Engineering Research and Design), 75, Sept. 1997, 539-562

## Slide 39: Myth about slow control One-point control
“Perfect operator”: Steps L directly to
correct steady-state value
(from 2.70 to 2.74)
Disturbance
in V
Want xD constant
Can adjust reflux L

## Slide 40: Myth about slow control One-point control
“Perfect operator”: Steps L directly
Feedback control: Simple PI control
Which response is best?
Disturbance
in V
CC
xDS

## Slide 41: Myth about slow control One-point control

## Slide 42: Myth about slow control Two-point control
“Perfect operator”: Steps L and V directly
Feedback control: 2 PI controllers
Which response is best?
CC
xDS: step up
CC
xBS: constant
V
L

## Slide 43: Myth about slow control Two-point control
V
L

## Slide 44: Myth about slow control
Conclusion:
Experience operator: Fast control impossible
  “takes hours or days before the columns settles”
BUT, with feedback control the response can be fast!
  Feedback changes the dynamics (eigenvalues)
  Requires continuous “active” control
Most columns have a single slow mode (without control)
  Sufficient to close a single loop (typical on temperature) to change the dynamics for the entire column

## Slide 45: Advanced control
May also add feedforward control from F (ratio V/F in this case)
Constraint on pressure drop, DP
Top product valueable, xD
Overpurify bottom
xBmin: Constraint
xB*:Optimal xB (overpurify)
TC
T
DPmax

## Slide 46
Case with valuable bottom product, xB.
Split range control (SRC): 1. Normally control xB with boilup V
…. But boilup V may reach constraint
2. First let reflux L take over
3. Then cut back on feedrate F if top reaches constraint
"Systematic Design of Active Constraint Switching Using Classical Advanced Control Structures". A. Reyes-Lua and S. Skogestad, Ind. Eng. Chem. Res. 2020, 59 (6), 2229-2241.
Advanced control….

## Slide 47: Conclusion distillation control
Not as difficult as often claimed
LV-configurations recommended for most columns
Use log transformations to reduce nonlinearity
Use composition estimators based on temperature
Usually: Close temperature loop (P-control OK)
May use MPC if strong interactions between loops
CC
LV
Two-point
LV-configuration
with inner T-loop
TC
Ts
xB
CC
xD
S. Skogestad, “The dos and don'ts of distillation columns control”,
Chemical Engineering Research and Design (Trans IChemE, Part A), 85 (A1), 13-23 (2007).

## Slide 48: Conclusion
Distillation as a separation process
  In spite of claims to the contrary it's an efficient process
    - it's the heat integration that may be inefficient
  Unbeatable for high-purity separations
2. Modelling
  In principle it's simple
  Normally use equilibrium stage model
  The thermodynamics (VLE) are the most important
3. Dynamics
  There is one dominant slow (drifting) mode
  related to the holdup of light and heavy key components inside the column
4. Optimal operation
  Minimize energy usage (V) and maximize recovery of valuable component (J = pF F – pD D – pB B + pV V)
  subject to satisfying purity specifications
  Always active constraint: Purity of valueable product («avoid give-away»)
5. Control
  Fist: stabilize the column (levels, pressure and one temperature)
    The temperature loop will speed up the slow mode, break interactions and provide indirect level control
  Next: Control active constraints and keep operation close to optimal
  May use MPC, but can usually do OK with advanced single-loop control
https://folk.ntnu.no/skoge/distillation/