## Slide 1: Ratio and bidirectional control applied to distillation columns
Brage Bang
Sigurd Skogestad
Department of Chemical Engineering
Norwegian University of Science and Technology (NTNU)
Trondheim
17 June 2025
DYCOPS
Bratislava, Slovakia

## Slide 2: “The goal of my research is to develop simple yet rigorous methods to solve problems of engineering significance”

## Slide 3: This talk
Simple data-based architectures applied to distillation control
PID control (feedback)
Ratio control
Bidirectional control with selectors

## Slide 4: Ratio control
Feedforward control without a model y=f(u,d)
Just process insight
Example: Food recipe
  1 part sugar
  3 parts milk
  3 parts coffee
  MIX

## Slide 5: Usually: Combine ratio (feedforward) with feedback
  Example cake baking: Use recipe (ratio control = feedforward), but a good cook adjusts the ratio to get desired result (feedback)

## Slide 6: Ratio control combined with feedback
The correct ratio setpoint is found by feedback control (VC) based on keeping the measured controlled variable y at its desired setpoint ys..
  So also here no model is needed (just data)
F1
F2
Mixing

## Slide 7: Distillation
At home doing moonshine
distillation (1979)

## Slide 8
Distillate product:
0.999 methanol
0.001 water
Bottoms product:
0.001 methanol
0.999 water
Feed:
0.50 methanol
0.50 water
Increase feedrate
by 10%
6 indpependent flows (valves):
Feed F (set FS, disturbance)
Distillate D (top level control)
Bottom product B (bottom level control)
Cooling VT (pressure control)
Reflux L (top composition control)
Boilup V (bottom composition control)
FS

## Slide 9: B1: L and V constant
Increase feedrate
by 10%
FS
Aspen

## Slide 10: B2: L/F and V constant
Increase feedrate
by 10%
FS

## Slide 11: B4: L/F and V/F constant
Oooops…. Drifting a little (even in simulation)….
…. Becuse feedforward
FS
Increase feedrate
by 10%

## Slide 12: B3: L/F and T constant
Ratio with Cascade
TC
FS

## Slide 13: B3: L/F and T constant
Increase feedrate
by 10%
The best!
… but still one problem… V must not saturate!
V
T

## Slide 14: Summary

## Slide 15: When should we use ratio control?
Answer: When the scaling property holds such thay fixing the ratio of all extensive variables (e.g., F2/F1) gives constant intensive variables (y) at steady state.
Similar to in thermodynamics, the scaling property holds exactly for equilibrium systems:
  Mixing
  Equilibrium reactors
  Distillation
General: If we have n steady-state independent extensive variables (flows), then we must fix n-1 ratios.
Distillation: n=3 (with constant levels and pressure) Fix 2 ratios

## Slide 16: Mathematically: Theory of ratio control
SCALING PROPERTY (steady state):
Scaling all independent extensive variables by X the same factor,
with all independent intensive variables x constant,
scales all the dependent extensive extensive variables Y by the same factor
And keeps all intensive variables y constant

## Slide 17: Conclusion ratio control
It’s a great idea!
  Very simple to implement
  Gives nonlinear feedforward action
Requires no model, just insight
  Theoretical basis: Scaling principle
For distillation: Must keep 2 ratios constant
  Or 1 ratio and 1 temperature/composition
  Don’t use ratio control for distillation if one flowrate saturates
  Could use L/D rather than L/F (even when F is the disturbance)

## Slide 18: Bidirectional control
What should we do if B, D, L, VT or V saturates (at max) so that we lose control?
One solution: «Override» to reduce throughput (feedrate F)
F
LC
SP
Fs
B
LC1
MIN
SPL
LC2
MIN
SPH
Fs
Bs
F
B

## Slide 19: Bidirectional control of gas-liquid separator

## Slide 20: Bidirectional control of distillation
Override if composition
control is lost because
V (heat input) saturates
V/F with cascade in bottom
Top composition most important
4 flows may saturate at max:
B
D
VT (cooling)
V (heating)
L (reflux) never saturates
V
VT
L

## Slide 21: Dynamic simulation with Aspen

## Slide 22
Dynamic simulation

## Slide 24: CONCLUSION «Data-based» control using Advanced regulatory control
Simple control elements put together in an archirecture
No overall process model
Data (measurements) is the most important
Sigurd Skogestad, ”Advanced control using decomposition and simple elements‘’. Annual Reviews in Control, vol. 56 (2023)

## Slide 25
Optimal centralized
Solution (EMPC)
Sigurd (me)
Academic process control community fish pond
Simple solutions that
work (ARC = PID++)
Please join me, I feel a little alone
Nitin

## Slide 27
Backup slides

## Slide 28: QUIZ What are the three most important inventions of process control?
Hint 1: According to Sigurd Skogestad
Hint 2: All were in use around 1940
SOLUTION
PID controller, in particular, I-action
Cascade control
Ratio control
None of these are easily implemented using MPC

## Slide 29: Cases where ratio control should not be used:
Heat exchangers (because the area is fixed during operation)
  This means, for example, that we should not fix the ratio between hot and cold flow.
  For the scaling property to hold for a heat exchanger, we would need to increase the heat transfer area A proportionally to the flow rates. This is reasonable during design but not during operation.
Non-equilibrium reactors (because the volume is fixed)
  Extent of reaction depends on kinetics and reactor volume
Compressors with varying thermodynamic efficiency
  This includes most real compressors
Mixing processes where one feed stream is fixed
Distillation with a fixed stream (e.g. heat input)

## Slide 32
Trondheim
Arctic circle
Geiranger fjord
Trondheim
Midnight or midday?

## Slide 33: About Sigurd Skogestad
•1955: Born in Flekkefjord, Norway
•1974-1978: MS (Siv.ing.) studies in chemical engineering at NTNU
• 1979: Military service (FFI)
•1980-1983: Worked at Norsk Hydro F-senter (process simulation)
•1983-1987: PhD student at Caltech (supervisor: Manfred Morari)
•1987-present: Professor of chemical engineering at NTNU
• 1994-95: Visiting Professor UC Berkeley
• 2001-02: Visiting Professor UC Santa Barbara
•1999-2009: Head of ChE Department, NTNU
•2015-..: Director SUBPRO (Subsea research center at NTNU)
Non-professional interests:
mountain skiing (cross country)
orienteering (running around with a map)
grouse hunting
1973

## Slide 34: «Advanced» control
Mainly used in the «supervisory» control layer
Two main options
  Standard «Advanced regulatory control» (ARC) elements
    This option is preferred if it gives acceptable performance
  Model predictive control (MPC)
    Requires a lot more effort to implement and maintain
  What about machine learning (AI)?
    No, it requires way too much data - would take years to learn
PROCESS
setpoint
setpoint

## Slide 36
TPM = throughput manipulator
Example: Inventory control

## Slide 37: Inventory control for units in series
Follows radiation rule
Radiating rule:
Inventory control should be ‘‘radiating’’ around a given flow (TPM).
Need to reconfigure inventory loops if TPM moves

## Slide 38: Generalization of bidirectional inventory control
Reconfigures TPM automatically with optimal buffer management!!
F.G. Shinskey, «Controlling multivariable processes», ISA, 1981, Ch.3
Cristina Zotica, Krister Forsman, Sigurd Skogestad ,»Bidirectional inventory control with optimal use of
intermediate storage», Computers and chemical engineering, 2022
,
Maximize
throughput:
Fs=∞

## Slide 39: When use MPC?
When conventional APC performs poorly or becomes complex
Cases with many changing constraints (where we cannot assign one input to each constraint)
Interactive process
Know future disturbances and setpoint changes (predictive capability)

## Slide 40: «Transformed inputs» v
Combining feedforward with feedback in an extremely simple way
Most effective for static feedforward
  Dynamic generalzation (= «feedback linearization») usually unrealistic because of many derivatives
Static model: y =f(u,d)
Select transformed inputs (= controller outputs): v = f(u,d)
Invert to get physical inputs: u = f-1(v,d)
Then response from v to y is: y= I v (linear, decoupled, perfect disturbance rejection)
FeedbackController
Calculation block (static FF)
Process
ys
y
V
d
u
y
Looks like magic but ut works
S. Skogestad, C. Zotica, N. Alsop., «Transformed inputs for linearization, decoupling and feedforward control», J. Proc. Control, 2023

## Slide 41: Example decoupling: Mixing of hot (u1) and cold (u2) water
Want to control
  y1 = Temperature T
  y2 = total flow F
Inputs, u=flowrates
May use two SISO PI-controllers
  TC
  FC
Insight: Get decoupled response with transformed inputs
  TC sets flow ratio, v1 = u1/u2
  FC sets flow sum, v2 = u1 + u2
Decoupler: Need «static calculation block» to solve for inputs
u1 = v1 v2 / (1+ v1)
u2 = v2 / (1 + v1)
T
F
u1
u2
v2=sum
v1=ratio

## Slide 42
TRANSFORMED INPUTS v=f(u,d): GENERAL APPROACH FOR COMBINED FEEDBACK,
FEEDFORWARD, DECOUPLING AND LINEARIZATION
Example: Mixing of hot and cold water
Controller
Calculation block (static)
Process
ys
y
V
d
u
y
Generalized ratio
Decoupler with feedforward:
It’s almost magic!