## Slide 1: Nonlinear input transformations for disturbance rejection, decoupling and linearization
Sigurd Skogestad
Cristina Zotica
Department of Chemical Engineering
Norwegian University of Science and Technology (NTNU)
Trondheim
Virtual seminar UFRJ Brazil. 05 October 2020
Thanks to Nicholas Alsop and Christian Holden

## Slide 2: Abstract
Title: “Nonlinear input transformations for disturbance rejection, decoupling and linearization”.
Abstract. The goal of my research is to develop simple yet rigorous methods to solve problems of engineering significance. The topic of input transformations is something I have been working on for the last year or so, and I think it has a lot of promise. The starting point is that I observed that industry frequently used static model-based calculation blocks for various purposes, such as counteracting nonlinearity, disturbances and coupling. Industry also frequently uses cascade control.
However, there is little theory for when to use these solutions, and we have found that the use of input transformations forms a good basis. The starting point is a nonlinear process model, which is transformed to a simpler model through the use of an input transformation. It is really very simple. Consider a nonlinear model dy/dt=f(y,u,d) and introduce v=f(y,u,d) as the transformed input to get a nonlinear transformed system dy/dt=v which is linear, decoupled and independent of disturbances. This transformation is a special case of feedback linearization, but we have extended the idea by adding a tuning parameter, by allowing for static process models and by making use of cascade control in a systematic way. The method has been tested on many process control examples.

## Slide 3
Trondheim
Arctic circle

## Slide 4: About Sigurd Skogestad
•1955: Born in Norway
•1978: MS (Siv.ing.) in chemical engineering at NTNU
•1979-1983: Worked at Norsk Hydro co. (process simulation)
•1987: PhD from Caltech (supervisor: Manfred Morari)
•1987-present: Professor of chemical engineering at NTNU
• 1994-95: Visiting Professor UC Berkeley
• 2001-02: Visiting Professor UC Santa Barbara
•1999-2009: Head of ChE Department, NTNU
•2015-..: Director SUBPRO (Subsea research center at NTNU)
Non-professional interests:
mountain skiing (cross country)
orienteering (running around with a map)
grouse hunting

## Slide 5: “The goal of my research is to develop simple yet rigorous methods to solve problems of engineering significance”

## Slide 6
Optimal centralized
Solution (EMPC)
Sigurd
Academic process control community fish pond
Simple solution
that work (PID++)

## Slide 7: Introduction
I have observed that industry frequently used model-based calculations blocks
… and they use a lot of cascade control
But no theory for when to use
Idea: Use nonlinear model equations to derive control strategy
“Control structures with embedded knowledge through input transformations”
Primary use:
  Nonlinear feedforward
  Decoupling
  Insight into when to use cascade control (extra measurements)

## Slide 8: The main idea: Trivial but almost magic
Nonlinear dynamic system (process)
Introduce transformed inputs
New transformed system is linear, first-order, decoupled if A is diagonal and independent of disturbances!
Static input calculation (inverse input transformation): u is solution to:
v can be calculated by conventional linear controller C (PI)
  For perfect disturbance rejection (y constant) we can keep v constant.
Assumptions
  Obvious: Know model f(y,u,d) and measure all disturbances (d)
  no. states (y) = no. inputs (u). (restrictive)
  The solution to the static inverse problem exists and satisfies certain properties.

## Slide 9: ~ Feedback linearization (Isidori)
Nonlinear dynamic system (process)
Introduce transformed inputs
New transformed system is linear, integrating, decoupled and independent of disturbances:
A more desciptive name would be «nonlinear static feedforward control and linearization – with a little feedback»
    The system is mainly linearized by static inversion of the nonlinear model f (feedforward)
    The most important property of «feedback linearization» is maybe that it eliminates disturbances (again by feedforward)
    Yes, there is some linearizing feedback from y, but not necessary a lot (see Extension 2).

## Slide 10: Extension 1: More general function f(y,u,d)
Textbook Feedback linearization assumes linearity (affine) input:
  Original system:
  Transformed input:
Then inverse transformation is then explicit for the scalar case
We allow for a more general function
  Original system:
  Transformed input:
The inverse transformation may need to be solved numerically

## Slide 11: Why transform to integrating?
Feedback linearization: Transformed linear system is integrating:
But imagine that we want fast control of a process which is fast.
  First turn system into «slow» integrator by input transformation (positive feedback)
  Then make fast again by using negative feedback in controller C
  Does not make much sense!
Also: Integrating systems are not easy to control

## Slide 12: Extension 2: Introduce tuning parameter A for dynamics
Original system:
Transformed input:
Get transformed system:
  First-order
  A can be used to get desired dynamics
  Decoupled if A is diagonal
  Special case A=0: Integrating («feeedback linearization»)
  One idea: Select at nominal operating point
    Then nominally the transformed system has the same dynamics as the original system
    and there is nominally no feedback from y to inverse v-block (input calculation)

## Slide 13: Extension 2’: Related transformation with steady-state gain I*
Original system:
Transformed input:
Get transformed system:
Closely related transformed input:
Get transformed system: (with tuning parameter (matrix) = -A-1)
  This system has linear setpoint response (from vA0=ys to y) with time constant τ0 and steady-state gain I, and perfect disturbance rejection.
  May then in theory avoid the outer feedback controller C (e.g., PI)
  BUT: The outer controller C is needed to correct for model errors and unknown disturbances
*Zotica, Alsop and Skogestad. 2020 IFAC World Congress

## Slide 14: Extension 3: Static systems
Static process:
Common in process control
Solve f=0 with respect to x to get the nonlinear static process model:
Introduce transformed input:
New transformed linear static system, independent of disturbances:
Note: v0 is independent of y, so the inverse input block is purely feedforward
So: This is simply nonlinear static feedforward control
Assumption: The solution to the static inverse problem, exists and is unique*.
  Warning: May encounter problems with the inversion if you apply a static transformation to a dynamic system and try to speed up the response with the outer controller. Extension 5: Solving the equations by feedback (I-control) may be safer.
*Don’t really need to know r(u,d). u is solution to equations: f(x,u,d)=0 with Cx=v0

## Slide 15: Examples («magic»)
Example 1. Heater with y=T and u=q or u=Q
Example 2: Shower (mixing) with one static and one dynamic equation
Example 3: Heat exchanger (static applied to dynamic system)

## Slide 16: Example 1. Electric heater, y=T
Energy balance:
Transformed input:
Transformed system:
Choice of tuning parameter:
= -1/nominal residence time
    Then at nominal operating point,
Inverse transformation to find u (with given vA).
With u=q (d=Q): % oops… if T0 increases above T
With u=Q (d=q):
Note: To keep T constant in spite of disturbances, keep vA constant

## Slide 17: Example 1. Simulation results
u=Q (heat rate)
1. d1=T0: 10->25 at t = 100 s
3. d2=q: 100 -> 50 % at t = 2000 s
4. Ts: 50->52 at t = 3000 s
y=T
u=Q
vA

## Slide 18: Example 1. Simulation results
u=Q (heat rate)
1. d1=T0: 10->25 at t = 100 s
3. d2=q: 100 -> 50 % at t = 2000 s
4. Ts: 50->52 at t = 3000 s
--- Dashed lines: Without measurement of d1=T0 (fixed at 10C in model). Need to use feedback (C) to change vA
y=T
u=Q
vA

## Slide 19: Example 2. Mix hot (1) and cold (2) water (shower), y=[q T]
Mass balance: (static equation for y1=q)
Energy balance: (dynamic equation for dy2/dt)
New transformed inputs: v0 and vA.
Inverse transformation (with u1=q1 and u2=q2):
Tuning parameter, A = -(q/V)* (nominal)

## Slide 20: Shower. Simulation responses with transformation only. -> Perfect disturbance rejection and decoupling
1. d1=T1: 20 ->22 °C at t = 50 s
2. d2=T2: 50 ->55 °C at t = 100 s
3. y2s=Ts: 35 ->36 °C at t = 150 s
4. y1s=qs: 10 ->11 kg/s at t = 200 s
y1
y2
u
d
1,2: v0 and vA constant
3: Step in vA
4: step in v0

## Slide 21: Example 3. Heat exchanger (static)
Energy balance,
v0
Use numerical inverse (to find u for given v0)
y
u

## Slide 22: Simulation applied to cell dynamic model
u
u
u

## Slide 23: But our dynamic transformation vA assumes nu=n
That is, we need as many inputs (nu) as differential equations (n)
One input: Can only handle first-order system
Can use feedback linearization and get a chain of integrators
  But not easy (Lie derivatives….)
  and not so good in practise (integrators….)

## Slide 24: Extension 4: Higher-order systems (n > nu)
Original system:
where w(u) represent other states («internal dynamics»)
Our solution:
Assume we can measure the variables (states) w
Introduce transformed inputs to get transformed system
But how to invert the transformation? How to obtain u from a given value of vA?
  1. If f and thus vA depends explicitly on u: Treat w as a measured disturbance and invert vA for u.
    «Potentially dangerous», for example, may have inverse response from u to y.
  2. If not, i.e., vA=f(y,w,d)-Ay.
    Use cascade control of w: Invert vA for w – and then control w using u (i.e., slave controller for w).
    Use chain of inverse transformations if model for w is known, dw/dt=f2(y,w,u,d)
More general (both cases): Cascade control of vA
    Extension 5: Solve the inverse transformation by feedback

## Slide 25: Inverse transformation using Cascade control of v
Use when actual system has additional (unknown) dynamics (w).
Slave controller: Tuned based on experimental response from u to calculated v (includes w-dynamics!)
Equivalent to static inverse transformation if slave controller is sufficiently fast
  Can be made arbitrary fast if response from u to v is static or first-order system with no effective delay
  Otherwise: Some «loss» dynamically (in terms of linearity and disturbance rejection)
Measured
variables

## Slide 26: Inverse transformation using Cascade control of v
Comment: May use cascade control of v also for cases without additional dynamics (w).
  Static function w(u,d) is uncertain (so cannot find u), but we measure w (e.g., flow controller)
  Inversion of input transformation is difficult (numerically or analytically)
    Extension 5: Use feedback control to invert the static equations
      Typically use pure I-action for the slave controller
  We want to «slow down» the inversion
    Example: Static transformation v0 = r(u,d) applied to dynamic system
Measured
variables

## Slide 27: Example 4. CSTR. ,
Component balance:
Energy balance:
Transformed input: vA
Extra measured variable (state):
Tuning parameter: (nominal)
Inverse transformation: Use cascade control

## Slide 28
Controller
C
(dynamic)
Slave vA-controller
(dynamic)
Process
(dynamic)
ys
y
u=Q
y=cA
Static input transformation
vA
d=CA0,q,T0
(setpoint)
vAs
w=T
y=cA
Measured
variables
Calculated
Two reasons to use slave controller
u=Q does not appear in vA
Avoid inverting expression for vA with respect to T
CA0,q
General cascade of v

## Slide 29
Controller
C
(dynamic)
Slave temperature controller
(dynamic)
Process
(dynamic)
ys
y
u=Q
y=cA
Inverse static input transformation
d=CA0,q,T0
vA
w=T
y=cA
Measured variables
Need to invert expression for vA with respect to T
Alternative cascade of w
Ts
CA0,q
=A
cA

## Slide 30: Example 4. Simulation results (alternative cascade of w)
y
u
w
v
1. d1= T0 : 77 ->87 °C at t = 10 s
2. d2= cA0 : 2 ->2.1 kmol/m3 at t = 40 s
3. ys=cAs: 0.67 ->0.8 kmol/m3 at t = 70 s

## Slide 31
Controller
C
(dynamic)
Process
(dynamic)
ys
y
u=Q
y=cA
Inverse static
vA input transformation
d=CA0,q,T0
vA
T
y=cA
Measured variables
Need to invert expression for vA with respect to T
Alternative: Chain of inverse transformations with no slave
CA0,q
=A
Can be used for series («chain») system if model for w is known
Also includes feedforward from T0’
  Feedforward control for T0 will be perfect, but not for CA0 and q (τ = -1/AT).
Inverse static vA0 input transformation
T0
Ts=
vA0
cA

## Slide 32: Example 5. Level control with flow controller
(level), (valve position),
Model (mass balance):
  where (valve equation):
  fv(z): nonlinear valve characteristic
Can use «standard method» with:
  Invert f to find u from given vA
  Complicated + Valve characteristic fv(z) uncertain + need measurement of DP
Much better if qout is measured: Introduce and use cascade control
  Tranformed input:
  Equivalent to standard solution with cascade control based on flow controller
flow in
flow out
y=V
u=z

## Slide 33
Controller
C
(dynamic)
Slave v- controller
(dynamic)
Process
(dynamic)
ys
y
u=z
y
Static input transformation
v = f(w,d)= qin-qout
d=qin
v = qin-qout
(setpoint)
vs
w=qout
Measured
variables
LC
y
ys
flow in
flow out
vs
FC
qout
u=z
master
slave
qin
v
Cascade control of v
Static input transformation

## Slide 34
Controller
C
(dynamic)
Slave w- controller
(dynamic)
Process
(dynamic)
ys
y
u=z
y
Inverse static input transformation
d=qin
qin
(setpoint)
v =
qin-qout
w=qout
Measured
variables
LC
y
ys
flow in
flow out
v=qin-qout
FC
w=qout
u=z
master
slave
qin
Alternative: Cascade control of w
ws
qout,s
Inverse static input transformation

## Slide 35: Discussion: Difficult systems for input transformations
Input transformation work best if we have a dominant dynamic equation involving the output of interest:
  M dy/dt = f(y,u,w,d) (where M is quite large)
But this does not always hold
Examples of «difficult» systems:
Example: Heat exchanger. y=T
  Partial differential eaquations (PDE). Use cell model withseries of interacting tanks.
  Can use static transformation. Works quite well, but will only be correct at steady state
Example: Distillation column, y = product composition
  Also modeled as series of interacting tanks (inside column)
  But have product tanks at the column ends

## Slide 36: Example 6: Distillation
y = distillate compostion
u= L (reflux)
L
y
V
yT
D
y
V
yT
Model reflux drum (component balance):
Note: does not depend explicity on u=L.
But yT depends on L. Introduce w=yT
Solution: Cascade control of vA or w=yT
yT is difficult to measure
But yT is closely related to temperature
This leads us towards the conventional solution with temperature cascade!

## Slide 37: Discussion of feedback linearization
«Feedback linearization» is powerful but rarely used in process control, because of perceived limitations and complexity.
Actully, the main idea is extremely simple!
And we have proposed extensions to overcome limitations:
Extension 1: More general function f(y,u,d)
Extension 2: Introduce tuning parameter A for dynamics
Extension 3: Static systems
Extension 4: Higher-order systems (n > nu) by adding measurements
Extension 5: Use feedback control to invert the static equations
These extensions are not really new (except maybe Extension 3?).
Extensions 1, 2 and 5: see Example 1 in “Output feedback performance recovery in the presence of uncertainties”. J. Lee , R. Mukherjee, H.K. Khalil, Systems & Control Letters, 90 (2016) 31–37.

## Slide 38: Discussion…
We have looked at many other examples
And in particular we have looked at the effect of uncertainty
  No big surprises
  It’s fairly robust!
  Mater theses by Callum Kingstree and Simen Bjorvand

## Slide 39: Conclusion
Need nonlinear process model for output (y) of interest
Original inputs: u
Transformed inputs: or
Resulting transformed system from v to y:
  Linear and first-order
  Perfect disturbance rejection
  Decoupled if A is diagonal
Can also hande static models y=r(u,d). Use
Very simple and potentially very powerful
Use cascade control of v (or w) if model is on the form
  Provides systematic approach for deriving cascade control solutions

## Slide 40: Extra

## Slide 41
Controller C
(dynamic)
Inverse input
tranformation
(Static)
Process
(dynamic)
ys
y
v
d
u
y
linear

## Slide 42
Controller
C
(dynamic)
Slave v-controller
(dynamic)
Process
(dynamic)
ys
y
u
y
Input transformation
(static)
d
v
(calculated )
(setpoint)
vs
w

## Slide 43: Special case (series system, f is independent of u) : Control of by Chain of transformations
Process 1:
Process 2:
w

## Slide 44: Some cases: Slave controller can be replaced by static block
  NO: series system (f independent of u. Here a static block for u is impossible so we must use cascade control. Problem: may be difficult to get fast slave loop)
  MAYBE parallell system (dangerous: may get unstable zero dynamics, so recommend cascade)
  YES. recycle system (no big problem, at least if delayed, since recycle gives positive feedback, here a static block may be OK)
Recycle system
  for initial response (s=infinity)
But be careful. Cascade is safer because then we can get real dynamics experimentally.