## Slide 1: PWC Basics: A Simple Chemical Process
Recycle A
C
O
L
U
M
N
Product B
REACTOR
A  B
Cooling
Duty
Fresh A
FEHE
ENERGY RECYCLE
MATERIAL RECYCLE
PROCESS INTEGRATION
Minimizes
A consumed per kg B product
Steam consumed per kg B product
ENHANCES PROCESS PROFITABILITY

## Slide 2: PWC Basics: Chemical Process Operation
Key Production Objectives
Operate plant to meet production objectives 24X7
Process Disturbances
Production Objective Itself Can Change
Safety
Stability
Economics
Production
Rate
Product
Quality
Effluent
Specs
Ambient
Conditions
Raw material
Quality
Sensor
Noise
Equipment
Characteristics

## Slide 3: PWC Basics
Safety
Stability
≡
Operate Process at Steady State
Accumulation Rate Rate Generation
Rate In Out Rate
=
+
−
Need PWC to drive accumulation of all independent inventories to zero
0

## Slide 4: PWC Basics
Regulatory Control System
  Drives all inventory accumulation terms to zero
  Ensures plant operation around a steady state
What steady state to operate at
  Economic Optimum
    Minimize expensive utility consumption
    Maximize production

## Slide 5: Plantwide Control Hierarchy
PLANT
Measurements
Regulatory Control Layer
(updates every few secs)
Supervisory Control Layer
(updates every few mins)
Optimization Layer
(updates every few hrs)
PLANTWIDE CONTROL SYSTEM
SETPOINT
SETPOINT
SIGNAL TO VALVE
Economic Operation
Safe & Stable Operation

## Slide 6: Regulatory PWCS Design
What to Control
  All independent inventories (DOF)
    Material – Liquid level or gas pressure
    Energy – Temperature or vapor pressure
    Component – Composition, tray temperature (inferential)
  Throughput or Production Rate
Degree of tightness of control
  Should energy inventories be tightly controlled?
  Should surge level inventories be tightly controlled?
What to manipulate
  Pair close
    Fast dynamics
    Tight closed loop control
Location of through-put manipulator a key decision for inventory management and economics

## Slide 7: The Transformation of Variability Perspective
HEAT EXCHANGER EXAMPLE
Condensate out
Process Stream in
HEAT EXCHANGER
Steam in
Control
Valve
Process Stream out
Transmitter
TC
TT
Steam Flow
Temperature
Steam Flow
Temperature
CONTROL
SYSTEM
Agent for transformation / management of process variability

## Slide 8: Where to Transform Variability
Surge level
  Does not affect steady state
  Regulate loosely for filtering out flow transients
Energy Inventories
  Regulate tightly to guarantee safety (rxn runaway?)
Product quality
  Regulate tightly
  Minimize “free” product give-away
Production rate
  Often “loose” is OK (eg meet the monthly target)
Recycle loop circulation rates
  Regulate to avoid large drifts
  All equipment inside recycle loop see acceptable variability

## Slide 9: Nonlinearity in Material Recycle Loops
Fresh Feed Rate
Recycle Rate
NO FEASIBLE STEADY STATES
Snowballing
Fixing the fresh feed rate of a recycled component is NOT a good idea
Possibility of overfeeding induced instability

## Slide 10: Material Recycle Snowball Effect
REACTOR
A  B
Cooling
Water
Fresh A
Recycle A
C
O
L
U
M
N
Product B
TC
LC
PC
LC
LC
RC
TC
FC
TPM
Time
%
FA
R
Recycle loop shows large swings
Large Throughput De-rating

## Slide 11: Material Recycle Snowball Effect
REACTOR
A  B
Cooling
Water
Fresh A
Recycle A
C
O
L
U
M
N
Product B
TC
LC
PC
LC
LC
RC
TC
FC
TPM
No large swings in recycle rate
Lower Throughput De-rating

## Slide 12: Alternative Material Balance Control Schemes
Configure control structure to transform recycle rate variability out of the recycle loop
F
P
Recycle
FC
IC
IC
Fixed Feed
Recycle Floats
FC
F
P
Recycle
IC
IC
Fixed Recycle
Feed Floats

## Slide 13: PWC Basics: Throughput Manipulation
THROUGHOUT MANIPULATOR (TPM)
The setpoint adjusted to effect a change in production/processing rate
FC
TPM
LC
LC
LC
Unit 1
Unit 2
Unit 3
*
Lost production
Unit 1
Unit 2
Unit 3
*
FC
TPM
LC
LC
LC
No (min) production loss

## Slide 14: PWC Basics: TPM Selection
When is TPM choice flexible
  Large storage tanks supply the fresh feed(s)
  Variability in storage tank level is acceptable
    Allows structures that bring in fresh feed(s) as make-up
Usually plant designs have large recycle rates
  Design in the snowballing region
  Capacity bottleneck then is likely inside the loop
Where to locate the TPM
  Inside the recycle loop
  If multiple recycle loops, on a common branch
  If bottleneck is known, AT the bottleneck

## Slide 15: Reactor Separator Recycle Process
A + B → C
FA
FB
C
O
L
U
M
N
Product C
Control DOFs 9
Surge Levels -2
Given Column Pr -1
---------------------------------
Steady State DOF 6
---------------------------------

## Slide 16: PWCS Design: TPM at Fresh Feed
A + B → C
FA
FB
C
O
L
U
M
N
Product C
PC
LC
TC
FC
LC
TC
CC
FC
X
LC
FC
TPM

## Slide 17: PWCS Design: Recycle Drifts
Beware of subtle plantwide recycle loop inventory drifts
Stoichiometric feed balancing
Plantwide balances close slowly due to recycle
Always examine process input-output structure
Every component must find a way out or get consumed (DOWNS’ DRILL)
For (near) pure C product, FA = FB
FC
IC
IC
FA
FB
PC
Recycle A
Recycle B

## Slide 18: PWCS Design: TPM at Column Boilup
A + B → C
FA
FB
C
O
L
U
M
N
Product C
PC
FC
LC
TC
CC
FC
X
LC
TC
FC
TPM
LC

## Slide 19: PWCS Design Steps
DOF analysis and control objectives
  Production rate, Product quality
  Safety limits (eg UFL < gas loop composition < LFL)
  Inventories
  Economic
Choose TPM
  Feed set by an upstream process
  On demand operation (utility plants)
  Flexible
    Inside the recycle loop at the feed of the most non-linear/fragile unit
    If bottleneck is known, at the bottleneck inside the recycle loop
Design “local” loops for closing all independent material and energy balances around the TPM
  Radiate outwards from the TPM
  Check consistency of material / energy balance closure (Downs’ Drill)
Design economic control loops
  Active constraint control & SOCV control

## Slide 20: Mode I Optimum Operation
A + B → C
FA
FB
C
O
L
U
M
N
Product C
OBJECTIVE
MIN J = Boilup
at given throughput
subject to process constraints
ACTIVE CONSTRAINTS
TrxrMAX Max reactor temperature
LVLrxrMAX MAX reactor level
xCprdMIN MIN product purity
EQUALITY CONSTRAINT
P Given throughput
UNCONSTRAINED DOFs
SOCV1 L/F Reflux to feed ratio
SOCV2 [A/B]rxr Reactor A/B ratio

## Slide 21: Mode II Optimum Operation
A + B → C
FA
FB
C
O
L
U
M
N
Product C
OBJECTIVE
MAX J = Throughput (P)
subject to process constraints
ACTIVE CONSTRAINTS
TrxrMAX Max reactor temperature
LVLrxrMAX MAX reactor level
xCprdMIN MIN product purity
∆PMAX Capacity bottleneck
UNCONSTRAINED DOFs
SOCV1 L/F Reflux to feed ratio
SOCV2 [A/B]rxr Reactor A/B ratio

## Slide 22: PWCS Design: TPM at Fresh Feed
A + B → C
FA
FB
C
O
L
U
M
N
Product C
PC
LC
TC
FC
LC
TC
CC
FC
X
LC
FC
TPM
MODE II CONSTRAINTS
TrxrMAX, LVLrxrMAX
xCprdMIN ,ΔPMAX
SOCVs
L/F, [A/B]rxr
CC
xCprdMIN
TrxrMAX
LVLrxrMAX
CRC
[A/B]rxr
X
L/F
∆PC
∆PMAX - δ
Long Loop → Large δ
MAX
MAX - δ

## Slide 23: PWCS Design: TPM at Fresh Feed
A + B → C
FA
FB
C
O
L
U
M
N
Product C
PC
LC
TC
FC
LC
TC
CC
FC
X
LC
FC
CC
xCprdMIN
TrxrMAX
LVLrxrMAX
CRC
[A/B]rxr
X
L/F
∆PC
∆PMAX - δ
Long Loop → Large δ
TPM
LS

## Slide 24: PWCS Design: TPM at Bottleneck
A + B → C
FA
FB
C
O
L
U
M
N
Product C
PC
FC
LC
TC
CC
FC
X
LC
TC
FC
TPM
LC
X
L/F
CRC
[A/B]rxr
TrxrMAX
LVLrxrMAX
CC
xCprdMIN
∆PC
∆PMAX - δ
MAX
MAX - δ
Negligible back-off

## Slide 25: PWCS Design: TPM at Bottleneck
A + B → C
FA
FB
C
O
L
U
M
N
Product C
PC
FC
LC
TC
CC
FC
X
LC
TC
FC
LC
X
L/F
CRC
[A/B]rxr
TrxrMAX
LVLrxrMAX
CC
xCprdMIN
∆PC
∆PMAX
TPM
LS

## Slide 26: Switching Regulatory Control Structure
A + B → C
FA
FB
C
O
L
U
M
N
Product C
TC
LC
FC
CC
xCprdMIN
PC
LC
FC
LC
TC
CC
FC
X
TrxrMAX
CRC
[A/B]rxr
X
L/F
TPM
LS
LS
LS
∆PC
∆PMAX
LTC
Σ
−2°C
LVLrxrMAX
HLC
Σ
−5%

## Slide 27: Summary
Locate TPM at bottleneck inside recycle loop
Economic considerations play a major role in regulatory control layer design
COMMON SENSE MUST PREVAIL
  Everything must be carefully thought through
  It pays to be systematic

## Slide 28: Case Study I: Ester Purification Process
Recycle
QReb
QCnd
FTot
FH2O
FCol
L
D
FEster
FFeed
Extractor
Distillation column
FAlc-wash
Ethyl acetate
Ethanol
Water

## Slide 29: Flowsheet Material Balances
Fresh feed
Water feed
EtOH-H2O recycle
Product
LLX feed
Alcohol wash
Column feed
Recycle
QReb
QCnd
FTot
FH2O
FCol
L
D
FEster
FFeed
Extractor
Distillation column
FAlc-wash

## Slide 30: Control Objective
Operate plant to maximize ester production
BOTTLENECK
  Maximum water solvent rate to the extractor
    Hydraulic constraint
  Limits alcohol extraction capacity

## Slide 31: Steady State Bifurcation Analysis
Infeasible setpoint
(a)
No setpoint Infeasibility
(b)
Fresh Water Rate = MAX

## Slide 32: Control Structure 2
Recycle
QReb
QCnd
FTot
FH2O
FCol
L
D
FEster
FFeed
Extractor
Distillation column
FAlc-wash
FC
TPM
PC
FC
MAX
LC
LC
TC
LC
LC
FC
X

## Slide 33: CS1: TPM at Bottleneck Feed
Recycle
QReb
QCnd
FTot
FH2O
FCol
L
D
FEster
FFeed
Extractor
Distillation column
FAlc-wash
FC
TPM
PC
FC
MAX
LC
LC
TC
LC
LC
FC
X

## Slide 34: CS1: TPM at Bottleneck Feed
Recycle
QReb
QCnd
FTot
FH2O
FCol
L
D
FEster
FFeed
Extractor
Distillation column
FAlc-wash
FC
TPM
PC
FC
MAX
LC
LC
TC
LC
LC
FC
X

## Slide 35: CS2: TPM at Fresh Feed
Recycle
QReb
QCnd
FTot
FH2O
FCol
L
D
FEster
FFeed
Extractor
Distillation column
FAlc-wash
FC
TPM
PC
FC
MAX
LC
LC
TC
LC
LC
FC
X

## Slide 36: CS1 Closed Loop Transients Large Feed Composition Change

## Slide 37: CS2 Closed Loop Transients Large Feed Composition Change

## Slide 38: Throughout Maximization Results
147.3 kmol/h
Nominal maximum throughput
174 kmol/h
136 kmol/h
CS1 → Self regulatory
CS2 → Overfeeding infeasibility