## Slide 1: Changing between Active Constraint Regions for Optimal Operation: Classical Advanced Control versus Model Predictive Control
Adriana Reyes-Lúa, Cristina Zotică, Tamal Das, Dinesh Krishnamoorthy and Sigurd Skogestad
Department of Chemical Engineering
Norwegian University of Science and Technology (NTNU)
Trondheim
ESCAPE’28. Graz, Austria, 13 June 2018

## Slide 2: Outline
Introduction: optimal operation of a process plant
Alternatives for implementing optimal operation (control)
  Model predictive control (MPC)
  Classical advanced control structures
Case Study: optimal control of a cooler
Conclusion

## Slide 3: Optimal operation (economics)
Minimize cost J = J(u,x,d)
u = degrees of freedom
x = states (internal variables)
d = disturbances
J = cost feed + cost energy – value of products
J
uopt
Jopt
1. Introduction

## Slide 4: Optimal operation (economics)
Minimize cost J = J(u,x,d)
Subject to satisfying constraints
u = degrees of freedom
x = states (internal variables)
d = disturbances
J
uopt
Jopt
constraint
J = cost feed + cost energy – value of products

## Slide 5: Active constraints
Active constraints:
  variables that should optimally be kept at their limiting value.
Active constraint region:
  region in the disturbance space defined by which constraints are active within it.
Region 1
Region 2
Region 3
Disturbance 1
Disturbance 2
Optimal operation:
How switch between regions?

## Slide 6: Outline
Introduction: optimal operation of a process plant
Alternatives for implementing optimal operation (control)
  Model predictive control (MPC)
  Classical advanced control structures (ACS)
Case Study: optimal control of a cooler
Conclusion

## Slide 7: Control hierarchy in a process plant
Regulatory control (PID):
  Stable operation (CV2)
Supervisory control (“Advanced control” or MPC):
  Economics: Switch between active constraints (CV1)
  Follow set points from long-term economic optimization layers.
CV = controlled variable

## Slide 8: Control is about implementing optimal operation in practice
Many cases: Solution is fully constrained, but constraints change
 Key is to control the active constraints
Region 1
Region 2
Region 3
Disturbance 1
Disturbance 2

## Slide 9: Model predictive control (MPC)
Can include constraints explicitly
If lack of DOF to meet control specifications:
  Conventional: Use weights
    (Partially) give up variables with small weights in objective function.
  Use two-stage MPC with constraint priority list:
    Stage 1. Check for steady-state feasibility and give up low-priority constraints if necessary
    Stage 2. Solve conventional dynamic MPC

## Slide 10: Optimization with PI-controller
max y
s.t. y ≤ ymax
u ≤ umax
Example: Drive as fast as possible from Graz to Vienna (u=power, y=speed, ymax = 130 km/h)
Optimal solution has two active constraint regions:
  y = ymax  speed limit
  u = umax  max power
Note: Positive gain from MV (u) to CV (y)
Solved with PI-controller
  ysp = ymax
  Anti-windup: I-action is off when u=umax
s.t. = subject to
y = CV = controlled variable
ysp = ymax
PI

## Slide 11: Optimization with PI-controller
min u
s.t. y ≥ ymin
u ≥ umin
Example: Minimize heating cost (u=heating, y=temperature, ymin=20 °C)
Optimal solution has two active constraint regions:
  y = ymin  minimum temperature
  u = umin  heating off
Note: Positive gain from MV (u) to CV (y)
Solved with PI-controller
  ysp = ymin
  Anti-windup: I-action is off when u=umin
s.t. = subject to
y = CV = controlled variable
ysp = ymin
PI

## Slide 12: Optimization with PI-controller
Both cases:
Normal operation: y=ysp
When u (MV) reaches constraint: control of y (CV) is given up
Generalization to multivariable case. Input saturation pairing rule:
Pair low-priority controlled variable (y, CV) (can be given up) with a manipulated variable (u, MV) that may saturate.
Or equivalently
Pair high-priority controlled variable (y, CV) (cannot be given up) with a manipulated variable (u, MV) that is not likely to saturate.
PI

## Slide 13: Multivariable using PI-control: Must decide on pairing
Input saturation pairing rule:
Pair high priority controlled variable (CV) (cannot be given up) with a manipulated variable (MV) that is not likely to saturate.
If we don’t follow rule: Need to use selector (max/min)
when input constraint is reached
Example priority list
1. u1 ≤ u1max
2. y1 = y1sp  high-priority CV
3. y2 = y2sp  low-priority CV
From rule: pair y1 with u2
PI
PI

## Slide 14: Classical advanced control structures (ACS)
Used when single-loop PID is not sufficient.
Examples:
  Cascade control
  Feedforward control / Ratio control
  Decoupling
  Selectors
  Split range control (SRC)
  Input resetting or valve positioning control (VPC)
Can handle constraint changes

## Slide 15: Outline
Introduction: optimal operation of a process plant
Alternatives for optimal operation in the supervisory layer
  Model predictive control (MPC)
  Classical advanced control structures (ACS)
Case Study: optimal control of a cooler
Conclusion

## Slide 16: 3. Optimal control of a cooler

## Slide 17: 3. Optimal control of a cooler
Main control objective:
y1=TH=THsp
Secondary objective (can be given up)
y2= FH=FHsp
Manipulated Variables:
u1=zC , u2=zH
Both valves may satúrate at max
Disturbance:
TCin
Cooling water

## Slide 18: Multivariable: Cooler example
max y2 (throughput)
s.t. y1 = y1sp  temperature
u1 ≤ u1max
u2 ≤ u2max  max. throughput
y2 ≤ y2sp  desired throughput
Active constraint regions:
  y1 = y1sp, y2 = y2sp  «unconstrained» region
  y1 = y1sp, u2 = u2max
  y1 = y1sp, u1 = u1max
Input saturation pairing rule: Pair y1 (temperature) with a manipulated variable (MV) that is not likely to saturate.
It’s not possible to follow this rule since both MVs may saturate…
Will pair y1 with u1 for dynamic reasons
And will need logic (max/min-selector) for case when u1 saturates

## Slide 19: Pairings at nominal «unconstrained» operating point
FC may saturate for a
large disturbance (TCin)
Use FC to control TH

## Slide 20: Solution: Split range control with min-selector
Tuning of TC using SIMC rule:
  τc = 2θ = 88 s
  Kc = -0.55
  τI = 74 s

## Slide 21: Simulation: Split range control with min-selector

## Slide 22: MPC for cooler
For represents the flow at the nominal point.
 Objective function
(CV constraints)
Model 
MV constraints 
Tuning  trial and error

## Slide 23: MPC weight selection
α = [3.0, 0.1]
β = [1.0, 1.0]
γ = [0.1, 3.0]
Tunings:
[ω₁ , ω₂ ]
Yellow:
Selected

## Slide 24: MPC vs PI
Disturbance (TCin)
t = 10 s; + 2°C
t = 1000 s; + 4°C
Yellow: MPC:
Δt = 50 s
ω₁ = 3
ω₂ = 0.1
FC
FH
TH
Red: Split Range Control (PI)

## Slide 25: 4. Conclusion
Optimal control for most simple systems can be achieved using classical advanced control structures.
  Comparable response to MPC.
  Simpler implementation compared to MPC.
  Shorter computational time.
A priority list of constraints is an important tool to design the supervisory control layer.

## Slide 26: Acknowledgement
This work was partly supported by the Norwegian Research Council under
HighEFF: Energy Efficient and Competitive Industry for the Future and
SUBPRO: Subsea Production and Processing

## Slide 27: Extra slides

## Slide 28: Optimize
Optimize for expected disturbances (d)
We need a good model, usually steady-state.
Optimization can be time consuming.
Main goal for control puposes: identify active constraint regions
Model equations
Operational constraints
min J(u,x,d)
s.t.
f(u,x,d) = 0
g(u,x,d)≤ 0
u

## Slide 29: Systematic procedure for plantwide control
Start “top-down” with economics:
Step 1: Define operational objectives and constraints
Step 2: Optimize steady-state operation
Step 3: Decide what to control (CVs)
Step 4: TPM location
Then bottom-up:
Step 5: Regulatory control
Finally: Make link between “top-down” and “bottom up”
Step 6: “Advanced/supervisory control” system

## Slide 30: Requirement for the supervisory layer
Maintain optimal operation despite:
  disturbances
  changes of active constraint region
Usually:
Number of controlled variables (CV)
Number of
degrees of freedom (MV)
≥
How should we use the available MVs?

## Slide 31: Priority list of constraints
P1: MV inequality constraints  physical constraints
P2: CV inequality constraints  may be given up
P3: MV or CV equality constraints  optimal operation
P4: Desired throughput  give up at bottleneck
P5: Self-optimizing variables  can be given up
A. Reyes-Lúa, C. Zotica, S. Skogestad, 2018. Optimal Operation with Changing Active Constraint Regions using Classical Advanced Control. In: 10th ADCHEM. IFAC, Shenyang, China.

## Slide 32: Model predictive control (MPC)
Meets constraints “by design”.
Explicit model required.
If lack of DOF to meet control specifications:
  Modify weights in objective function.
  Use two-stage MPC with a priority list:
    Sequence of local steady state LPs and/or QPs
      Add constraints in order of priority
      Find feasibility
    MPC: dynamic optimization problem

## Slide 33: Optimal operation using advanced control structures Multivariable: Must decide on pairing
Input saturation pairing rule
Pair the high priority controlled variable (CV) (cannot be given up) with a manipulated variable (MV) that is not likely to saturate.

## Slide 34: Optimal operation using advanced control structures
Control structure (pairing) may vary with the operating region.
Region 1
Region 2
Region 3
Disturbance 1
Disturbance 2
A. Reyes-Lúa, C. Zotica, S. Skogestad, 2018. Optimal Operation with Changing Active Constraint Regions using Classical Advanced Control. In: 10th ADCHEM. IFAC, Shenyang, China.

## Slide 35: Priorities and constraints
Priority level | Description | Constraints
1 | Feasibility region | FH ≤ FHmax FC ≤ Fcmax
2 | Main control objective | TH = THsp
3 | Desired throughput | FH = FHsp
MV constraints | CV constraints
FH ≤ FHmax FC ≤ Fcmax | TH = THsp FH = FHsp

## Slide 36: Handling constraints using ACS
Input saturation pairing rule
A high priority controlled variable (CV) (which cannot be given up) should be paired with a manipulated variable (MV) that is not likely to saturate.
Pairing rule was followed?
Constraint reached
Do nothing
Give-up a low priority CV using selector
Do nothing: give-up controlling low priority CV
Reassign high priority CV to MV controlling low priority CV: ACS + min/max selector
YES
NO
Low priority?
YES
NO
MV
CV

## Slide 37: Active constraint regions
Active constraint in each region:

## Slide 38: 4. Alternatives for supervisory layer
  MPC
  Define:
  Priority list of constraints
  Objective function
  Prediction horizon
  Sampling time
  Control intervals
  Tuning (Δt, N, ωi)  trial and error
  Advanced Control Structures
  Define:
  Priority list of constraints
  Pairing at nominal point
  Gain of MVs on CV
  Tuning of PI-controller(s)
   well-known rules
  Set-up and solve dynamic optimization problem at every step.
  Set-up control structure.