## Slide 1: Ch 11.4 Stability
TexPoint fonts used in EMF.
Read the TexPoint manual before you delete this box.: AAAAAAAAAAA
NOTE: Stability of a linear system is a SYSTEM property, that is,
independent of the input signal (sine or step, etc.) and of where it
enters the system (input or disturbance, etc.)
Stability is a very important issue for control systems

## Slide 2: Linear system. Is g(s) stable?
g(s) = n(s)/d(s). Poles are solutions s=pi to d(s)=0.
    Example: G(s) = 1/(s-1)(s+2). Get p1=1 (unstable pole), p2=-2 (stable pole)
So time response contains term ept
    Example: G(s) = 1/(s-1), p=1
      Step response is: y(t) = -1(1-et) = et – 1 (unstable)
From this we see that for a polynomial system g(s)=n(s)/d(s) (no time delay):
Stability , Re(pi)<0 (all poles have negative real part)
, All poles in left half plane (LHP)
  Applies also to the linear system dx/dt = Ax + Bu, but here the poles (pi) are the eigenvalues of A (see proof below)
Repetition

## Slide 3: Poles = Eigenvalue of A-matrix
Linear system in deviation variables (state space form)
dx/dt = A x + B u
y = C x + D u
Laplace. Get transfer function from u to y
G(s) = C (sI-A)-1 B + D = n(s)/d(s)
From mathematics: (sI-A)-1 = adj(sI-A)/det(sI-A), so
d(s) = det(sI-A) = pole polynomial
But det(sI-A)=0 is also the formula for finding the eigenvalues of A
Conclusion: Solutions to d(s)=0 are the poles which are identical to the eigenvalues of A
pi = eig(A)
Repetition

## Slide 4: Pole in right half plane (RHP): UNSTABLE
Unstable
Stable
Stable
Oscillations
Unstable
Oscillations
G(s) = n(s)/d(s) where
d(s) = (s-p1)(s-p2)
Real pole p: Get term ept .
For Re(p)>0 (RHP-pole):
Unstable since ept! 1 (as t! 1)
Complex pole pair (p12 = p § jω)
Gives oscillations:
c1 ep1t + c2ep2t = c ept sin(ωt + Á)
Which are unstable if Re(p)>0
Repetition

## Slide 5
0
0.2
0.4
0.6
0.8
1
1.2
1.4
1.6
1.8
2
-2
-1
0
1
2
3
4
Step Response
Time (seconds)
Amplitude
step(g1,g2,g3,g4,g5,g6,2)
(p=1, unstable)
(p=0,
borderline)
(p=-1, stable)
(p1,2=0±10i, borderline)
(p1,2=0.5 ±3.12i, unstable)
(p1,2=-0.5 ±3.12i, stable)
Repetition

## Slide 6: Stability of closed-loop systems
Closed-loop transfer functions, T(s) = n(s)/d(s)
  n(s) = direct path
  d(s) = 1 + loop(s)
    where loop(s) = g(s) gm(s) c(s)
Same d(s) for any input (disturbance)/output!
  Makes sense because stability is a system property
Conclusion: Closed-loop poles are given by solutions to “closed-loop characteristic equation”
    d(s) = 1 + loop(s) = 0
Repetition

## Slide 7: What about time delay?
Can use Pade approximation, for example, order n:
Comment: More exact for stability of closed-loop system with delay: Frequency response and Bode criterion (later)
Repetition

## Slide 8: How do we test for stability? T(s) = n(s)/d(s)
Method 1. Compute poles p (roots of d(s)=0) = eigenvalues of A-matrix for system T(s), p=λ(A).
    Stable if and only if all poles are in left half plane, Re(p)<0
    OK numerically (for given system), but difficult to find poles p analytically
Method 2 (much simpler). Look at coefficients ai in d(s),
  d(s)= a0 + a1s + … + ansn
    Good for analytical results. Don’t need to find poles p
    Test 1. All a’s must have same sign* for stability (necessary condition)
    Test 2. Routh array (Routh-Hurwitz condition): Necessary and sufficient**
Method 3. Closed-loop system. Frequency analysis (see later)
    Don’t use poles
    Consider loop transfer function, L = GC
    Bode stability test for stability: Loop gain|L| < 1 at frequency ω180
    Can include time delay (exact)
* Necessary and sufficient for 2nd order system (n=2)
** The detailed formulas are no longer in the book by Seborg, but it remains part of your syllabus.
See also Exercise 11. You will get the formulas if you need it on the exam.

## Slide 9: Important
The only way we can change dynamics (move poles) and stabilize is by feedback
So: Stabilization with feedforward does NOT work
  Example: level control
    G(s) = k’/s
    Integrating process with pole at s=0. At the limit to instability
    It is practically impossible to control level by trying to set qout=qin using feedforward.
    We get «internal instability»: Level will eventually go out of bound
But we need to be careful: Feedback often causes oscillations and even instability

## Slide 10: Example 1
Unstable plant (reactor): g(s) =1/(s-1)
P-controller: c(s)=Kc
For what Kc is system stable?
  Method 1 (poles),
  Method 2 (sign coefficients),
  Root locus (plot location of closed-loop poles as function of Kc)
Re(p)
Im(p)
Root locus for s=1-Kc
= Location of pole s for increasing gain
-3 -2 -1 0 1 2
Kc=2 (stable)
Kc=1 (limit to instability)
Kc increases
(more stable for large Kc)
Kc=0 (unstable)

## Slide 11: Method 1. Analytic solution using poles. A lot of work*!
Analytic dolution with Matlab:
syms s Kc
g=1/(6*s+1)
gm=(-s+1)/(s+1)
clpoles=solve(1+Kc*g*gm==0)
solve(real(clpoles(1))==0)
solve(real(clpoles(2))==0)
Solution:
g =1/(6*s + 1)
gm =-(s - 1)/(s + 1)
clpoles =
Kc/12 + (Kc^2 - 38*Kc + 25)^(1/2)/12 - 7/12
Kc/12 - (Kc^2 - 38*Kc + 25)^(1/2)/12 - 7/12
ans =-1.0
ans =7.0
Method 2 (simpler). Coefficients
Test 1. Check signs of Char. Eq..:
d(s) = 1 + loop = 1 + Kc*(-s+1)/[(s+1)(6s+1)]=0
6s^2 + (7-Kc)s + (1+Kc) = 0
Stable -> all coefficients positive ->
Kc>-1 (lower limit for positive feedback)
Kc<7 (upper limit because of RHP-zero)
(necessary and sufficient for 2nd order system)
* Difficult for order 3, very difficult for order 4,
Impossible for order 5 or higher (Abel)
EXAMPLE 2
Kc=7: Poles cross into RHP
and we have instabiliy
Kc=0: Start at open-loop poles
(-1 and -1/6)
Root locus:

## Slide 12
Complete Routh array
b1 = (17*8-10*(1+Kc)) / 17
b2 = 0
c1 = (1+Kc)
Stability: Elements in first column > 0.
Conclusion:
b1>0 -> Kc<12.6
c1>0 -> Kc>-1
Test 2. ROUTH array: Find location (RHP/LHP) of poles without actually having to find them.
“Advanced version of looking at sign of coefficients in pole polynomial d(s)”
Kc
-1
12.6
STABLE
UNSTABLE
UNSTABLE
From old edition of Seborg book:

## Slide 13: Root locus: How do the closed-loop poles depend on the controller gain Kc?
s=tf('s')
Kc=12.6 % limit to instability)
loop = Kc/[(5*s+1)*(2*s+1)*(s+1)]
sisotool(loop) % root locus
Kc=0 (root locus starts at the poles x in g)
Kc large

## Slide 14
Root locus: How do the closed-loop poles depend on the controller gain Kc?
Kc=0
Kc=0: Open-loop poles
Kc=0.1: Starts oscillating
Kc=15: Goes unstable
Step response for Kc=1.62:
0
1
2
3
4
5
6
7
0
0.1
0.2
0.3
0.4
0.5
0.6
0.7
0.8
0.9
1
Step Response (P-control)
Time (seconds)
Amplitude
s=tf('s')
Kc=1.62
g = 4/[(s+1)*(s+2)*(s+3)]
loop = Kc*g
sisotool(loop) % root locus, etc.
PI-control
(11-104)
EXAMPLE 11.12
11.5
Figure 11.27
(11-105)
/
All coefficients in d(s)=1+L(s) are always positive but still the system goes unstable for Kc>15 (can use Routh Array to find this value)