## Slide 1: Frequency analysis
Important for understanding stability and robustness of feedback systems
TexPoint fonts used in EMF.
Read the TexPoint manual before you delete this box.: AAAAAAAAAA

## Slide 2
Chapter 14
Mathematics. Complex number G, j2=-1
Re(G)
Im(G)
G(jω)=R+jI
R
I
G
Im(G)=R, Re(G)=I
Polar form
May also use i instead of j, i2=-1. (i is common in mathematics; j is more common in control)
arctan = arctg = atan = tan-1
From degrees to radians: Multiply by
Examples:
j-axis =
Real axis =
Euler’s formula

## Slide 3
Chapter 14
Multiply complex numbers:
Multiply magnitudes and add phases
Polar form
|
|
G

## Slide 4
Force linear system with sinusoidal input: u(t) = u0 sin t
Output has same frequency: y(t) = y0 sin (t + ϕ)
Chapter 14
14.1
Period: P[s]
Frequency:  [rad/s] = 2π / P
Phase shift: ϕ [rad] =
Amplitude ratio (gain): AR = y0/u0
We have assumed deviation variables, otherwise we need to add an «average» or «bias» to both u(t) and y(t).
We assume that the input sinusoid is persistent and consider the «steady-state» as
One period (cycle) = 2π [rad] = 360o
u0=
y0=
u

## Slide 5
Example: Ground temperature phase shift
Surface temperature:
u(t) = uavg + u0 sin ((t-t0))
    uavg = 62oF (= 17C)
    Amplitude u0 = 62-40=22oF
Frequency of oscillations:
  P = 365d,
  =0.017 rad/d,
Ground temperature:
y(t) = yavg + y0 sin ((t-t0) + ϕ)
    yavg = 62oF (= 17C)
    y0 and φ depend on depth X
Amplitude (y0) and Gain decreases with depth X.
X=5ft, y0 = 62-50=12 F,
Gain = AR = 0.55
Time shift and phase shift increases with depth X.
X=5 ft, Δt = 35 days (=from Feb.4 to Mar. 11 = from Aug. 6 to Sep.10):
ϕ = - Δt  = -35d * 0.017 rad/d= - 0.602 rad = -34.5o
0oC
33oC
u(t)
y(t)
AR = amplitude ratio = gain =

## Slide 6
General: Simple method to find sinusoidal response of system G(s)
Input signal to linear system: u = u0 sin(ωt)
Steady-state (“persistent”, t→∞) output signal: y = y0 sin(ωt + φ)
What is AR = y0/u0 and φ?
Solution (extremely simple!)
Find system transfer function, G(s)
Let s=jω (imaginary number, j2=-1) and evaluate G(jω) = R + j I (complex number)
Then (“believe it or not!”)
    AR = |G(jω)| (magnitude of the complex number)
    φ = Å G(jω) (phase of the complex number)
Re(G)
Im(G)
G(jω)=R+jI
R
I
Å G
|G|
G(s)
u
y

## Slide 7
u
y
As t →∞: (see 4-26)
y(t) = AR *A*sin(ωt+φ)
u(t) = A sin(ωt)
General (VERY SIMPLE).
Set s=jω in G(s). Then
AR = |G(jω)|
φ = Å G(jω)
(5-22)
Note: A is the same as u0
AR =
Proof, first-order system

## Slide 8
Example: Gain and phase shift for first-order system:
R I
Chapter 14
Gain and phase shift
1.
2.
3.
SIMPLER: Use polar form formulas for complex numbers! G=G1/G2, where G1=k, G2=τs+1.
Set
This method is
not really
recommended

## Slide 9
0
2
4
6
8
10
12
14
16
18
20
-1
-0.8
-0.6
-0.4
-0.2
0
0.2
0.4
0.6
0.8
1
0
2
4
6
8
10
12
14
16
18
20
-1
-0.8
-0.6
-0.4
-0.2
0
0.2
0.4
0.6
0.8
1
0
2
4
6
8
10
12
14
16
18
20
-1
-0.8
-0.6
-0.4
-0.2
0
0.2
0.4
0.6
0.8
1
0
2
4
6
8
10
12
14
16
18
20
-1
-0.8
-0.6
-0.4
-0.2
0
0.2
0.4
0.6
0.8
1
0
2
4
6
8
10
12
14
16
18
20
-1
-0.8
-0.6
-0.4
-0.2
0
0.2
0.4
0.6
0.8
1
SINUSOIDAL RESPONSE OF FIRST-ORDER SYSTEM
k = 1, τ = 1 [s]
u(t) = sin(ωt)
y(t) = AR sin(ωt + φ )
w=0.3; tau=1; t = linspace(0,20,1000);
u = sin(w*t);
AR = 1/sqrt((w*tau)^2+1)
phi = - atan(w*tau), phig=phi*180/pi, dt=-phi/w
y = AR*sin(w*t+phi);
plot(t,y,t,u)
6 Plots: Increase ω from 0.1 to 30 rad/s
1
2
3
4
5
6
!
=
0
.
1
r
a
d
/
s
,
P
=
6
2
.
8
s
A
R
=
0
.
9
9
5
Á
=
-
0
.
1
r
a
d
=
-
5
.
7
o
¢
t
=
0
.
9
9
7
s
!
=
1
r
a
d
/
s
,
P
=
6
.
2
8
s
A
R
=
0
.
7
0
7
Á
=
-
0
.
7
8
5
r
a
d
=
-
4
5
o
¢
t
=
0
.
7
8
5
s
!
=
1
0
r
a
d
/
s
,
P
=
0
.
6
2
8
s
A
R
=
0
.
0
9
9
5
Á
=
-
1
.
4
7
r
a
d
=
-
8
4
.
3
o
¢
t
=
0
.
1
4
7
s
!
=
3
0
r
a
d
/
s
,
P
=
0
.
2
0
9
s
A
R
=
0
.
0
3
3
Á
=
-
1
.
5
4
r
a
d
=
-
8
8
.
1
o
¢
t
=
0
.
0
5
1
s
!
=
3
r
a
d
/
s
,
P
=
2
.
0
9
s
A
R
=
0
.
3
1
6
Á
=
-
1
.
2
4
r
a
d
=
-
7
1
.
6
o
¢
t
=
0
.
4
1
6
s
!
=
0
.
3
r
a
d
/
s
,
P
=
2
0
.
9
s
A
R
=
0
.
9
5
8
Á
=
-
0
.
2
9
1
r
a
d
=
-
1
6
.
7
o
¢
t
=
0
.
9
7
2
s

## Slide 10
Chapter 14

## Slide 11
Chapter 14
1/√2 = 0.707
-arctg(10)=-84.3◦
-arctg(1)=-45◦
-arctg(0.1)=-5.7◦

## Slide 12
Misprint: Should start from 1.0
Note: Nyquist plot is not included in last edition

## Slide 13: Example: Ground temperature phase shift. X=5ft What is τ if assume a first-order response from u to y? g(s) = k/(τs+1)
Data: u0 = A= 22, y0 = 12, =0.017 rad/d, ϕ = – 35o
Solution:
We know from physics that the gain k=1. So g(s) = 1/(τs+1)
From amplitude data: AR = y0/u0 = 0.545.
  Get:
From phase shift data. ϕ = – 35o
  Get:
Conclusion: This system is more complex than first order (no big surprise!)
It’s described by partial differential equations and can be approximated by a high-order system with many poles and zeros.
For example, g(s) = (τ2s+1) / (τ1s+1) (τ3s+1) where τ1 > τ2 > τ3

## Slide 14: Frequency response of time delay
g=e-θs
Gain = |g(jω)| = 1
Phase shift = ϕ = (g(jω)) = - ωθ [rad]
Alternative proof: Time domain
u(t)
y(t)

## Slide 17
Solution:
If we also have a time delay

## Slide 18
OK!

## Slide 20
Oops! Phase drops for RHP zero
Phase increases for LHP zero
Peak goes to infinity when ξ=0

## Slide 21
Figure 14.4 Bode diagram for a time delay, e-θs.
Chapter 14
-1 rad = -57o at ωθ = 1
=-ωθ
Bode plot of time delay.
G = exp(-θs)
|G(jω)| = 1

## Slide 22
ASYMPTOTES
Frequency response of term (Ts+1): set s=jω.
Asymptotes:
(jωT + 1) ~ 1 for ωT << 1 (slope n=0, phase=0)
(jωT + 1) ~ jωT for ωT >> 1 (slope n=1, phase=90o)
Gain slope n: |G|~ωn
Rule for asymptotic Bode-plot, L = k(Ts+1)/(τs+1)….. :
Start with low-frequency asymptote (s→0)
(a) If constant (L(0)=k):
Gain=k (slope=0)
Phase=0o
(b) If integrator (L=k’/s):
Gain slope= -1 (on log-log plot). Need one fixed point, for example, gain=1 at ω=k’
Phase: -90o.
2. Break frequencies (order … from large T and τ … to small T and τ):
3. Time delay, e-θs. Gain: no effect, Phase contribution: -ωθ [rad] (-1 rad = -57o at ω=1/θ)
 | Change in gain slope | Change in phase
ω=1/T (zero) | +1 | +90o (-90o if T negative)
ω=1/τ (pole) | -1 | -90o (+90o if τ negative)

## Slide 23
Example with phase lead (not so common in process control)
Frequency
[rad/s ]

## Slide 24
Chapter 14
=2
PI-controller:

## Slide 25
Bode plots of ideal parallel PID controller and series PID controller with filter.
Ideal parallel:
Series with Derivative Filter:
C
C
Chapter 14

## Slide 26
EXAMPLE
L(s)=G(s)C(S):
Loop transfer function for
SIMC PI-control with τc=4 for
G(s) = 1/(100s+1)(2s+1)
Example: Typical L=GC

## Slide 27
Slope=-1
-90o
-180o
-2
-1
-2
-90o
ω=0.01
ω=0.05
ω=0.5
-180o
TexPoint fonts used in EMF.
Read the TexPoint manual before you delete this box.: AAAAA
L(s): SIMC PI-control with τc=4 for g(s) = 1/(100s+1)(2s+1)
Slope
Help lines
-2
-1
SOLUTION
Asymptotes: Start at low frequency, ω→0:
|L(jω)| = 1/ω. So: |L|=103 at ω=10-3

## Slide 28: Electrical engineers (and Matlab) use decibel for gain
|G| [dB] = 20 log10|G|
¦G¦ | ¦G¦ [dB]
0.1 | -20 dB
1 | 0 dB
2 | 6 dB
10 | 20 dB
100 | 40 dB
1000 | 60 dB
s=tf('s')
g = 10*(100*s+1)/[(10*s+1)*(s+1)]
bode(g) % gives AR in dB*
0
10
20
30
40
Magnitude (dB)
10
-4
10
-3
10
-2
10
-1
10
0
10
1
10
2
-90
-45
0
45
90
Phase (deg)
Bode Diagram
Frequency (rad/s)
GM=2 is same as GM = 6dB
Other way: |G| = 10|G|(dB)/20
*To change magnitude from dB to abs: Right click + properties + units (absolute, log scale)
*

## Slide 29: Bode stability condition (Closed-loop stability condition from analyzing loop L(s) = G C Gm)
Proof
Starting point: Stability is a system property for linear systems, so if the system is stable for one signal it’s stable for all signals.
  Consider a particular signal: Sinusoid with frequency ω180 (frequency where frequency shift around loop L(s) is -180o = -π rad).
  With negative feedback, the total phase shift around the loop is -360o, so this sinusoid comes «back in phase»
  If the gain around the loop is less than 1, the sinusoid will die out.
  Conclusion: The closed-loop system is stable if and only if |L(jω)|<1 at frequency ω180

## Slide 30
Chapter 14
c
c
180
180
Sigurd’s preferred notation in red 
|L(jω)| =
Å L(jω)=
Time delay margin (DM), Δθ= PM[rad]/ωc
GM = 1/|L(jω180)|
ω180 = frequency where phase shift around
the loop is -180o = - π rad.
Å L(jω180) = -180o = - π rad
PM = Å L(jωc) + 180o
= Å L(jωc) + π [rad]
ωc = frequency where loop gain is 1.
|L(jωc)| = 1
GM (dB)
Question: For SIMC, is ωc=1/τc? No, but it’s related. In many cases ωc=1/(θ+τc)

## Slide 31
L = gcgm = loop transfer function with negative feedback
Bode’s stability condition: |L(jω180)|<1|
  Limitations
    Open-loop stable (L(s) stable)
    Phase of L crosses -180o only once
  Stability margins
    GM = 1/|L(jω180)|, where Å L(jω180)|=-180o
    PM = Å L(jωc) + 180o , where |L(jωc)|=1
    How much delay will “eat up” the PM?
    Answer: PM= ωc Δθ [rad] DM = Δθ= PM[rad]/ωc
The same but more general: Nyquist stability condition:
  Locus of L(jω) should encircle the
  (-1)-point P times in the anti-clockwise
  direction (where P = no. of unstable
  poles in L).
Summary: CLOSED-LOOP STABILITY IN FREQUENCY DOMAIN
Stable plant (P=0): Closed-loop stable if L has no encirclements of -1
(=Bode’s stability condition)
GM = gain margin (>1 for stability; typicall want >3)
PM = phase margin (>0 for stability; typically want > 50o)
DM = delay margin (>0 for stability; typically want > 2θ)

## Slide 32
Example 1. P-control of delay process, g(s)=ke-θs. For what Kc is system stable?
Example 2. I-control of delay process. For what KI is system stable?
Solution. Stable if and only if
P-control: kKc < 1
I-control: kKI <

## Slide 33
Example 2, continued. I-control of delay process
what is ωc, ω180, GM, PM and DM & give for SIMC (analytical)
Solution
For any KI:
wc=k’ KI, w180=(pi/2)(1/theta).
GM = w180/k’KI = (pi/2)/(k’KI theta),
PM=(pi/2)- k’KI*theta,
DM = PM/wc = (pi/2)/k’KI - theta
SIMC with τc=θ gives k’KI = , so
wc = , w180= =
GM =π = 3.14.
PM = (pi-1)/2 = 1.07 rad = 61.5o
DM = (pi-1)*theta = 2.14 theta
General SIMC-PID for 2nd order delay process (with τI= τ1) gives: L(s) =
DM = (GM-1)θ

## Slide 34
EXAMPLE 3
L(s): SIMC PI-control with τc=4 for
g(s) = 1/(100s+1)(2s+1)

## Slide 35
-180o
TexPoint fonts used in EMF.
Read the TexPoint manual before you delete this box.: AAAAA
L(s): SIMC PI-control with τc=4 for g(s) = 1/(100s+1)(2s+1)
PM=57o
GM=1/0 = ∞
ωc = 0.19 rad/s
ω180 = ∞
SOLUTION
1

## Slide 36
With added delay, e-θs with θ=2
No change in gain
With added delay, e-θs with θ=2.
Contribution to phase is:
-5.7o at ω=0.1/θ = 0.05
-57o at ω=1/µ = 0.5
-180o
GM=1/0,4=2.5
PM=35o
= 0.61 rad
ωc = 0.19
ω180 = 0.4
EXAMPLE3’: ADD 2 UNITS OF DELAY
Now phase crosses -180o so
GM is no longer infinity
Phase addition from delay = -ωθ
At ωc: - -ωcθ= 0.19*2 = - 0.38 rad (-22o)
So new PM = 57o (old) – 22o = 35o

## Slide 37: Example 4. PI-control of integrating process with delay. Compare ZN and SIMC*
g(s) =k’e-θs/s
ZN: Use P-control and increase Kc until instability.
    Find: Pu = 4θ and Ku = (π/2)/(k’θ)
    Derivation:
      so: ,
      and at limit to instability: =
PI-controller, c(s) = Kc (1+1/(τIs))
 | Kc | τI
Ziegler-Nichols | 0.45Ku = 0.707/(k’ θ) | Pu/1.2=3.33θ
SIMC (τc=θ) | 0.5/(k’ θ) | 8θ
*Task: Compare Bode-plot (L=gc), robustness and simulations (use k’=1, θ=1).

## Slide 38
10
-2
10
0
10
2
10
4
Magnitude (abs)
10
-2
10
-1
10
0
10
1
-720
-540
-360
-180
0
Phase (deg)
Bode Diagram
Gm = 2.96 (at 1.49 rad/s) , Pm = 46.9 deg (at 0.515 rad/s)
Frequency (rad/s)
 | GM | PM | Delay margin, Δθ
Ziegler-Nichols | 1.87 | 24.9o | 0.57 s
SIMC (τc=θ) | 2.97 | 46.9o | 1.88 s
Ziegler-Nichols PI
SIMC-PI
Δθ= PM[rad]/ωc
ZN: Δθ = 24.9*(3.14/180)/0.76 = 0.572s
SIMC: Δθ = 46.9*(3.14/180)/0.515 = 1.882s
SIMC is a lot more robust:
s=tf('s')
g = exp(-s)/s
Kc=0.707, taui=3.33
c = Kc*(1+1/(taui*s))
L1 = g*c
figure(1), margin(L1) % Bode-plot with margins
% To change magnitude from dB to abs: Right click + properties + units
Kc=0.5, taui=8
c = Kc*(1+1/(taui*s))
L2 = g*c
figure(2), margin(L2)
10
-2
10
0
10
2
10
4
Magnitude (abs)
10
-2
10
-1
10
0
10
1
-720
-540
-360
-180
0
Phase (deg)
Bode Diagram
Gm = 1.87 (at 1.35 rad/s) , Pm = 24.9 deg (at 0.76 rad/s)
PM
PM
GM
GM

## Slide 39
Delay = 1

## Slide 40
0
5
10
15
20
25
30
35
40
-2
-1.5
-1
-0.5
0
0.5
1
1.5
2
2.5
3
SIMC
ZN
OUTPUT, y
INPUT, u
Conclusion: Ziegler-Nichols (ZN) responds faster to the input disturbance,
but is much less robust.
ZN goes unstable if we increase delay from 1s to 1.57s.
SIMC goes unstable if we increase delay from 1s to 2.88s.
t=0: setpoint change, t=20: input disturbance
Simulink file: tunepid4
s=tf('s')
g = exp(-s)/s
Kc=0.707, taui=3.33, taud=0 % ZN
sim('tunepid4')
plot(Tid,y,'red',Tid,u,'red')
Kc=0.5, taui=8, taud=0 % SIMC
sim('tunepid4')
hold
plot(Tid,y,'blue',Tid,u,'blue')
hold off

## Slide 41
0
5
10
15
20
25
30
35
40
-2
-1
0
1
2
3
4
ZN is almost unstable when the delay is increased from 1s to 1.5s.
SIMC does not change very much
SIMC
ZN
t=0: setpoint change, t=20: input disturbance
OUTPUT, y
INPUT, u

## Slide 42: Bode stability condition. Why may D-action help in some cases?
Some unstable processes, for example a double integrating process, may need D-action for stabilization. The reason is to add positive phase and therefore stabilize the system. Why does this help?
  Recall the Bode stability condition. It says that the loop gain should be less than 1 at the frequency where the phase shift around the loop -180 degrees.
  Another statement is that phase shift should be less than -180o at the frequency where the loop gain is 1.
  So for stability and robustness we want as little phase shift as possible (to improve the phase margin). The things that add negative phase shift are time delay (the worst), poles and RHP-zeros.
  LHP-zeros (D-action, (Td*s +1)) have the opposite (positive) effect on the phase, and this is why they may be added for stabilization in difficult cases, for example, an unstable process. Of course, zeros will also affect the loop gain, but at frequencies up to the break frequency, 1/Td, the positive effect on the phase is most important.
  So why don’t we always add D-action? One reason is that it increases the controller gain and therefore the input usage. However, the main reason is probably that it does not help very much in most cases and it makes the controller design more complicated (and easier to do mistakes).

## Slide 43: Closed-loop frequency response
10
-2
10
-1
10
0
10
1
10
-3
10
-2
10
-1
10
0
10
1
ZN
SIMC
w = logspace(-2,1,1000);
[mag1,phase]=bode(1/(1+L1),w);
[mag2,phase]=bode(1/(1+L2),w);
figure(1), loglog(w,mag1(:),'red',w,mag2(:),'blue',w,1,'-.')
axis([0.01,10,0.001,10])
SIMC: Ms=1.70
ZN: Ms = 2.93
Control: GOOD
BAD
NO EFFECT
e
|S|