## Slide 1: Input-output Controllability Analysis
Idea: Find out how well the process can be controlled - without having to design a specific controller
Note: Some processes are impossible to control
Reference: S. Skogestad, ``A procedure for SISO controllability analysis - with application to design of pH neutralization processes'',
Comp.Chem.Engng., 20, 373-386, 1996.
TexPoint fonts used in EMF.
Read the TexPoint manual before you delete this box.: AAAAA

## Slide 2
WANT TO QUANTIFY!

## Slide 3
WANT TO QUANTIFY!
Want slow and small response from disturbance (DV) to output (CV)
Want fast and large response from input (MV) to output (CV)
Opposite for feedback and feedforward

## Slide 4: Recall: Closed-loop frequency response
10
-2
10
-1
10
0
10
1
10
-3
10
-2
10
-1
10
0
10
1
ZN
SIMC
s=tf('s')
g = exp(-s)/s;
Kc=0.707; taui=3.33; c = Kc*(1+1/(taui*s)); L1 = g*c; % ZN
Kc=0.5; taui=8; c = Kc*(1+1/(taui*s)); L2 = g*c; % SIMC
w = logspace(-2,1,1000);
[mag1,phase]=bode(1/(1+L1),w);
[mag2,phase]=bode(1/(1+L2),w);
L0=1*exp(-s); [mag0,phase]=bode(L0,w); % Trick to make a line for 1
figure(1), loglog(w,mag1(:),'red',w,mag2(:),'blue',w,mag0(:),'black')
axis([0.01,10,0.001,10])
SIMC: Ms=1.70
ZN: Ms = 2.93
Control: GOOD
BAD
NO EFFECT
e
|S|

## Slide 5: Performance requirement for disturbances with feedback control
e=y-ys (opposite sign compared to previous slide, doesn’t matter here because we look at magnitude)
Recall: e = S Gd d . S=1/(1+L); L = GC
Performance requirement: Want |e(t)|<emax for worst-case disturbance: d(t)=dmax sin(ωt) (at any frequency)
So want |S Gd dmax| < emax (at all frequencies)
Or |1+L| emax > |Gd| dmax (at all frequencies)
At low frequency where |L| is large:
  set |1+L|
    A bit «optimistic» around |L|=1, but OK (see figure)
  Performance requirement becomes: |L| >|Gd| dmax/emax
  so at least we need ωc > ωd
  where ωc and ωd are defined as: |L(jωc)|=1, |Gd(jωd)|= emax/dmax
  This can also be used to tune the controller: τc < 1/ωd (approx)
Normally I assume the variables (and model (G, Gd)) have been scaled such that emax=1, dmax=1.
[mag3,phase]=bode((1+L2),w);
[mag4,phase]=bode(L2,w);
Plot |L| and |1+L1
figure(3), loglog(w,mag0(:),'black',w,mag3(:),'blue',w,mag4(:),'red’)
axis([0.01,10,0.01,100])
|L|
|1+L|
ωc=0.515
ωd=1 (assume emax=dmax=1)
|Gd|
QESTION: What about example on right?
Was SIMC-tuned with τc = 1 which happens to be = 1/ωd
– but resulting ωc=0.515 is NOT larger than ωd=1
So does not look promising for sinusoidal disturbance
Let’s check step response (which is not sinusoid)
gd= exp(-s)/s;
[mag5,phase]=bode(gd,w);
figure(4), loglog(w,mag0(:),'black',w,mag5(:),'blue')
axis([0.01,10,0.01,100])
ωd is the frequency up to which control is needed to get |e|<emax for disturbances (faster disturbances are averaged out by the process)
ωc is the frequency up to which feedback is effective (|L|>1)
This means we need ωc> ωd (Rule 1)

## Slide 6: Check: Step disturbance
G = Gd = e-s/s
SIMC PI-controller with τc=1
  Kc=0.5, τI = 8
s=tf('s');
g = exp(-s)/s; gd=g; % Input disturbance
Kc=0.5; taui=8; c = Kc*(1+1/(taui*s));
L2 = g*c; S2=1/(1+L2);
step(S2*gd,30)
As expected from frequency analysis we get peak
Would be OK with Gd = 0.5 e-s/s which would give ωd=0.5 < ωc=0.515

## Slide 7: Input usage
y = Gu + Gd d
To reject a disturbance d (and achieve y=0) we need for both feedforward and feedback
  u = - G-1 Gd d
Assume |d|=dmax and we must have |u|<umax
This means that we must require to avoid input saturation
  |G-1||Gd| dmax < umax
  or: |G| umax > |Gd| dmax (at all frequencies where we need control)
Normally I assume the variables )and model (G, Gd)) have been scaled such that emax=1, dmax=1, umax=1.
  The requirement to avoid input saturation then becomes:
  |G| > |Gd| (at all frequencies where we need control)

## Slide 8: Controllability rules (approximate)
Rule 1. Need ωc > ωd for disturbance rejection
Rule 2. Need ωc < 1/θ for robustness
Rule 3. Need ωc > p for stabilization (g(s)=1/(s-p))
Rule 4. Need |g||Δumax| > |gd||Δd| to avoid constraints
  ωd = frequency where |gd(jωd)| Δd /Δemax = 1 (|gd(jωd )|=1 in scaled units)
  ωc = 1/ τc (bandwidth frequency; frequency where |L| crosses 1 from above)
    Note: This τc is close to but not idential to the τc used in SIMC
  Θ = effective delay
  p = unstable pole
  Δemax = max allowed output error
  Δumax = max input change (because of input constraints)
  Δd = max expected disturbance
  Combined Rules 1 & 2: Must require ωd θ < 1
  Rule 1 is for typical case where |gd| is highest at low frequencies
    The more exact rule 1 is: Need |Sgd|Δd < Δemax at all frequencies. Note that |S|1/|L| at low frequencies
  Rule 4: Applies at frequencies where control is needed (up to ωd). In scaled units the rule simplifies to |g| > |gd|.
  Scaled units:
    Maximum allowed control error Δemax = 1.
    Maximum input change, Δumax = 1.
    Maximum expected disturbamce Δd =1
This situation is OK according to rules 1-3:
1/ θ
ω
ωd
p
ωc must be in this range

## Slide 9: Example: Controllability requirements for first-order process
Assume process (g) has effective delay θ
Assume maximum allowed output change (error) is Δymax
Consider response to disturbance, gd = kd/(τd s+1)
Time domain analysis
  For step Δd : Output reaches Δy = (kd θ /τd) Δd at time θ (approximately; see figure)
  If this is larger than acceptable (Δymax) then we are in trouble
  To be controllable, we must require
  (kd θ /τd) < Δemax/ Δd
Check with more general Rules in frequency domain:
  The controllability requirement is (Rule 1&2): ωd θ < 1
  where |gd(jωd)|=Δemax/Δd
  Asymptote for gd at ω > 1/τd: |gd|(jω)|= kd/τdω
  So ωd = kd/(τd Δemax/ Δd)
  And ωd θ < 1 gives the expected controllability requirement: (kd θ /τd) < Δemax/ Δd
In addition we must avoid input saturation. We have: Δy = gd Δd + g Δu
So to get Δy =0 without exceeding constraint Δumax, we must require (Rule 4)
  At all frequencies ω<ωd (where we need control) : |g(jw) Δumax | > |gd(jw) Δd|
  At steady state: |k Δumax | > |kd Δd|
  Initial response (approximately): |k /τ Δumax | > | kd/τd Δd|

## Slide 10: Controllability analysis
Use of controllability analysis
  To avoid spending time on impossible control problem
  To help design the process (e.g., size buffer tanks)
Also useful for tuning.
  τc = SIMC tuning parameter
  Must for acceptable controllability have:
    Note
      Tight control: τc,min = θ
      “Smooth” control: τc,max = 1/ωd
ωd is defined as frequency where |gd(jωd)|=Δemax/Δd

## Slide 11: If process is not controllable: Need to change the design
For example, dampen disturbance by adding buffer tank:
Level control unimportant,
but need good mixing
Level control is NOT tight
-> level varies
Integral action is not recommended for averaging level control

## Slide 12: Scaled model
In all problems below, we assume that models have beed scaled such that
    Δemax=1
    Δumax=1
    Δd =1
    Define ωd as frequency where |Gd(jωd)|=1.
      For first-order disturbance model (scaled units): ωd = kd/τd

## Slide 13: Problem 1
SCALED MODEL
NOT OK with constraints. (Rule 4 at steady state)

## Slide 14: Problem 2
SCALED MODEL
NOT OK with constraints. (Rule 4 for ω from about 0.25 to 2)

## Slide 15: Problem 3
-
SCALED MODEL
OK.
Rule 1 (performance) is Ok since effective delay in G is zero,
Rule 4 (constraints) is OK since |G|>|Gd| up to frequency ωd where |Gd|=1
(Note: Gd has an effective delay of 0.8+0.1=0.9 (half rule), but the delay in Gd does not matter)

## Slide 16: Problem 4
SCALED MODEL
N
Disturbance: Approximate as first-order with delay with kd=4, taud=3.5 4/3.5 = 1.14
NOT OK with PI (Rule 1) since effective process delay is θ=10/2+1=6 so ωd θ =6.9 > 1
BUT OK with PID (Rule 1) since effective process delay is θ=0.5 so ωd θ =0.6 < 1
No problem with constraints, |G|>|Gd|
Disturbances. When does y reach 1 (ωd)?
What is effective delay?

## Slide 17: Problem 4
SCALED MODEL
Check simulation PID:
%PID (w/o D-action on setpoint)
g = 200/((20*s+1)*(10*s+1)*(s+1))
gd = 4/((3*s+1)*(s+1)^3)
Kc=(1/200)*20/1,taui=20,taud=10.5
y
u
d=1
OK!
Control error e=y-ys alwys
less that emax=1
ys=1

## Slide 18: Problem 5
-
SCALED MODEL
NOT OK (Rule 1/2) since effective process delay is at least 5.1 (both PI and PID),
so ωd θ = 2*5.1=10.2 > 1
|Gd|
ωd =kd/τd=2
YOU CAN TRY FOREVER TO DESIGN A CONTROLLER WHICH IS OK BUT IT’S IMPOSSIBLE

## Slide 19: Problem 6
pH-Neutralization.
Want product with pH=7+-1
Define c = (cH+ - cOH- ), want |c|<10-6
u = qbase (cOH-=10mol/l, pH=15)
d = qacid (cH+ =10mol/l, pH=-1,)
Using tanks in series,
Acid and base in tank 1.
Scaled model: kd = 2.5e6
Each tank: τ = 1000s
Control: θ = 10s (meas. delay for pH)
Problem: How many tanks?
ω [rad/s]
SCALED MODEL
n=2
n=3
n=1
|Gd|
Reference for more applications of controllability analysis: Chapter 5 in book by Skogestad and Postlethwaite (2005)
1/θ= 0.1

## Slide 20: Control system
3 tanks: Neutralization (base addition) only in tank 1 gives large effective delay (>> 10s) because of tank dynamics in g(s)
Suggested solution is to add (a little) base also in the other tanks:
pH 5
pH 2

## Slide 21
10
-3
10
-2
10
-1
10
0
10
1
10
-2
10
-1
10
0
10
1
10
2
10
3
s=tf('s')
g = 500/((50*s+1)*(10*s+1))
gd = 9/(10*s+1)
w = logspace(-3,1,1000);
[mag,phase]=bode(g,w);
[magd,phased]=bode(gd,w);
loglog(w,mag(:),'blue',w,magd(:),'red',w,1,'black'), grid on
SCALED MODEL
PROBLEM 7, g = 500/((50*s+1)*(10*s+1))
ωd=0.9
|G|
|Gd|
gd = 9/(10*s+1)
PI- control: θeff = 5 (from half rule):
ωd θ =kd θ /τd = 9*5/10=4.5 > 1
NOT CONTROLLABLE WITH PI!
PID-control : θeff = 0. Controllable!

## Slide 22
CHECK CONTROLLABILITY ANALYSIS WITH SIMULATIONS

## Slide 23: Problem 7: PI control not acceptable*
0
50
100
150
200
250
300
350
400
450
500
0
1
2
3
4
5
6
± 1
y
s=tf('s')
g = 500/((50*s+1)*(10*s+1))
gd = 9/(10*s+1)
% SIMC-PI with tauc=theta=5
Kc=(1/500)*(55/(5+5)); taui=55; taud=0;
SCALED MODEL
*As expected since need ωc > ωd= 0.9, but can only achieve ωc<1/θ = 1/5 = 0.2
Ooops! e = y-ys>1
ys=1

## Slide 24: Problem 7: PID control acceptable: e and u are within ±1
0
50
100
150
200
250
300
350
400
450
500
-1
-0.5
0
0.5
1
1.5
2
y
u
g = 500/((50*s+1)*(10*s+1))
gd = 9/(10*s+1)
%SIMC-PID (cascade form) with tauc=1/wd=1:
Kc=(1/500)*(50/(1+0)); taui=50; taud=10;
SCALED MODEL

## Slide 25: Exam.
Tuesday 10 Dec. 2024. 9-13 (Physical)
One sheet with own notes (both sides OK; printed OK)
Simple calculator
Note: Remember to state clearly all assumptions you make.
General: Look through the whole exam before you start, read the questions carefully!
Q&A session: Thursday 05 Dec. 14-16, (H1)
(please send questions before by email: sigurd.skogestad@ntnu.no)