## Slide 1: Modelling and linearization
Seborg: Chapter 2 + 3.4 (lin.)
Skogestad: Ch. 11
TexPoint fonts used in EMF.
Read the TexPoint manual before you delete this box.: AAAAAAAAA

## Slide 2
Reference group process control:
Need 4 students (volunteers)

## Slide 3
Chapter 2
Mathematical Modeling of Chemical Processes
Mathematical Model (Eykhoff, 1974)
“a representation of the essential aspects of an existing system (or a system to be constructed) which represents knowledge of that system in a usable form”
“Everything should be made as simple as possible, but no simpler.” (A. Einstein)
“All models are wrong, but some are useful.”
TexPoint fonts used in EMF.
Read the TexPoint manual before you delete this box.: AAAAAAAAAAA

## Slide 4
General Modeling Principles
The model equations are at best an approximation to the real process.
Modeling inherently involves compromise between
  Model accuracy and complexity
  and: Cost and effort required to develop model
Process modeling is both an art and a science.
  Creativity (art) is required to make simplifying assumptions that result in an appropriate model.
Dynamic models of chemical processes consist of:
  ordinary differential equations (ODE)
  and/or partial differential equations (PDE)
  plus related algebraic equations (AE).
Chapter 2

## Slide 5
Balance principle (“Conservation laws”): Applies to mass, mols of molecules, energy and momentum
This gives what is known as “first principles model” or “physical model” or “nonlinear state space model”
For reactions [mol]
=0 for mass and energy
=0 for mass and energy
System boundary
(= control volume)

## Slide 6
General process system
Q [J/s]
m [kg], V[m3]
nA [mol A]
E [J], T[K]
win [kg/s]
FA,in [mol A/s]
Ein [J/s], Tin [K]
wout [kg/s]
FA,out [mol A/s]
Eout [J/s], Tout [K]
W [J/s]
Formulate balances for mass (m), energy (E) and component mass (nA)
Mass (m) and energy (E) are conserved quantities (no generation or loss)
Chemical components (A) may be generated by chemical reactions. GA [mol A/s]

## Slide 7
Mass balance:
Chapter 2

## Slide 8
Molar component balance:
Chapter 2
GA [mol A/s]

## Slide 9
Energy balance (=First Law of Thermodynamics)
The total energy of a thermodynamic system, E, is the sum of its internal energy, kinetic energy, and potential energy: E = U + KE + PE + other (surface energy, etc)
Also many forms of work: W = Ws + pV-work + other (electric, etc.)
where pV-work = Pinqin – poutqout – pex dV/dt
1) Neglect KE and PE. 2) Neglect «other» work. 3) Introduce Hin=Uin + pinqin. etc. Get:
Energy is a conserved quantity (no generation or loss).
Heat of reaction is included in E with common reference state (usually elements)
p [N/m2]
pex [N/m2]

## Slide 10
Waterfall: (1) potential energy -> (2) kinetic energy -> (3) thermal energy
Thermal energy is included in internal energy (U).
Can usually neglect kinetic and potential energy in energy balance
Proof: Energy balance (for m=1kg water): PE1 = KE2 = U3
mgh1 = ½ mv22 = mcPT3 [J]
where
g = 10 m/s2
cP = 1 kcal/kg,K = 4184 J/kg,K

## Slide 11: Which control volume and which balance?

## Slide 12: Dot notation
In the control field (EE), a dot means derivative (of quantity inside boundary)
But in other fields (ME) it may mean a transfer rate (through boundary)
For this reason I usually avoid dot-notation

## Slide 13: Dynamic modeling. Examples
You should do many examples!
See my book: CHEMICAL AND ENERGY PROCESS ENGINEERING, CRC Press (Taylor & Francis Group), 2009, Chapter 11..
Chapter 11 on dynamics available here:
    http://folk.ntnu.no/users/skoge/prosessregulering/course-material/
Example 1. Mixing tank (CSTR)
Q
m, V
nA, cA
T
w
q
cA
T
wF [kg/s]
qF [m3/s]
cAF [mol/m3]
TF [K]
8
Task:
Formulate mass, component and energy balances
to find expressions for dV/dt, dcA/dT, dT/dt
Assume:
Perfect mixing
No reaction
Constant density
Constant heat capacity
Single phase (liquid)
Do NOT assume constant volume V

## Slide 14: Example 2. Buffer tank on gas pipeline (Example 11.10)
Task:
Find residence time, ¿r
Find time constant ¿ for dynamic response
Hint: Find expression for dp/dt and rearrange to standard form to find time
constant (gives dynamics for effect of changes in pin on p, Fin, etc.)
Note: Only one mass (mole) balance, so this is a first-order system
Assume:
T constant; Ideal gas, pV = nRT
Linear valves: Fin = c (pin-p), Fout= c(p-pout)
Data at steady state:
pin=10.1 bar, p=10 bar, pout=9.9 bar, V = 10m3, Fin=Fout = 100 mol/s, T=300K
Gas dynamics
are very fast!

## Slide 15: Summary: Dynamic modeling
Use of the “balance principles” (resulting in differential equations) combined with other equations for equilibrium, heat transfer etc. (resulting in algebraic equations), gives in a “nonlinear state space model” on the general form:
The states x1, x2… are usually the balanced quantities (mass, energy, molar holdup). It is possible to redefine the states, for example, to replace x1=H (energy) by x1=T (temperature), but this requires work (see example), so we often don’t do it.

## Slide 16: Linearization = Tangent approximation = Taylor series expansion
x
x*
x=x*+¢x
f(x)
f(x*)
Tangent approximation:
f(x)=f(x*+¢x) ¼ f(x*) + C¢¢x
where C = slope = (f/x)*
error
Negligible error for small deviations from point * (small ¢x)
x |  | 
0 |  | 
0.5 |  | 
1 | 1 | 
2 |  | 

## Slide 17: Linearization (Linear model)
What is a linear system?
  1. Gain k = Δy/Δu is constant, independent of magnitude of Δu.
  2. Satisfies the superposition principle: that is, the total response is the sum of individual responses. Let
    f(u1)=y1(t) y1 = change in temperature when change u1 (put on heater)
    f(u2)=y2(t) y2 = change in temperature when change u2 (open window)
    Then
    f(u1+u2) = y1(t) + y2(t) = y(t) (y=change in y with both at same time)
Why linearize?
  Much simpler mathematics (transfer functions)
  All real systems behave linearly for small deviations from steady state (using control!)
How linearize?
  1. Linearize nonlinear dynamic model (e.g., obtained from balance equations):
  dx/dt = f(x,u)
  to get a linear «state space» model in deviation variables (Δx(t) = x(t) – x*, etc.):
  dΔx/dt = A Δx + B Δu
  where A = (f/x)* and B = (f/u)* are constants (matrices in the general case).

## Slide 18: Linearization of dynamic model. Proof of «How»
But some things become simpler for normal case when we linearize around steady state:
Special case (slight extension) when we linearize around a steady state (f*=0):
Nonlinear model: V(t) dx/dt = f(x,u) (Here V(t) can be any function or variable)
Linear model becomes: V* dΔx/dt = Δf
Proof (assume that * is a steady state so f*=0).
Rewrite nonlinear model as: dx/dt = f/V
Linearize using brown box: dΔx/dt = (1/V*) Δf – (f*/V*2) ΔV = (1/V*) Δf
QED
Conclusion: Set LHS=RHS (f* drops out!):

## Slide 19: This is how I do it

## Slide 20: Example 1: Outflow from tank (bath-tub with no plug)
Note: Time constant for flow response (liquids)
  Twice residence time for turbulent outflow
  Equal to residence time for laminar outflow
  Gas dynamics are much faster!
Nonlinear static model

## Slide 21
Notes
1. Bilinear term on RHS: Δ(xu) = x* Δu + y* Δu
2. Linearize LHS:
Note: When you have a nonlinear model on the form V(t)dT/dt = f,
And you linearize a steady state, the linear version simply becomes V* dΔT/dt = Δf, that is, you can use V* on the left hand side.
Proof : See bottom of proof slide (in red)
Example 2: CSTR
Start here part 3 - lecture 4 (10 sep 2024)

## Slide 22
Example 2: Linearization CSTR

## Slide 24: Summary linearization
Note: If you also have static model equations then I recommend to start by linearizing these

## Slide 25: Linearize static model (for algebaic equations)
    Static model
    y=f(x,u)
    Consider small deviations in u from nominal point where y*=f(x*,u*)
    Linear model in deviation variables (Δx(t) = x(t) – x*, etc.):
    Δy = C Δx + D Δu
    where
    C= (f/x)*
    D= (f/u)*
    are constants (matrices in the general case)

## Slide 26: Example 3 linearization: Flash
Flash tank with two components (zF,y,x: mole fraction light component)
VLE: Assume constant relative volatility ®=21:
Model assumptions: Well mixed, neglect vapor mass
p and M constant (using Q and L)
u = V
d = F, zF
y = y (output)
Nominal data: F*=1 kmol/min, z*F=0.5, y*=0.84, M = 1kmol
Task: 1. Derive dynamic model + 2. Find nominal steady-state + 3. Linearize to find model (in deviation variables)
L, x
V, y
F, zF
M
Q

## Slide 27: Solution
x
y
Slope=c=0.84
VLE
0=
(I usually start by linearizing the static equations)

## Slide 29
% Using symbolic toolbox in Matlab
syms y x
f=21 - (y/x) / ((1-y)/(1-x)) % definition relative volatility=21
y=solve(f,y)
fplot(y,[0 1])
dydx(x)=diff(y,x)
dydx(0.2)
eval(ans)
Result:
f =21 - (y*(x - 1))/(x*(y - 1))
y =(21*x)/(20*x + 1)
dydx(x) =21/(20*x + 1) - (420*x)/(20*x + 1)^2
ans =21/25
ans =0.8400

## Slide 31
Solution

## Slide 34: Minimum realization
Unobservable states x are unintersting for us as they have no effect on the outputs (y)
Uncontrollable states x cannot be effected by our inputs (u)
Model from u to y: Eliminate unobsevable and uncontrollable* states to get model with fewest number of states («minimal realization»). Saves computation time.
Corresponds to cancelling identical poles and zeros, (s+a)/(s+a), in transfer function
  Note how much simpler it becomes with transfer functions (Laplace)
*But initial value of uncontrollable states will affect outputs, at least temporarily