## Slide 1: PID Tuning using the SIMC rules Sigurd Skogestad NTNU, Trondheim, Norway

## Slide 2: Need a model for tuning
Model: Dynamic effect of change in input u (MV) on output y (CV)
First-order + delay model for PI-control
Second-order model for PID-control
  Recommend: Use second-order model (PID control) only if ¿2>µ
MODEL

## Slide 3: 1. Step response experiment
Make step change in one u (MV) at a time
Record the output (s) y (CV)
MODEL, Approach 1: From data

## Slide 4: Step response first-order process
STEP IN INPUT u
RESULTING OUTPUT y
: Delay - Time where output does not change
1: Time constant - Additional time to reach
63% of final change
k =  y(∞)/ u : Steady-state gain
Δy(∞)
Δu
MODEL, Approach 1
If the output y keeps ramping (with little sign of flattening) after about 4 times the delay θ
then you can use an integrating process model (so you don’t need τ1).

## Slide 5: Step response integrating process
Δy
Δt
MODEL, Approach 1
Slope k’ = «integrating process gain»

## Slide 6: 2. Model reduction of more complicated model
Start with complicated stable model on the form
Want to get a simplified model on the form
Most important parameter is the “effective” delay 
Use second-order model only if ¿2>µ
MODEL, Approach 2: From more complicated model

## Slide 7
Details:
MODEL, Approach 2

## Slide 8: Example 1
Half rule
MODEL, Approach 2

## Slide 9
s=tf('s')
g=(-0.1*s+1)/[(5*s+1)*(3*s+1)*(0.5*s+1)]
g1 = exp(-2.1*s)/(6.5*s+1)
g2 = exp(-0.35*s)/[(5*s+1)*(3.25*s+1)]
step(g,g1,g2)
0
5
10
15
20
25
30
35
40
-0.2
0
0.2
0.4
0.6
0.8
1
Step Response
Time (seconds)
Amplitude
0
0.5
1
1.5
2
2.5
3
3.5
4
4.5
5
-0.05
0
0.05
0.1
0.15
0.2
0.25
0.3
0.35
0.4
Step Response
Time (seconds)
Amplitude
Example 2
Original (third-order with inverse response)
First-order approx. using half rule
Second-order approx. using half rule

## Slide 10
half rule
3
MODEL, Approach 2
Comment: The subtraction of T0=0.08 from the effective delay follows from the approximation (0.08s+1)/(0.2s+1) (rule T3).
Alternatively, we could have used the approximation (0.08s+1)/(0.05s+1) (rule T1b) which would reduce the effective delay by 0.05 (instead of 0.08). In any case, it only has a small effect om the effective delay, so it does not matter much for the final result.

## Slide 11
half rule
3
MODEL, Approach 2

## Slide 12
g0: Original complicated system
(with 2 zeros and 8 poles)
g2: 2nd order with delay (half rule, θ=0.77)
g1: 1st order with delay (half rule, θ=1.47)
Example 3.
MODEL, Approach 2

## Slide 13: Example 4. Integrating process
Example. g0 = 5/(s*(3*s+1)),
g = 5*exp(-1.5*s)/s,
step(g,g0,10)
Doesn’t look so good
But it’s OK

## Slide 14: Approximation of LHP-zeros
τc = desired closed-loop time constant
MODEL, Approach 2
Normally, we should approximate T0 by a “close-by” 0 .
BUT: The goal is to use the model for control purposes, so we should keep (i.e., not approximate) the  which is closest to the desired c.
In Example E3, we have two possible values for 0 , namely 20 and 1. Since T0=15, it seems clear that we should select the closest 0 = 20 and use rule T2.
But what if T0=2, maybe selecting 0 = 1 is better (and using rule T1)?
No, this is not clear. Since c =θ is between 0.05 (PID) and 0.15 (PI), we may want to keep  =1 which is closest to c ,that is, also in this case select 0 = 20 (and use rule T2)
This may seem surprising, but. in any case, it turns out that it will not matter very much for the PI/PID-tunings for this example (try!), because k/tau1 (and thus Kc) will not change much and because tauI = min(tau,4(tauc+theta)).
Of course, if T0 gets very close to 1, then we should select 0 = 1.
Generally, the LHP-zeros approximation rules results in acceptable (robust) PI/PID-settings, but not necessarily the “optimal” settings.
See: Exam 2022, Problem 1 and Problem 5d
g0
g2
g1
PID-controller (from 2nd order model) will give performance improvement because τ2 > θ
(you are not expected to remember this)

## Slide 15: Step response (without control)
g0 = 2*(15*s+1)/((20*s+1)*(s+1)*(0.1*s+1)^2)
g1=1.5*exp(-0.15*s)/(1.05*s+1)
g2=1.5*exp(-0.05*s)/((s+1)*(0.15*s+1))
step(g0,g1,g2,1)
Note: It’s the initial
response that matters
for feedback control
(time from 0 to about 5*tauc)
g1
g0, g2
g0
g1, g2

## Slide 16
Alternative: Obtain model from data numerically. Here: use procest (matlab)- but procest seems not to be reliable when I study other cases
% We generate some artifical data from a high-order model
s=tf('s')
G = 3*(1-0.1*s)/((10*s+1)*(3*s+1)*((s+1)^3))
Ts=1; % sampling time 1 s (Comment: This may be too long; could make shorter to fit only initial response)
t = Ts*[0:109]';
u = [zeros(10,1); ones(100,1)]; % Step response
y = lsim(G,u,t);
% Now fit the data to a second-order plus delay model using Matlab
data=iddata(y,u,Ts); %
type=('P2D') % P2D = 2nd order model + delay
sys = procest(data,type)
% Compare the two models
k=sys.Kp; tau1=sys.Tp1; tau2=sys.Tp2; Td=sys.Td;
Gfit = k*exp(-Td*s)/((tau1*s+1)*(tau2*s+1))
step(G,Gfit,'--')
figure(2),step(G,Gfit,'--',10)
OUTPUT FROM procest (MATLAB):
Process model with transfer function:
Kp
G(s) = ----------------- * exp(-Td*s)
(1+Tp1*s)(1+Tp2*s)
Kp = 2.9986
Tp1 = 9.6838
Tp2 = 3.9211,
Td = 2.478
Half rule: Gives similar result
Half rule:
Kp = 3
Tp1 = 10
Tp2=3+0.5=3.5
Td=0.5+2*1+0.1=2.6

## Slide 17
Time domain (“ideal” PID)
Laplace domain (“ideal”/”parallel” form)
For our purposes. Simpler with cascade/series form
Usually τD=0. Then the two forms are identical.
Only two parameters left (Kc and τI)
How difficult can it be to tune???
  Surprisingly difficult without systematic approach!
PID controller
e

## Slide 18: Tuning of PID controllers
SIMC tuning rules (“Skogestad IMC”)(*)
Main message: Can usually do much better by taking a systematic approach
Key: Look at initial part of step response
  Initial slope: k’ = k/1
One tuning rule!
c: desired closed-loop response time (tuning parameter)
For robustness select: c ≥ 
Let’s start with the CONCLUSION
Reference: S. Skogestad, “Simple analytic rules for model reduction and PID controller design”, J.Proc.Control, Vol. 13, 291-309, 2003
(Also reprinted in MIC)
(*) “Probably the best simple PID tuning rules in the world”
For cascade-form PID controller:

## Slide 19
Derivation of SIMC-PID tuning rules
PI-controller (based on first-order model)
For second-order model add D-action.
  For our purposes, simplest with the “series” (cascade) PID-form:

## Slide 20
Basis: Direct synthesis (IMC)
Closed-loop response to setpoint change
Idea: Specify desired response:
and from this get the controller. ……. Algebra:

## Slide 21
SIMC-tunings
NOTE: Setting the steady-state gain = 1 in T will result in integral action in the controller!
Time delay is not really desired
but it cannot be avoided
Note: Process g has time delay (θ)

## Slide 22: IMC Tuning = Direct Synthesis
Algebra:
Surprisingly, this PID-controller is generally better, or at least more robust with respect to changes in the time delay θ, than the Smith Predictor controller from which it was derived. We are lucky .
Reference: Chriss Grimholt and Sigurd Skogestad. ''Should we forget the Smith Predictor?'' (2018) In 3rd IFAC conference on Advances in PID control, Ghent, Belgium, 9-11 May 2018. In IFAC papers Online (2018) .
IMC-tuning is the same as “Lambda-tuning”: c is sometimes called λ

## Slide 23: Example step setpoint response (with choice τc=θ =2)
s=tf(‘s’);
k=1; tau=10; theta=2;
g = k*exp(-theta*s)/(tau*s+1);
tauc=theta;
Kc=(1/k)*(tau/(tauc+theta)); % Kc=2.5
taui=tau;
c = Kc*(1+ 1/(taui*s));
T = g*c/(1+g*c);
Tideal = exp(-theta*s)/(tauc*s+1);
step(T,Tideal,20)
y (PI)
Red: «ideal» = «originally desired» (with Smith Predictor)
PI: Overshoot (y=1.04) is from approximation exp(-θs) = 1 - θs

## Slide 24: Input usage for setpoint response
%Input usage
figure(2);
KS = c/(1+g*c);
KSideal = (1/k)*(tau*s+1)/(tauc*s+1);
step(KS,KSideal,20);
axis([0 20 0 5])
u (PI)
Red: «ideal» (with Smith Predictor)
Input u «overshoots» because we are are «speeding up» the response from τ=10 to τc=2.
Input starts from 0

## Slide 25
Integral time
Found: Integral time = dominant time constant (I = 1)
Gives P-controller for integrating process (I = ∞)
  This works well for setpoint changes
  But: I needs to be modified (reduced) for integrating disturbances
  Example. “Almost-integrating process” with disturbance at input:
  G(s) = e-s/(30s+1)
    Original integral time I = 30 gives poor disturbance response
    Try reducing it!
g
c
d
y
u
SIMC-tunings

## Slide 26: Effect of decreasing Integral Time
I = 1
Reduce I to this value:
I = 4 (c+) = 8 
Setpoint change at t=0
Input disturbance at t=20
SIMC modification:
Decrease integral time to improve disturbance rejection for slow processes (with large τ)!

## Slide 27: Integral time
Want to reduce the integral time for “integrating” processes
But to avoid “slow oscillations” (not caused by the delay θ) we must require k’KcτI≥4, which with the SIMC-rule for Kc gives:
Proof: Need k’KcτI≥4 to avoid slow oscillations (from last week):
SIMC-tunings

## Slide 28: Conclusion: SIMC-PID Tuning Rules
One tuning parameter: c
SIMC-tunings

## Slide 29
Some special cases
One tuning parameter: c
SIMC-tunings
(1)(*) Note that we get pure I-controller for static process with delay.

## Slide 30: Selection of tuning parameter c
Two main cases
TIGHT CONTROL (τc small): Want “fastest possible control” subject to having good robustness
    Want tight control of active constraints (“squeeze and shift”)
    Select τc = θ (effective delay)
SMOOTH CONTROL (τc large): Want “slowest possible control” subject to acceptable disturbance rejection
    Prefer smooth control if fast control is not required
SIMC-tunings

## Slide 31
Typical closed-loop SIMC responses with the choice c=
TIGHT CONTROL

## Slide 32
TIGHT CONTROL
(can increase process gain k by factor 3 before we get instability from «overreaction»)

## Slide 33
Example 2. Compare PI and PID
s=tf('s')
g=(-0.3*s+1)*(0.08*s+1)/((2*s+1)*(s+1)*(0.4*s+1)*(0.2*s+1)*(0.05*s+1)^3)
k=1;
tau1=2.5, tau2=0, theta=1.47, tauc=theta % 1st order
%tau1=2, tau2=1.2, theta=0.77, tauc=theta % 2nd order
Kc=(1/k)*tau1/(tauc+theta) % Kc. PI: 0.85 PID: 1.30
taui=min(tau1,4*(tauc+theta)) % taui. PI: 2.50 PID: 2
taud=tau2; % taud. PI: 0 PID: 1.2
cpi=Kc*(1+1/(taui*s));
cd=(taud*s+1)/(0.1*taud*s+1);
cpid=cpi*cd;
L = cpid*g
S=inv(1+L)
%setpoint response
Ty=g*cpi*S, Ty=minreal(Ty); % without D-action on setpoint
Tuy=cpi*S, Tuy=minreal(Tuy); % without D-action on setpoint
%Input disturbance
gd=g;
Td=gd*S; Td=minreal(Td);
Tud=-gd*cpid*S; Tud=minreal(Tud);
Typi=Ty; Tdpi=Td; Tuypi=Tuy; Tudpi=Tud;
%Typid=Ty; Tdpid=Td; Tuypid=Tuy; Tudpid=Tud;
figure(1),step(Typi,'blue',Typid,'blue--',Tuypi,'red',Tuypid,'red--',15)
figure(2),step(Tdpi,'blue',Tdpid,'blue--',Tudpi,'red',Tudpid,'red--',15)
TIGHT CONTROL
Note: tau2=1.2 > theta=0.77
so 2nd order and PID should give improvement compared to PI

## Slide 34
Input u
Input u
STEP SETPOINT CHANGE (ys)
(note: without D-action on setpoint,
so u jumps initially to Kc also for PID)
STEP INPUT DISTURBANCE (gd=g)
PI
PID
Output y
Output y
Conclusion:
PID is quite a lot better.
(expected since tau2=1.2
> theta=0.77)
Example 2.
PI
PID
PID
PI
PI
PID

## Slide 35
Comments
1. Derivative action (PID) can help a little to speed up response for a process with time delay (e.g. use D = θ/3), but we then need to reduce C (i.e., increase Kc) to get the performance benefit (e.g., reduce C from θ to θ/2).
We did not do this in the above simulation, so this is why the benefit of D-action is small.
2. Use derivative action (PID) for unstable processes, for example, a double integrating process (not so common in process control).
SIMC-tunings
SHOULD WE ADD DERIVATIVE ACTION TO COUNTERACT TIME DELAY?
NO

## Slide 36
Too complicated

## Slide 37: When do we need «tight control»? For hard constraints where backoff is costly
«SQEEZE and SHIFT» RULE
Original
tuning
Improved
tuning
Optimized
operation
Setpoint
Squeeze
variance
Shift setpoint to reduce backoff
time
New backoff

## Slide 38: Tuning for smooth control
SMOOTH CONTROL
Tuning parameter: c = desired closed-loop response time
Selecting c= if we need “tight control” of y.
Other cases: “Smooth control” of y is sufficient, so select c >  for
  slower control
  smoother input usage
    less disturbing effect on rest of the plant
  less sensitivity to measurement noise
  better robustness
Question: Given that we require some disturbance rejection.
  What is the largest possible value for c ?
  ANSWER: c,max =1/ωd (where ωd is defined as the frequence where |gd(jωd)| = ymax/dmax )
Proof: S. Skogestad, ``Tuning for smooth PID control with acceptable disturbance rejection'', Ind.Eng.Chem.Res, 45 (23), 7817-7822 (2006).

## Slide 39: Level control (integrating process)
Level control often causes problems
Typical story:
  Level loop starts oscillating
  Operator detunes by decreasing controller gain
  Level loop oscillates even more
  ......
???
Explanation: Level is by itself unstable and requires control.
LEVEL CONTROL

## Slide 40: Level control (integrating process): Can have both fast and slow oscillations with PI-control
Fast oscillations (Kc too high): P < π τI
  Caused by (effective) time delay
Slow oscillations (Kc too low): P > π τI
  Caused by integral action in controller
  Avoid slow oscillations:
LEVEL CONTROL
P=period of oscillations = 2π/ω

## Slide 41: How avoid slowly oscillating levels?
LEVEL CONTROL
0.1 ¼ 1/2

## Slide 42: Case study oscillating level
We were called upon to solve a problem with oscillations in a distillation column
Closer analysis: Problem was oscillating reboiler level in upstream column
Use of Sigurd’s rule solved the problem
LEVEL CONTROL

## Slide 43
LEVEL CONTROL

## Slide 44
SIMC-rule with measurement dynamics
Rule: Combine the measurement dynamics gm(s) and the process model g(s) and apply the SIMC-rules on ggm. This applies both to the model approximation (half rule) to get a 1st or 2nd model and to the PI- or PID-tuning, including the choice of τc.
Proof: handwritten note

## Slide 45: Tuning of PID controllers
SIMC tuning rules (“Skogestad IMC”)(*)
Main message: Can usually do much better by taking a systematic approach
Key: Look at initial part of step response
  Initial slope: k’ = k/1
One tuning rule!
c: desired closed-loop response time (tuning parameter)
For robustness select: c ≥ 
CONCLUSION
Reference: S. Skogestad, “Simple analytic rules for model reduction and PID controller design”, J.Proc.Control, Vol. 13, 291-309, 2003
(Also reprinted in MIC)
(*) “Probably the best simple PID tuning rules in the world”
For cascade-form PID controller:
Note: The delay θ includes any measurement delay

## Slide 46: For later
After you learn about robustness and Ziegler-Nichols

## Slide 47: Choice of SIMC-tuning parameter c. 1. Trade-off between robustness (Ms) and performance (J=IAE)
Conclusion: c= gives a good trade-off
Ms = Peak of |S(jω)| = 1/(smallest distance to (-1)-point). Want less than 1.7

## Slide 48: SIMC: GM and DM increase linearly with τc
Ms
GM
PM
c /
c /
DM=
D / =
PM/ωc
3
1
2
1.6
1
60o
1/Ms
Choice of tuning SIMC-parameter c. 2. Relationship between c and robustness (Ms, GM, PM, DM)
Conclusion: c/ gives a acceptable robustness (Ms=1.6, PM=60o, GM=3, DM=2)