## Slide 1
DEFINITION LAPLACE TRANSFORM

## Slide 2
Table 3.1 Laplace Transforms for Various Time-Domain Functions
f(t) F(s)
1
0
AREA=1
1
0
Rule exponential (e-at): Opposite sign in Laplace

## Slide 3
Table 3.1 Laplace Transforms for Various Time-Domain Functions
f(t) F(s)
AppndixA
Note: This is step response of first-order system

## Slide 4
Table 3.1 Laplace Transforms for Various Time-Domain
Functionsa (continued)
f(t) F(s)
Appendix A
Alternative forms of step
response for 2nd order system
Transfer function for time delay µ is e-µs
Laplace of derivatives

## Slide 5
Laplace Transform
Examples
Usually f(t) is in deviation variables so f(t=0) = 0
Definition*:
Appendix A
*Will often misuse notation and write f(s) instead of F(s)
a/s = Laplace of step a
2.
5.

## Slide 6
Most important property for us.
Laplace of derivative.
Differentiation: replaced by multiplication with s
Integration: replaced by multiplication with 1/s
Proof:
Set v=e-st and du=df and use integration by parts
Note: d(uv) = u dv + v du

## Slide 7
Other properties of Laplace transform:
A. Final value theorem
“steady-state value”
Example:
Appendix A
Comment (relevant to step responses):
If Y(s) = g(s)/s then y(t=∞)=g(0)

## Slide 8
B. Initial value theorem
by initial value theorem
(multiply Y(s) by s and set s=1)
by final value theorem
(multiply Y(s) by s and set s=0)
Example
AppendixA
C. Initial slope property

## Slide 9
Comment on notation
Appendix A
 | Sigurd | Book (Seborg)
Time signal | y(t) | y(t)
Steady-state value | y* | y
Deviation | Δy = y – y* | y’ = y - y
Laplace of Δy(t) | y(s) | Y(s)

## Slide 10
(e.g., deviation variables!)

## Slide 11: Partial fraction expansion of f(s)
Consider a Laplace transform
f(s) =n(s)/d(s)
Assume the order of the polynomial d(s) is higher or equal to order of polynomial n(s).
We first factorize d(s) as a product of terms, for example,
d(s)= k(τ1*s+1)(τ2*s+1)...
where τi are the time constants
  Note that s=-1/τi are the roots in the polynomial d(s)=0.
We then write the “partial fraction expansion” of f(s):
f(s) = α0 + α1/(τ1*s+1) + α2/(τ2*s+1) + ....
The constants (α's) may be determined in many ways.
One simple method is to multiply by both sides by (τ1*s+1) and then set s=-1/τ1. This gives α1. Then we find α2, etc.
α0 may be found by letting s=∞.
  Note that α0=0 except for systems with the same number as zeros as poles.
Example. f(s) = (-0.25s+1)/(10s-1)
This a bit unusual since the system is unstable (note the negative sign in d(s)), but it does not matter. We write
f(s) = (-0.25s+1)/(10s-1) = α0 + α1/(10s-1) (*)
To determine α1: Multiply on both sides of (*) by 10s-1 and set s=0.1: (-0.25s+1) = -0.025+1 = 0.975 = α1
To determine α0: Let s=∞ on both sides of (*): -0.25/10 = α0 -> α0=-0.025
Conclusion: f(s) = -0.025 + 0.975/(10s-1)

## Slide 13: Transfer function of first-order plus delay (FOD) process
Dynamic model in time domain:
Laplace transform:
Rearrange : where
- Transfer function!
  Independent of what u(t) is (step, sinus, etc…)
  To obtain y(s): Just multiply u(s) with G(s)
FOD process
u
y

## Slide 14: Examples transfer functions
First-order with delay
First-order (concentration in tank)
Integrating
Closed-loop
PID
Higher order
See lectures

## Slide 15
Use of Laplace Transforms in control
Standard notation in dynamics and control for linear
systems (shorthand notation)
  Independent variable: Change from t (time) to s (complex variable; inverse time)
  Just a mathematical change in variables: Like going from x to y=log(x)
2. Converts differential equations to algebraic operations
3. Advantageous for block diagram analysis.
Transfer function, G(s):
Appendix A
G(s)
u(s)
y(s) = G(s) u(s)
Dynamic system
Can just multiply G and u!
Note: Here I use capital letters for the transfer function G(s),
but we may sometimes use lower case, g(s)

## Slide 16: General procedure in this course
Nonlinear dynamic model
Steady state model: Use to find missing data
Introduce deviation variables and linearize*
Laplace of both sides of linear model (t ! s)
Algebra ! Transfer function, G(s)
Block diagram
Controller design
*Note: We will only use Laplace for linear systems with deviation variables!