## Slide 1: Self-optimizing control Theory
Sigurd Skogestad

## Slide 2: Outline
Skogestad procedure for control structure design:
  Top Down
    Step S1: Define operational objective (cost) and constraints
    Step S2: Identify degrees of freedom and optimize operation for disturbances
    Step S3: Implementation of optimal operation
      Control active constraints
      Control self-optimizing variables for unconstrained, c=Hy
    Step S4: Where set the production rate? (Inventory control)
  Bottom Up
    Step S5: Regulatory control: What more to control (secondary CV’s)?
    Step S6: Supervisory control
    Step S7: Real-time optimization

## Slide 3: Step S3: Implementation of optimal operation
Optimal operation for given d*:
  subject to:
  Model equations:
  Operational constraints:
→
Problem: Usally cannot keep constant because disturbances d change
How should we adjust the degrees of freedom (u)?
What should we control?

## Slide 4: “Optimizing Control”
y

## Slide 5: “Self-Optimizing Control”
What should we control?
(What is c? What is H?)
y
: Nonsquare matrix
  Usually selection matrix of 0’s and some 1’s (measurement selection)
  Can also be full matrix (measurement combinations)
Self-optimizing control: Constant setpoints give acceptable loss

## Slide 6: Self-optimizing control
Self-optimizing control is when we can achieve an acceptable loss with constant setpoint values for the controlled variables
BAD
Good
c

## Slide 7: Recap: marathon runner
CV = heart rate is good “self-optimizing” variable
Simple and robust implementation
Disturbances are indirectly handled by keeping a constant heart rate
May have infrequent adjustment of setpoint (cs)
c = heart rate
select one measurement
c=heart rate
J=T
copt
Optimal operation - Runner

## Slide 8: Optimal operation
Cost J
Controlled variable c
copt
Jopt

## Slide 9: The ideal “self-optimizing” variable is the gradient, Ju
  Keep gradient at zero for all disturbances (c = Ju=0)
  Problem: Usually no measurement of gradient
Unconstrained degrees of freedom
u
cost J
Ju=0
Ju<0
Ju<0
uopt
Ju
0
*I.J. Halvorsen, S. Skogestad, Indirect on-line optimization through setpoint control, in: AIChE 1997 Annual Meeting, Los Angeles; paper 194h.
*I.J. Halvorsen, S. Skogestad, J.C. Morud, V. Alstad, Optimal selection of controlled variables, Industrial & Engineering Chemistry Research 42 (14) (2003) 3273–3284
Notes: 9

## Slide 10: Unconstrained optimum: NEVER try to control a variable that reaches max or min at the optimum
  In particular, never try to control directly the cost J
  Assume we want to minimize J (e.g., J = V = energy) - and we make the stupid choice os selecting CV = V = J
    Then setting J < Jmin: Gives infeasible operation (cannot meet constraints)
    and setting J > Jmin: Forces us to be nonoptimal (two steady states: may require strange operation)
u
J
Jmin
J>Jmin
J<Jmin
?

## Slide 11: Measurements or mesurement combinations
Ideally: c = Ju
In practice: c = Hy
measurement noise
steady-state
control error
disturbance
controlled
variable

## Slide 12: Optimal measurement combination
Candidate measurements (y): Include also inputs u
H
measurement noise
control error
disturbance
controlled
variable

## Slide 13: Nullspace method
Proof: Given , and :
To make for any , we must have .
No measurement noise (ny=0)
V. Alstad, S. Skogestad, Null space method for selecting optimal measurement combinations as controlled variables,
Industrial & Engineering Chemistry Research 46 (2007) 846–853.
Jäschke, J., Cao, Y., & Kariwala, V. (2017). Self-optimizing control–A survey. Annual Reviews in Control, 43, 199–223.

## Slide 14: Nullspace method gives Ju=0
Proof:
Formula for :
Let . We can verify that . Therefore, , and thus controlling c () leads to .
Proof. Appendix B in: Jäschke and Skogestad, ”NCO tracking and self-optimizing control in the context of real-time optimization”, Journal of Process Control, 1407-1416 (2011)

## Slide 15: Nullspace method (HF=0) gives Ju=0
Proof. Appendix B in: Jäschke and Skogestad, ”NCO tracking and self-optimizing control in the context of real-time optimization”, Journal of Process Control, 1407-1416 (2011)
Proof (constant d):

## Slide 16: Example. Nullspace Method for Marathon runner
u = power, d = slope [degrees]
y1 = hr [beat/min], y2 = v [m/s]
F = dyopt/dd =
H = [h1 h2]
HF = 0  h1 f1 + h2 f2 = 0.25 h1 – 0.2 h2 = 0
Choose h1 = 1  h2 = 0.25/0.2 = 1.25
Conclusion: c = hr + 1.25 v
Control c = constant  hr increases when v decreases (OK uphill!)

## Slide 17: Marathon runner: Exact local method
Normalized H1 = D*H = [1 1.02]
Conclusion: c = hr + 1.02 v
Before (nullspace method): c = hr + 1.25 v
Note: Gives same as nullspace when Wny is small

## Slide 18: Extension: "Exact local method" (with measurement noise)
General analytical solution (“full” H):
No disturbances (Wd= [ ]) + same noise for all measurements (Wny= Y = I):
Optimal is H=GyT (“control sensitive measurements”)
    Proof: Use analytic expression
No noise (Wny=0): Cannot use analytic expression, but optimal is clearly
HF = 0 (Nullspace method)
    Assumes enough measurements: #y #u + #d
    If “extra” measurements (>) then solution is not unique
V. Alstad, S. Skogestad, E.S. Hori, Optimal measurement combinations as controlled variables, Journal of Process Control 19 (1) (2009) 138–148.
Jäschke, J., Cao, Y., & Kariwala, V. (2017). Self-optimizing control–A survey. Annual Reviews in Control, 43, 199–223.

## Slide 19
Note: HF=0 -> copt=0 (Nullspace method)
z

## Slide 20: Obtaining F
is defined as the gain matrix from the disturbances to the optimal measurements 
Brute force method:
For every disturbance :
  Perturb the system with , small
  Reoptimize the system  obtain change in measurements
  Obtain -th column of :
Return

## Slide 21: Linearization method for F
can also be obtained through a linearized state-space model:
0

## Slide 22: Toy Example.
Reference: I. J. Halvorsen, S. Skogestad, J. Morud and V. Alstad, “Optimal selection of controlled variables”, Industrial & Engineering Chemistry Research, 42 (14), 3273-3284 (2003).
Here:
For , =100
For ,
For ,
Single measurements

## Slide 23: Toy Example. Exact local method. Combine all measurements
Reference: V. Alstad et al. , Journal of Process Control 19 (2009) 138–148
H = (Y YT )-1 G y
Here:
(Y YT )-1 =
1.0000 0 0 0
0 0.0632 -0.2342 -0.0468
0 -0.2342 0.9415 -0.0117
0 -0.0468 -0.0117 0.9977
H = (Y YT )-1 G y = [0.1000 -1.1241 4.7190 -0.0562]
Normalized to have 2-norm = 1.
H = [ 0.0206 -0.2317 0.9725 -0.0116]

## Slide 24: Toy Example: Nullspace method (not unique)

## Slide 25: Toy Example. Nullspace method with 2 measurements

## Slide 26: Conclusion: GOOD “SELF-OPTIMIZING” CV = c
Optimal value is constant (independent of disturbance d):
   Want small optimal sensitivity:
c is “sensitive” to input u (MV) (to reduce effect of measurement noise)
   Want large gain
(Equivalently: Optimum should be flat!)
BAD
Good