## Slide 1: Plantwide process control Introduction
Sigurd Skogestad, NTNU

## Slide 2: Shortcourse PSE Asia 2019: Economic process control 13 January 2019 from 9:00-17:00 at Faculty of Engineering, Chulalongkorn University
Presenters:
Professor Sigurd Skogestad, NTNU
Professor Nitin Kaistha, IIT Kanpur (case studies)
This workshop focuses on the big picture when designing a control system for process plants. The overall objectives is to maximize the operational profit. This should also be the basis for designing the control system, all the way from PID controllers at the bottom of the control hierarchy to the possible RTO layer at the top.
09.00 Session 1. Overview of economic plantwide control
- Control degrees of freedom
- Our paradigm: Hierarchical decision (control) layer
- What is optimal operation?
- Distillation examples
10.00 Session 2. What to control? (Selection of primary controlled variables based on economics)
- Degrees of freedom
- Optimization
- Active constraints
- Self-optimizing control
11.00 Case studies
12.00 Lunch
13.00 Session 3. Where to set the production rate and bottleneck
- Inventory control
- Consistency
- Radiation rule
- Location of throughput manipulator (TPM)
14.00 Session 4. Design of the regulatory control layer ("what more should we control")
- PID control, Stabilization
- Secondary controlled variables (measurements)
- Pairing with inputs
15.00 Session 5 Design of supervisory control layer
- Cascade control
- Switching between active constraints
- MV saturation (SIMO controllers) : Split range control / Controllers with different setpoints
- CV changes: Selectors
- Decentralized versus centralized (MPC)
Session 6. Real-time optimization (see plenary tomorrow)
Alternative implementations:
- Conventional RTO
- Dynamic RTO / Economic MPC
- Combination with Self-optimizing control
- Extremum seeking control / NCO tracking / Hill climbing
16.00 Session 7 Case studies (throughout the day)
- Case studies using Hysys

## Slide 3: Part 1. Plantwide control
Introduction to plantwide control (what should we really control?)
Introduction.
  Objective: Put controllers on flow sheet (make P&ID)
  Two main objectives for control: Longer-term economics (CV1) and shorter-term stability (CV2)
  Regulatory (basic) and supervisory (advanced) control layer
Optimal operation (economics)
  Define cost J and constraints
  Active constraints (as a function of disturbances)
  Selection of economic controlled variables (CV1). Self-optimizing variables.

## Slide 4: Why control?
Operation
time
Actual value(dynamic)
Steady-state (average)
In practice never steady-state:
  Feed changes
  Startup
  Operator changes
  Failures
  …..
Control is needed to reduce the effect of disturbances
30% of investment costs are typically for instrumentation and control
“Disturbances” (d’s)

## Slide 5: Countermeasures to disturbances (I)
Eliminate/Reduce the disturbance
  Design process so it is insensitive to disturbances
      Example: Use buffertank to dampen disturbances
  Detect and remove source of disturbances
      “Statistical process control”
      Example: Detect and eliminate variations in feed composition
inflow
outflow
∞
Tin
Tout

## Slide 6: Countermeasures to disturbances (II)
II. Process control
Do something (usually manipulate valve)
to counteract the effect of the disturbances
  (a) Manual control: Need operator
  (b) Automatic control: Need measurement + automatic valve + computer
    Goals automatic control:
      Smaller variations
        more consistent quality
        More optimal
      Smaller losses (environment)
      Lower costs
      More production
    Industry: Still large potential for improvements!

## Slide 7: Classification of variables
Process
u
input (MV)
y
output (CV)
d
Independent variables (“the cause”):
  Inputs (MV, u): Variables we can adjust (valves)
  Disturbances (DV, d): Variables outside our control
Dependent (output) variables (“the effect or result”):
  (c) Primary outputs (CVs, y1): Variables we want to keep at a given setpoint
  (d) Secondary outputs (y2): Extra measurements that we may use to improve control

## Slide 8: Inputs for control (MVs)
Usually: Inputs (MVs) are valves.
  Physical input is valve position (z), but we often simplify and say that flow (q) is input
Valve Equation

## Slide 9: Notation feedback controllers (P&ID)
TC
2nd letter:
C: controller
I: indicator (measurement)
T: transmitter (measurement)
1st letter: Controlled variable (CV) = What we are trying to control (keep constant)
T: temperature
F: flow
L: level
P: pressure
DP: differential pressure (Δp)
A: Analyzer (composition)
C: composition
X: quality (composition)
H: enthalpy/energy
Ts
(setpoint CV)
T
(measured CV)
MV (could be valve)

## Slide 10
LC
H
Hs
Inflow (d)
Outflow (u)
INPUT (u): OUTFLOW (Input for control!)
OUTPUT (y): LEVEL
DISTURBANCE (d): INFLOW
Example: Level control
CLASSIFICATION OF VARIABLES:

## Slide 11: How we design a control system for a complete chemical plant?
Where do we start?
What should we control? and why?
etc.
etc.

## Slide 12: Plantwide control = Control structure design
Not the tuning and behavior of each control loop,
But rather the control philosophy of the overall plant with emphasis on the structural decisions:
  Selection of controlled variables (“outputs”)
  Selection of manipulated variables (“inputs”)
  Selection of (extra) measurements
  Selection of control configuration (structure of overall controller that interconnects the controlled, manipulated and measured variables)
  Selection of controller type (LQG, H-infinity, PID, decoupler, MPC etc.).
That is: Control structure design includes all the decisions we need make to get from ``PID control’’ to “PhD” control

## Slide 13: Previous work on plantwide control:
Page Buckley (1964) - Chapter on “Overall process control” (still industrial practice)
Greg Shinskey (1967) – process control systems
Alan Foss (1973) - control system structure
Bill Luyben et al. (1975- ) – case studies ; “snowball effect”
George Stephanopoulos and Manfred Morari (1980) – synthesis of control structures for chemical processes
Ruel Shinnar (1981- ) - “dominant variables”
Jim Downs (1991) - Tennessee Eastman challenge problem
Larsson and Skogestad (2000): Review of plantwide control

## Slide 14
Alan Foss (“Critique of chemical process control theory”, AIChE Journal,1973):
The central issue to be resolved ... is the determination of control system structure. Which variables should be measured, which inputs should be manipulated and which links should be made between the two sets? There is more than a suspicion that the work of a genius is needed here, for without it the control configuration problem will likely remain in a primitive, hazily stated and wholly unmanageable form. The gap is present indeed, but contrary to the views of many, it is the theoretician who must close it.

## Slide 15: Main objectives control system
Economics: Implementation of acceptable (near-optimal) operation
Regulation: Stable operation
ARE THESE OBJECTIVES CONFLICTING?
Usually NOT
  Different time scales
    Stabilization fast time scale
  Stabilization doesn’t “use up” any degrees of freedom
    Reference value (setpoint) available for layer above
    But it “uses up” part of the time window (frequency range)

## Slide 16: Optimal operation (economics)
Example of systems we want to operate optimally
Process plant
  minimize J=economic cost
Runner
  minimize J=time
«Green» process plant
  Minimize J=environmental impact (with given economic cost)
General multiobjective:
  Min J (scalar cost, often $)
  Subject to satisfying constraints (environment, resources)

## Slide 17
Theory: Optimal operation
Objectives
Present state
Model of system
Theory:
  Model of overall system
  Estimate present state
  Optimize all degrees of freedom
Problems:
  Model not available
  Optimization complex
  Not robust (difficult to handle uncertainty)
  Slow response time
Process control:
  Excellent candidate for centralized control
(Physical) Degrees of freedom
CENTRALIZED
OPTIMIZER

## Slide 18: Practice: Engineering systems
Most (all?) large-scale engineering systems are controlled using hierarchies of quite simple controllers
  Large-scale chemical plant (refinery)
  Commercial aircraft
100’s of loops
Simple components:
  on-off + PI-control + nonlinear fixes + some feedforward
Same in biological systems

## Slide 19
Practical operation: Hierarchical structure
Manager
Process engineer
Operator/RTO
Operator/”Advanced control”/MPC
PID-control
u = valves
Our Paradigm

## Slide 20
Practice: Process operation
Practice:
Hierarchical structure
Each layer has its own goal (”default action”):
  Keep CV at given setpoint
Boss: layer above (adjusts setpoint)
Goal each layer: Action without boss is «Self-optimizing»
CV = controlled variable

## Slide 21
cs = y1s
MPC
PID
y2s
RTO
Follow path (+ look after other variables)
Stabilize + avoid drift
Min J (economics)
u (valves)
OBJECTIVE
Dealing with complexity
Plantwide control: Objectives
The controlled variables (CVs)
interconnect the layers
Notes: 21

## Slide 22: Translate optimal operation into simple control objectives: What should we control?
CV1 = c ? (economics)
CV2 = ? (stabilization)

## Slide 23: CV1 = Economic controlled variables
Systematic procedure for selecting economic controlled variables (CV1)
  Active constraints
  Remaining unconstrained degrees of freedom:
    «Self-optimizing» variables

## Slide 24: Outline
Skogestad procedure for control structure design
  I Top Down
    Step S1: Define operational objective (cost) and constraints
    Step S2: Identify degrees of freedom and optimize operation for disturbances
    Step S3: Implementation of optimal operation
      What to control ? (primary CV’s) (self-optimizing control)
    Step S4: Where set the production rate? (Inventory control)
  II Bottom Up
    Step S5: Regulatory control: What more to control (secondary CV’s) ?
    Step S6: Supervisory control
    Step S7: Real-time optimization

## Slide 25: Step S1. Define optimal operation (economics)
What are we going to use our degrees of freedom (u=MVs) for?
Typical cost function*:
*No need to include fixed costs (capital costs, operators, maintainance) at ”our” time scale (hours)
Note: J=-P where P= Operational profit
J = cost feed + cost energy – value products

## Slide 26: Optimal operation distillation column
Distillation at steady state with given p and F: N=2 DOFs, e.g. L and V (u)
Cost to be minimized (economics)
  J = - P where P= pD D + pB B – pF F – pVV
Constraints
  Purity D: For example xD, impurity · max
  Purity B: For example, xB, impurity · max
  Flow constraints: min · D, B, L etc. · max
  Column capacity (flooding): V · Vmax, etc.
  Pressure: 1) p given (d) 2) p free (u): pmin · p · pmax
  Feed: 1) F given (d) 2) F free (u): F · Fmax
Optimal operation: Minimize J with respect to steady-state DOFs (u)
value products
cost energy (heating+ cooling)
cost feed

## Slide 27: Step S2. Optimize (a) Identify degrees of freedom (b) Optimize for expected disturbances
Need good model, usually steady-state
Optimization is time consuming! But it is offline
Main goal: Identify ACTIVE CONSTRAINTS
A good engineer can often guess the active constraints

## Slide 28: Step S2a: Degrees of freedom (DOFs) for operation
NOT as simple as one may think!
To find all operational (dynamic) degrees of freedom:
Count valves! (Nvalves)
“Valves” also includes adjustable compressor power, etc.
Anything we can manipulate!
BUT: not all these have a (steady-state) effect on the economics
Steady-state DOFs

## Slide 29: Steady-state degrees of freedom (DOFs)
IMPORTANT!
DETERMINES THE NUMBER OF VARIABLES TO CONTROL!
No. of primary CVs = No. of steady-state DOFs
CV = controlled variable
Methods to obtain no. of steady-state degrees of freedom (Nss):
Equation-counting
  Nss = no. of variables – no. of equations/specifications
  Very difficult in practice
Valve-counting (easier!)
  Nss = Nvalves – N0ss – Nspecs
  Nvalves: include also variable speed for compressor/pump/turbine
  Nspecs: Equality constraints (normally included in constraints)
  N0ss = variables with no steady-state effect
    Inputs/MVs with no steady-state effect (e.g. extra bypass)
    Outputs/CVs with no steady-state effect that need to be controlled (e.g., liquid levels)
Potential number for some units (useful for checking!)
Correct answer: Will eventually find it when we perform optimization
Steady-state DOFs

## Slide 30: Does a pump give a degree of freedom?
Yes, if it has variable speed drive

## Slide 31
Nvalves = 6 , N0y = 2* ,
NDOF,SS = 6 -2 = 4 (including feed and pressure as DOFs)
Typical Distillation column
*N0y : no. controlled variables (liquid levels) with no steady-state effect
4 DOFs:
With given feed and pressure:
NEED TO IDENTIFY 2 more CV’s
- Typical: Top and btm composition
1
2
3
4
5
6
Steady-state DOFs

## Slide 32: Steady-state degrees of freedom (Nss): 3. Potential number for some process units
each external feedstream: 1 (feedrate)
splitter: n-1 (split fractions) where n is the number of exit streams
mixer: 0
compressor, turbine, pump: 1 (work/speed) (BUT: Must have variable speed)
adiabatic flash tank: 0*
liquid phase reactor: 1 (holdup reactant)
gas phase reactor: 0*
heat exchanger: 1 (bypass or flow of cooling/heating)
column (e.g. distillation) excluding heat exchangers: 0* + no. of sidestreams
pressure* : add 1DOF at each extra place you set pressure (using an extra valve, compressor or pump), e.g. in adiabatic flash tank, gas phase reactor or absorption column
*Pressure is normally assumed to be given by the surrounding process and is then not a degree of freedom
Ref: Araujo, Govatsmark and Skogestad (2007)
Extension to closed cycles: Jensen and Skogestad (2009)
Real number may be less, for example, if there is no bypass valve or no variable speed
Steady-state DOFs

## Slide 33
“Potential number”,
Nss= 0 (column distillation) + 1 (feed) + 2*1 (heat exchangers) + 1 (split) = 4
With given feed and pressure: N’ss = 4 – 2 = 2
Distillation column (with feed and pressure as DOFs)
split
Steady-state DOFs

## Slide 34: Step S2b: Optimize for expected disturbances
What are the optimal values for our degrees of freedom u (MVs)?
Minimize J with respect to u for given disturbance d (usually steady-state):
  minu J(u,x,d)
  subject to:
  Model equations (e,g, Hysys): f(u,x,d) = 0
  Operational constraints: g(u,x,d) < 0
  OFTEN VERY TIME CONSUMING
  Commercial simulators (Aspen, Unisim/Hysys) are set up in “design mode” and often work poorly in “operation (rating) mode”.
  Optimization methods in commercial simulators often poor
    We use Matlab or even Excel “on top”
J = cost feed + cost energy – value products

## Slide 35: Step S3: Implementation of optimal operation
Have found the optimal way of operation. How should it be implemented?
What to control ? (primary CV’s).
  Active constraints
  Self-optimizing variables (for unconstrained degrees of freedom)
Objective: Move optimization into control layer

## Slide 36: Optimal operation of runner
  Cost to be minimized, J=T
  One degree of freedom (u=power)
  What should we control?
Optimal operation - Runner

## Slide 37: 1. Optimal operation of Sprinter
  100m. J=T
  Active constraint control:
    Maximum speed (”no thinking required”)
    CV = power (at max)
Optimal operation - Runner

## Slide 38: 2. Optimal operation of Marathon runner
    40 km. J=T
    What should we control? CV=?
    Unconstrained optimum
Optimal operation - Runner
u=power
J=T
uopt

## Slide 39
Any self-optimizing variable (to control at constant setpoint)?
    c1 = distance to leader of race
    c2 = speed
    c3 = heart rate
    c4 = level of lactate in muscles
Optimal operation - Runner
Self-optimizing control: Marathon (40 km)

## Slide 40: Conclusion Marathon runner
c = heart rate
select one measurement
CV = heart rate is good “self-optimizing” variable
Simple and robust implementation
Disturbances are indirectly handled by keeping a constant heart rate
May have infrequent adjustment of setpoint (cs)
Optimal operation - Runner
c=heart rate
J=T
copt

## Slide 41: Step 3. What should we control (c)? (primary controlled variables y1=c)
Selection of controlled variables c
  Control active constraints!
  Unconstrained variables: Control self-optimizing variables!

## Slide 42: Expected active constraints distillation
Both products (D,B) generally have purity specs
Valuable product: Purity spec. always active
  Reason: Amount of valuable product (D or B) should always be maximized
    Avoid product “give-away” (“Sell water as methanol”)
    Also saves energy
Control implications:
ALWAYS Control valuable product at spec. (active constraint).
May overpurify (not control) cheap product
valuable
product
methanol
+ max. 0.5%
water
cheap product
(byproduct)
water
+ max. 2%
methanol
methanol
+ water
Selection of CV1

## Slide 43: Example with Quiz: Optimal operation of two distillation columns in series

## Slide 44: Operation of Distillation columns in series With given F (disturbance): 4 steady-state DOFs (e.g., L and V in each column)
DOF = Degree Of Freedom
Ref.: M.G. Jacobsen and S. Skogestad (2011)
Energy price: pV=0-0.2 $/mol (varies)
Cost (J) = - Profit = pF F + pV(V1+V2) – pD1D1 – pD2D2 – pB2B2
> 95% B
pD2=2 $/mol
F ~ 1.2mol/s
pF=1 $/mol
< 4 mol/s
< 2.4 mol/s
> 95% C
pB2=1 $/mol
N=41
αAB=1.33
N=41
αBC=1.5
> 95% A
pD1=1 $/mol
QUIZ: What are the expected active constraints?
1. Always. 2. For low energy prices.
QUIZ 1

## Slide 45: Operation of Distillation columns in series With given F (disturbance): 4 steady-state DOFs (e.g., L and V in each column)
DOF = Degree Of Freedom
Ref.: M.G. Jacobsen and S. Skogestad (2011)
Energy price: pV=0-0.2 $/mol (varies)
Cost (J) = - Profit = pF F + pV(V1+V2) – pD1D1 – pD2D2 – pB2B2
> 95% B
pD2=2 $/mol
F ~ 1.2mol/s
pF=1 $/mol
< 4 mol/s
< 2.4 mol/s
> 95% C
pB2=1 $/mol
1. xB = 95% B
Spec. valuable product (B): Always active!
Why? “Avoid product give-away”
N=41
αAB=1.33
N=41
αBC=1.5
> 95% A
pD1=1 $/mol
2. Cheap energy: V1=4 mol/s, V2=2.4 mol/s
Max. column capacity constraints active!
Why? Overpurify A & C to recover more B
QUIZ: What are the expected active constraints?
1. Always. 2. For low energy prices.
Hm….?
SOLUTION QUIZ 1

## Slide 46: Control of Distillation columns in series
Given
LC
LC
LC
LC
PC
PC
QUIZ. Assume low energy prices (pV=0.01 $/mol).
How should we control the columns?
HINT: CONTROL ACTIVE CONSTRAINTS
Red: Basic regulatory loops
QUIZ 2

## Slide 47: Control of Distillation columns in series
Given
LC
LC
LC
LC
PC
PC
Red: Basic regulatory loops
CC
xB
xBS=95%
MAX V1
MAX V2
1 unconstrained DOF (L1):
Use for what?? CV=?
Not: CV= xA in D1! (why? xA should vary with F!)
Maybe: constant L1? (CV=L1)
Better: CV= xA in B1? Self-optimizing?
General for remaining unconstrained DOFs:
LOOK FOR “SELF-OPTIMIZING” CVs = Variables we can keep constant
WILL GET BACK TO THIS!
SOLUTION QUIZ 2
QUIZ. Assume low energy prices (pV=0.01 $/mol).
How should we control the columns?
HINT: CONTROL ACTIVE CONSTRAINTS
Hm…….
HINT: CONTROL ACTIVE CONSTRAINTS!

## Slide 48: Comment: Distillation column control in practice
Add stabilizing temperature loops
  In this case: use reflux (L) as MV because boilup (V) may saturate
  T1s and T2s then replace L1 and L2 as DOFs.
Replace V1=max and V2=max by dpmax-controllers (assuming max. load is limited by flooding)
See next slide

## Slide 49: Control of Distillation columns in series
Given
LC
LC
LC
LC
PC
PC
TC
TC
T1s
T2s
T1
T2
Comment: In practice
MAX V2
MAX V1
CC
xB
xBS=95%

## Slide 50: Active constraint regions for two distillation columns in series
CV = Controlled Variable
3
2
0
1
1
0
2
[mol/s]
[$/mol]
1
Cheap energy: 1 remaining unconstrained DOF (L1)
-> Need to find 1 additional CVs (“self-optimizing”)
More expensive energy: 3 remaining unconstrained DOFs
-> Need to find 3 additional CVs (“self-optimizing”)
Energy
price
Distillation example: Not so simple
Mode 2: operate at BOTTLENECK
Higher F infeasible because
all 5 constraints reached
Mode 1

## Slide 51: How many active constraints regions?
Maximum:
  nc = number of constraints
BUT there are usually fewer in practice
Certain constraints are always active (reduces effective nc)
Only nu can be active at a given time
  nu = number of MVs (inputs)
Certain constraints combinations are not possibe
  For example, max and min on the same variable (e.g. flow)
Certain regions are not reached by the assumed disturbance set
Distillation
nc = 5
  25 = 32
xB always active
2^4 = 16
-1 = 15
In practice = 8

## Slide 52: More on: Optimal operation
Mode 1. Given feedrate
Mode 2. Maximum production
Comment: Depending on prices, Mode 1 may include many subcases (active constraints regions)
minimize J = cost feed + cost energy – value products
Two main cases (modes) depending on marked conditions:

## Slide 53: Mode 1. Given feedrate
Amount of products is then usually indirectly given and
Optimal operation is then usually unconstrained
“maximize efficiency (energy)”
Control:
Operate at optimal trade-off
NOT obvious what to control
CV = Self-optimizing variable
J = cost feed– value products + cost energy
c
J = energy
copt
Often constant

## Slide 54: Mode 2. Maximum production
Assume feedrate is degree of freedom
Assume products much more valuable than feed
Optimal operation is then to maximize product rate
“max. constrained”, prices do not matter
Control:
Focus on tight control of bottleneck
“Obvious what to control”
CV = ACTIVE CONSTRAINT
c
J
cmax
Infeasible
region
J = cost feed + cost energy – value products

## Slide 55
If constraint can be violated dynamically (only average matters)
  Required Back-off = “measurement bias” (steady-state measurement error for c)
If constraint cannot be violated dynamically (“hard constraint”)
  Required Back-off = “measurement bias” + maximum dynamic control error
Jopt
Back-off
Loss
c ≥ cconstraint
c
J
More on: Active output constraints
Need back-off
  Want tight control of hard output constraints to reduce the back-off. “Squeeze and shift”-rule
The backoff is the “safety margin” from the active constraint and is defined as the difference between the constraint value and the chosen setpoint
Backoff = |Constraint – Setpoint|
CV = Active constraint

## Slide 56
Hard Constraints: «SQUEEZE AND SHIFT»
CV = Active constraint

## Slide 57: Hard Constraints: «SQUEEZE AND SHIFT»
© Richalet
SHIFT
SQUEEZE
CV = Active constraint
Rule for control of hard output constraints:
“Squeeze and shift”!
Reduce variance (“Squeeze”) and “shift” setpoint cs to reduce backoff

## Slide 58
Example. Optimal operation = max. throughput. Want tight bottleneck control to reduce backoff!
Time
Back-off
= Lost production
CV = Active constraint

## Slide 59: Example back-off. xB = purity product > 95% (min.)
D1 directly to customer (hard constraint)
  Measurement error (bias): 1%
  Control error (variation due to poor control): 2%
  Backoff = 1% + 2% = 3%
  Setpoint xBs= 95 + 3% = 98% (to be safe)
  Can reduce backoff with better control (“squeeze and shift”)
D1 to large mixing tank (soft constraint)
  Measurement error (bias): 1%
  Backoff = 1%
  Setpoint xBs= 95 + 1% = 96% (to be safe)
  Do not need to include control error because it averages out in tank
CV = Active constraint
D1
xB
8
xB
xB,product
±2%

## Slide 60: Unconstrained optimum: Control “self-optimizing” variable.
Which variable is best?
Often not obvious (marathon runner)

## Slide 61: Control of Distillation columns. Cheap energy
Given
LC
LC
LC
LC
PC
PC
Overpurified: To avoid loss of valuable product B
CC
xB
xBS=95%
MAX V1
MAX V2
1 unconstrained DOF (L1): What is a good CV?
Not: CV= xB in D1! (why? Overpurified, so xB,opt increases with F)
Maybe: constant L1? (CV=L1)
Better: CV= xA in B1? Self-optimizing?
Example.
Overpurified
Overpurified

## Slide 62
Given
LC
LC
LC
LC
PC
PC
CC
xB
xBS=95%
MAX V1
MAX V2
CC
xAS=2.1%
Control of Distillation columns. Cheap energy
Solution.
Notes: 62

## Slide 63
Given
(TPM)
LC
LC
LC
LC
PC
PC
CC
xB
xBS=95%
MAX V1
MAX V2
CC
xAS=2.1%
What happens if we increase the federate?
Is this control structure still OK??
Notes: 63

## Slide 64
Given
(TPM)
LC
LC
LC
LC
PC
PC
CC
xB
xBS=95%
MAX V1
MAX V2
CC
xA
xAS=95%
Increase federate: Reach xA-constraint
TPM
Notes: 64

## Slide 65
LC
LC
LC
LC
PC
PC
CC
xB
xBS=95%
MAX V1
MAX V2
CC
xA
xAS=95%
Increase federate further: Reach also xC-constraint (Bottleneck)
TPM
CC
xC
xCS=95%
TPM used
as MV
Notes: 65

## Slide 66
LC
LC
LC
LC
PC
PC
CC
xB
xBS=95%
MAX V1
MAX V2
CC
xA
xAS=95%
Move TPM
CC
xC
xCS=95%
TPM used
as MV
Move TPM to F2 (closer to bottleneck) and rearrange level loop
Notes: 66

## Slide 67
Q1: I have to set back-off on output active constraints, right? Should I set it before evaluating losses? How much back-off should be set, 5%?
[Sigurd Skogestad] 5% is a good start, but it depends mostly on the measurement accuracy. Note that it must be a hard output constraint.
The value of the active constraint is usually considered a disturbance; this also takes care of the backoff variation
Q2: When I consider input active constraints as disturbance too. Ex. Temp feed to SOFC (T0f, T0a) are active at upper bound. Should I set +10% on this disturbance change or just -10%.
Is it possible to set +10% in this case?
[Sigurd Skogestad] Yes, the actual available input could be larger than what you think
Q3: In region I, I would like to try same structure as in region II which means Uf,MCFC set at 75% (upper bound) but it is an input active constraint
which considered as disturbance too. Hence Uf,MCFC doesn’t a disturbance in region I, am I right? Then region I have 4 disturbances but region II and III have 5 disturbances, am I right?
[Sigurd Skogestad] No, because also the value of the active constraint is usually considered as a disturbance
Q4: Do I need back-off on input active constraints too?
Answer: Input constraint: Normally not, except of it is a bottleneck constraint and the TPM is located somewhere else

## Slide 68: More on: WHAT ARE GOOD “SELF-OPTIMIZING” VARIABLES?
Intuition: “Dominant variables” (Shinnar)
More precisely
  Optimal value of CV is constant
  CV is “sensitive” to MV (large gain)
Unconstrained variables

## Slide 69: GOOD “SELF-OPTIMIZING” CV=c
Optimal value copt is constant (independent of disturbance d):
  c is “sensitive” to MV=u (to reduce effect of measurement noise)
Equivalently: Optimum should be flat
Unconstrained optimum
BAD
Good
Good

## Slide 70: Conclusion optimal operation
ALWAYS:
1. Control active constraints and control them tightly!!
  Good times: Maximize throughput -> tight control of bottleneck
2. Identify “self-optimizing” CVs for remaining unconstrained degrees of freedom
Use offline analysis to find expected operating regions and prepare control system for this!
  One control policy when prices are low (nominal, unconstrained optimum)
  Another when prices are high (constrained optimum = bottleneck)
ONLY if necessary: consider RTO on top of this