## Slide 1: Plantwide process control
Sigurd Skogestad
Norwegian University of Science and Technology

## Slide 2: Part 1. Plantwide control
Introduction
  Objective: Put controllers on flow sheet (make P&ID)
  Two main objectives for control: Longer-term economics (CV1) and shorter-term stability (CV2)
  Regulatory (basic) and supervisory (advanced) control layer
Optimal operation (economics)
  Define cost J and constraints
  Active constraints (as a function of disturbances)
  Selection of economic controlled variables (CV1). Self-optimizing variables.

## Slide 3: Why do we need control?
Operation
time
Actual value(dynamic)
Steady-state (average)
In practice steady state doesn’t happen:
  Feed changes
  Startup
  Operator changes
  Failures
  …..
Control is needed to reduce the effect of disturbances
30% of investment costs are typically for instrumentation and control
“Disturbances” (d’s)

## Slide 4: Countermeasures to disturbances (I)
Eliminate/reduce the disturbance
  Design process so it is insensitive to disturbances
      Example: Use buffer tank to dampen disturbances
  Detect and remove source of disturbances
      “Statistical process control”
      Example: Detect and eliminate variations in feed composition
inflow
outflow
∞
Tin
Tout

## Slide 5: Countermeasures to disturbances (II)
Process control
Do something (usually manipulate a valve) to
counteract the effect of the disturbance
  Manual control: Need operator
  (b) Automatic control: Need measurement + automatic valve + computer
    Goals automatic control:
      Smaller variations
        more consistent quality
        More optimal
      Smaller losses (environment)
      Lower costs
      More production
    Industry: Still large potential for improvements!

## Slide 6: Classification of variables
Independent variables (“the cause”):
  (a) Inputs (MV, u): Variables we can adjust (valves)
  (b) Disturbances (DV, d): Variables outside our control
Dependent (output) variables (“the effect or result”):
  (c) Primary outputs (CVs, y1): Variables we want to keep at a given setpoint
  (d) Secondary outputs (y2): Extra measurements that we may use to improve control
Process
u
input (MV)
y
output (CV)
d

## Slide 7: Inputs for control (MVs)
Usually: Inputs (MVs) are valves.
  Physical input is valve position (z), but we often simplify and say that flow (q) is input
Valve equation:

## Slide 8: Feedback vs. feedforward control
Feedback: «reactive»  sees changes in output and tries to correct it through manipulation
Feedforward: «predictive»  uses disturbance measurement to improve control action
Example: cooking
  Feedforward: follow recipe exactly
  Feedback: look at colour, taste, texture

## Slide 9: Notation feedback controllers (P&ID)
TC
2nd letter:
C: controller
I: indicator (measurement)
T: transmitter (measurement)
1st letter: Controlled variable (CV)
T: temperature
F: flow
L: level
P: pressure
DP: differential pressure (Δp)
A: Analyzer (composition)
C: composition
X: quality (composition)
H: enthalpy/energy
…
Ts
(setpoint CV)
T
(measured CV)
MV (e.g., a valve)

## Slide 10: Example: Level control
LC
H
Hs
Inflow
Outflow
INPUT (u): OUTFLOW (Input for control!)
OUTPUT (y): LEVEL
DISTURBANCE (d): INFLOW

## Slide 11
MV = manipulated variable (controller output)
CV = controlled variable (controller input)
Block diagrams: All lines are signals (information)
Combine:
u = process input (adjustable)
d = disturbance (non-adjustable)
y = process output (with setpoint ys)
w = extra measured process variable (state x, y2)
NOTATION and BLOCK DIAGRAMS

## Slide 12: What is best? Feedback or feedforward?

## Slide 13
Example: Feedback vs. feedforward for setpoint control of uncertain process
G
y = G(s) u

## Slide 14
Example: Feedback vs. feedforward for setpoint control of uncertain process
G
y = G(s) u

## Slide 15
But what happens if the process changes?
  Consider a gain change so that the model is wrong
    Process gain from k=3 to k’=4.5

## Slide 16
Gain error (feedback and feedforward): From k=3 to k’=4.5
Time delay (feedback): From

## Slide 17: How can we design a control system for a complete chemical plant?
Where do we start?
What should we control? And why?

## Slide 18: Plantwide control = Control structure design
Not the tuning and behavior of each control loop…
But rather the control philosophy of the overall plant with emphasis on the structural decisions:
  Selection of controlled variables (“outputs”)
  Selection of manipulated variables (“inputs”)
  Selection of (extra) measurements
  Selection of control configuration (structure of overall controller that interconnects the controlled, manipulated and measured variables)
  Selection of controller type (LQG, H-infinity, PID, decoupler, MPC etc.)

## Slide 19: Main objectives of a control system
Economics: Implementation of acceptable (near-optimal) operation
Regulation: Stable operation
ARE THESE OBJECTIVES CONFLICTING?
Usually NOT
  Different time scales
    Stabilization  fast time scale
  Stabilization doesn’t “use up” any degrees of freedom
    Reference value (setpoint) available for layer above
    But it “uses up” part of the time window (frequency range)

## Slide 20: Optimal operation
General approach: minimize cost / maximize profit, subject to satisfying constraints (product quality, environment, resources)
Mathematically,

## Slide 21: Optimal operation (in theory)
objectives
present state
model of system
degrees of freedom
Procedure:
Obtain model of overall system
Estimate present state
Optimize all degrees of freedom
Problems:
Model not available
Optimization is complex
Not robust (difficult to handle uncertainty)
Slow response time
CENTRALIZED OPTIMIZER
(example: Economic MPC)

## Slide 22: Engineering systems
Most (all?) large-scale engineering systems are controlled using hierarchies of quite simple controllers
  Large-scale chemical plant (refinery)
  Commercial aircraft
100’s of loops
Simple components:
  on-off + PI-control + nonlinear fixes + some feedforward

## Slide 23: Practical operation: Hierarchical structure
Manager
Process engineer
Operator/RTO
Operator/”Advanced control”/MPC
PID-control
u = valves

## Slide 24: Optimal operation and control objectives: What should we control?
CV1 (economics)
CV2 (stabilization)

## Slide 25: Outline
Skogestad procedure for control structure design:
  Top Down
    Step S1: Define operational objective (cost) and constraints
    Step S2: Identify degrees of freedom and optimize operation for disturbances
    Step S3: Implementation of optimal operation
      What to control? (primary CV’s) (self-optimizing control)
    Step S4: Where set the production rate? (Inventory control)
  Bottom Up
    Step S5: Regulatory control: What more to control (secondary CV’s)?
    Step S6: Supervisory control
    Step S7: Real-time optimization

## Slide 26: Step S1. Define optimal operation (economics)
What are the ultimate goals of the operation?
Typical cost function*:
*No need to include fixed costs (capital costs, operators, maintainance) at ”our” time scale (hours)
Note: J=-P where P= Operational profit
J = cost feed + cost energy – value products

## Slide 27: Example: distillation column
Distillation at steady state with given p and F: N=2 DOFs, e.g. L and V (u)
Cost to be minimized (economics)
  J = - P where P= pD D + pB B – pF F – pVV
Constraints
  Purity D: For example, xD, impurity ≤ max
  Purity B: For example, xB, impurity ≤ max
  Flow constraints: min ≤ D, B, L etc. ≤ max
  Column capacity (flooding): V ≤ Vmax, etc.
  Pressure: 1) p given (d) 2) p free (u): pmin ≤ p ≤ pmax
  Feed: 1) F given (d) 2) F free (u): F ≤ Fmax
Optimal operation: Minimize J with respect to steady-state DOFs (u)
value products
cost energy (heating + cooling)
cost feed

## Slide 28: Outline
Skogestad procedure for control structure design:
  Top Down
    Step S1: Define operational objective (cost) and constraints
    Step S2: Identify degrees of freedom and optimize operation for disturbances
    Step S3: Implementation of optimal operation
      What to control? (primary CV’s) (self-optimizing control)
    Step S4: Where set the production rate? (Inventory control)
  Bottom Up
    Step S5: Regulatory control: What more to control (secondary CV’s)?
    Step S6: Supervisory control
    Step S7: Real-time optimization

## Slide 29: Step S2. Optimize
(a) Identify degrees of freedom
(b) Optimize for expected disturbances
    Need good model, usually steady-state
    Optimization is time consuming! But it is offline
    Main goal: Identify ACTIVE CONSTRAINTS
    A good engineer can often guess the active constraints

## Slide 30: Step S2a: Degrees of freedom (DOFs) for operation
NOT as simple as one may think!
To find all operational (dynamic) degrees of freedom:
Count valves! (Nvalves)
“Valves” also includes adjustable compressor power, etc.
Anything we can manipulate!
BUT: not all these have a (steady-state) effect on the economics
Steady-state DOFs

## Slide 31: Steady-state degrees of freedom (DOFs)
IMPORTANT!
DETERMINES THE NUMBER OF VARIABLES TO CONTROL!
No. of primary CVs = No. of steady-state DOFs
CV = controlled variable
Methods to obtain no. of steady-state degrees of freedom (Nss):
Equation-counting
  Nss = no. of variables – no. of equations/specifications
  Very difficult in practice
Valve-counting (easier!)
  Nss = Nvalves – N0ss – Nspecs
  Nvalves: include also variable speed for compressor/pump/turbine
  Nspecs: Equality constraints (normally included in constraints)
  N0ss = variables with no steady-state effect
    Inputs/MVs with no steady-state effect (e.g. extra bypass)
    Outputs/CVs with no steady-state effect that need to be controlled (e.g., liquid levels)
Potential number for some units (useful for checking!)
Correct answer: Will eventually find it when we perform optimization
Steady-state DOFs

## Slide 32: Example: typical distillation column
Nvalves = 6 , N0y = 2* ,
NDOF,SS = 6 -2 = 4 (including feed and pressure as DOFs)
*N0y : no. controlled variables (liquid levels) with no steady-state effect
1
2
3
4
5
6
Steady-state DOFs
4 DOFs:
With given feed and pressure:
NEED TO IDENTIFY 2 more CV’s
- Typical: Top and btm composition

## Slide 33: Step S2b: Optimize for expected disturbances
What are the optimal values for our degrees of freedom u (MVs)?
Minimize J with respect to u for given disturbance d (usually steady-state):
  subject to:
  Model equations (e,g, Hysys):
  Operational constraints:
  OFTEN VERY TIME CONSUMING
  Commercial simulators (Aspen, Unisim/Hysys) are set up in “design mode” and often work poorly in “operation (rating) mode”.
  Optimization methods in commercial simulators often poor
    We can use Matlab or even Excel “on top”
J = cost feed + cost energy – value products
  …. BUT A GOOD ENGINEER CAN OFTEN GUESS THE SOLUTION (active constraints)

## Slide 34: Outline
Skogestad procedure for control structure design:
  Top Down
    Step S1: Define operational objective (cost) and constraints
    Step S2: Identify degrees of freedom and optimize operation for disturbances
    Step S3: Implementation of optimal operation
      What to control? (primary CV’s) (self-optimizing control)
    Step S4: Where set the production rate? (Inventory control)
  Bottom Up
    Step S5: Regulatory control: What more to control (secondary CV’s)?
    Step S6: Supervisory control
    Step S7: Real-time optimization

## Slide 35: Step S3. Implementation of optimal operation
Now we have found the optimal way of operation. How should it be implemented?
What to control? (primary CV’s)
  Active constraints
  Self-optimizing variables (for unconstrained degrees of freedom)

## Slide 36: Optimal operation of runner
Cost to be minimized: (total time)
One degree of freedom: power
What should we control?
Optimal operation - Runner

## Slide 37: 1. Sprinter case
100 meters run.
Active constraint control:
  Maximum speed ("no thinking required")
  CV = power (at max)
Optimal operation - Runner

## Slide 38: 2. Marathon runner case
40 km run. (total time)
What should we control? CV = ?
Unconstrained optimum:
Optimal operation - Runner
u = power
J = T
uopt

## Slide 39: Self-optimizing control: Marathon
Optimal operation - Runner
Any self-optimizing variable (to control at constant setpoint)?
  c1 = distance to leader of race
  c2 = speed
  c3 = heart rate
  c4 = level of lactate in muscles

## Slide 40: Conclusion Marathon runner
CV = heart rate is good “self-optimizing” variable
Simple and robust implementation
Disturbances are indirectly handled by keeping a constant heart rate
May have infrequent adjustment of setpoint (cs)
c = heart rate
select one measurement
c=heart rate
J=T
copt
Optimal operation - Runner

## Slide 41: Step S3: What should we control (c)?
(primary controlled variables )
Selection of controlled variables :
  Control active constraints!
  Unconstrained degrees of freedom: find and control self-optimizing variables!
Notes: First lecture: ended on this slide

## Slide 42: Sigurd’s rules for CV selection
Always control active constraints! (almost always)
Purity constraint on expensive product always active (no overpurification):
  (a) "Avoid product give away" (e.g., sell water as expensive product)
  (b) Save energy (costs energy to overpurify)
Unconstrained optimum: NEVER try to control a variable that reaches max or min at the optimum
  In particular, never try to control directly the cost J
  - Assume we want to minimize J (e.g., J = V = energy) - and we make the stupid choice os selecting CV = V = J - Then setting J < Jmin: Gives infeasible operation (cannot meet constraints) - and setting J > Jmin: Forces us to be nonoptimal (which may require strange operation; see Exercise on recycle process)

## Slide 43: Distillation: expected active constraints
valuable
product
methanol
+ max. 0.5%
water
cheap product
(byproduct)
water
+ max. 2%
methanol
methanol
+ water
Both products (D, B) generally have purity specs
Valuable product: Purity spec. always active
  Reason: Amount of valuable product (D or B) should always be maximized
    Avoid product “give-away” (“Sell water as methanol”)
    Also saves energy
Control implications:
ALWAYS Control valuable product at spec. (active constraint)
May overpurify (not control) cheap product

## Slide 44: Operation of distillation columns in series
DOF = Degree Of Freedom
Ref.: M.G. Jacobsen and S. Skogestad (2011)
Energy price: pV=0-0.2 $/mol (varies)
Cost (J) = - Profit = pF F + pV(V1+V2) – pD1D1 – pD2D2 – pB2B2
> 95% B
pD2=2 $/mol
F ~ 1.2mol/s
pF=1 $/mol
< 4 mol/s
< 2.4 mol/s
> 95% C
pB2=1 $/mol
N=41
αAB=1.33
N=41
αBC=1.5
> 95% A
pD1=1 $/mol
QUIZ: What are the expected active constraints?
1. Always. 2. For low energy prices.
QUIZ 1
With given feed and pressures (disturbances): 4 steady-state DOFs (e.g., L and V in each column)

## Slide 45: Operation of distillation columns in series
DOF = Degree Of Freedom
Ref.: M.G. Jacobsen and S. Skogestad (2011)
Energy price: pV=0-0.2 $/mol (varies)
Cost (J) = - Profit = pF F + pV(V1+V2) – pD1D1 – pD2D2 – pB2B2
> 95% B
pD2=2 $/mol
F ~ 1.2mol/s
pF=1 $/mol
< 4 mol/s
< 2.4 mol/s
N=41
αAB=1.33
N=41
αBC=1.5
> 95% A
pD1=1 $/mol
QUIZ: What are the expected active constraints?
1. Always. 2. For low energy prices.
SOLUTION QUIZ 1
With given feed and pressures (disturbances): 4 steady-state DOFs (e.g., L and V in each column)
1. xB = 95% B
Spec. valuable product (B): Always active!
Why? “Avoid product give-away”
2. Cheap energy: V1=4 mol/s, V2=2.4 mol/s
Max. column capacity constraints active!
Why? Overpurify A & C to recover more B
> 95% C
pB2=1 $/mol

## Slide 46: Control of distillation columns in series
Given
LC
QUIZ. Assume low energy prices (pV=0.01 $/mol).
How should we control the columns?
HINT: CONTROL ACTIVE CONSTRAINTS
Red: Basic regulatory loops
QUIZ 2
LC
PC
PC
LC
LC

## Slide 47: Control of distillation columns in series
Given
LC
QUIZ. Assume low energy prices (pV=0.01 $/mol).
How should we control the columns?
HINT: CONTROL ACTIVE CONSTRAINTS
Red: Basic regulatory loops
SOLUTION QUIZ 2
LC
PC
PC
LC
LC
CC
MAX V1
MAX V2
xB,s = 95%
1 unconstrained DOF (L1):
Use for what?? CV=?
Not: CV= xA in D1! (why? xA should vary with F!)
Maybe: constant L1? (CV=L1)
Better: CV= xA in B1? Self-optimizing?
General for remaining unconstrained DOFs:
LOOK FOR “SELF-OPTIMIZING” CVs = Variables we can keep constant
WILL GET BACK TO THIS!

## Slide 48: Active constraint regions for two distillation columns in series
Distillation example: Not so simple

## Slide 49: How many active constraints regions?
Maximum:
  where nc = number of constraints
BUT there are usually fewer in practice
Certain constraints are always active (reduces effective nc)
Only nu can be active at a given time
  nu = number of MVs (inputs)
Certain constraints combinations are not possibe
  For example, max and min on the same variable (e.g. flow)
Certain regions are not reached by the assumed disturbance set
Distillation
nc = 5
  25 = 32
xB always active
24 = 16
-1 = 15
In practice = 8

## Slide 50: More on: Optimal operation
Two main cases (modes) depending on market conditions:
Mode 1. Given feed rate
Mode 2. Maximum production (more constrained)
Comment: Depending on prices, Mode 1 may include many subcases (active constraints regions)
min J = cost feed + cost energy – value products

## Slide 51: Mode 1. Given feedrate
Amount of products is then usually indirectly given and
Optimal operation is then usually unconstrained
“maximize efficiency (energy)”
Control:
Operate at optimal trade-off
NOT obvious what to control
CV = Self-optimizing variable
J = cost feed – value products + cost energy
c
J = energy
copt
Often constant

## Slide 52: Mode 2. Maximum production
Assume feed rate is degree of freedom
Assume products much more valuable than feed
Optimal operation is then to maximize product rate
“max. constrained”, prices do not matter
Control:
Focus on tight control of bottleneck
“Obvious what to control”
CV = ACTIVE CONSTRAINT
c
J
cmax
Infeasible
region
J = cost feed + cost energy – value products

## Slide 53: More on: Active output constraints
Need back-off
If constraint can be violated dynamically (only average matters)
  Required Back-off = “measurement bias” (steady-state measurement error for c)
If constraint cannot be violated dynamically (“hard constraint”)
  Required Back-off = “measurement bias” + maximum dynamic control error
Jopt
Back-off
Loss
c ≥ cconstraint
c
J
  Want tight control of hard output constraints to reduce the back-off. “Squeeze and shift”-rule
The backoff is the “safety margin” from the active constraint and is defined as the difference between the constraint value and the chosen setpoint
Backoff = | Constraint – Setpoint |

## Slide 54: Motivation for better control: Squeeze and shift rule
y

## Slide 55: Example: max. throughput.
Want tight bottleneck control to reduce backoff!
Time
Back-off
= Lost production

## Slide 56: Example: purity on distillate
xB = purity of product > 95% (min.)
D2 directly to customer (hard constraint)
  Measurement error (bias): 1%
  Control error (variation due to poor control): 2%
  Backoff = 1% + 2% = 3%
  Setpoint xBs= 95 + 3% = 98% (to be safe)
  Can reduce backoff with better control (“squeeze and shift”)
D2 to large mixing tank (soft constraint)
  Measurement error (bias): 1%
  Backoff = 1%
  Setpoint xBs= 95 + 1% = 96% (to be safe)
  Do not need to include control error because it averages out in tank
xB
xB,product
±2%
D2
xB

## Slide 57: Unconstrained optimum
Control “self-optimizing” variable!
Which variable is best?
Often not obvious (marathon runner)
What are good self-optimizing variables?
  Optimal value of CV is constant
  CV is “sensitive” to MV (large gain)

## Slide 58: Conclusion optimal operation
ALWAYS:
1. Control active constraints and control them tightly!!
  Good times: Maximize throughput  tight control of bottleneck
2. Identify “self-optimizing” CVs for remaining unconstrained degrees of freedom
Use offline analysis to find expected operating regions and prepare control system for this!
  One control policy when prices are low (nominal, unconstrained optimum)
  Another when prices are high (constrained optimum = bottleneck)
ONLY if necessary: consider RTO on top of this