## Slide 1: Perspectives and future directions in control structure selection
Sigurd Skogestad
NTNU
Trondheim
16 Aug. 2017

## Slide 2: Control structure selection
Optimal: minimize cost J subject to constraints (for varying disturbances)
Cost J: Should include both economics and robustness
Optimal solution is centralized
  «One big optimizing controller» (economic MPC)
So: Control structures selection arises because we want to use non-optimal hiearchical (vertical) and/or decentralized (horizontal) decomposition
MPC / «advanced control»
PID
RTO / Extremum seeking / Manual

## Slide 3: Control structure decisions
Basic control layer (single-loop decentralized control)
  Selection of stabilizing CVs (CV2)
  Selection of MV2
  Pairing of CV2 with MV2
    Usually fairly obvious once TPM has been located
Advanced control layer (decentralized or MPC)
  Selection of «econonomic» CVs (CV1) (also when we use MPC)
    Active constraints
    Self-optimizing variables c = Hy (which require infrequent update of setpoints)
      Control structure decision: Structure of H (which measurements y?)
  Selection of MV1 to control CV1:
      CV2s / unused MV (also when we use MPC)
  Feedforward control
  Pairing of CV1 and MV1 (if decentralized control)
      Classical: «pair close» and avoid pairing on negative RGA-elements (integrity)
      New issue: Prepare for constraint switching
Supervisory control: Switching between active constraint regions
  Alternative: Single control structure in several regions (with acceptable loss)?
TPM = throughput manipulator (traditionally the feed rate)
CV1s
CV2s
MV

## Slide 4: Switching between active constraint regions (Supervisory control)
Reach new constraint (because of disturbance or setpoint change):
CV constraint
  Give up another less important CV (max/min selector)
MV constraint (the MV is used for control of a CV, otherwise it would not saturate)
  Low-priority CV (e.g., self-optimizing variable or throughput): No special action needed; Give up CV («let CV float»)
  Important CV (active constraint): Must find another MV
    Split range control (SRC) or some other logic
    Suboptimal (avoid switching): Use the other MV for valve position control (= Input resetting = Midranging)
  Notes.
  Case 1: This case is preferable so get pairing rule:
    «MV that may saturate should be paired with CV that may be given up»
    Alternative interpretaton: «Avoid using MV that may optimally saturate (steady-state) to control important CV»
  Case 2: Unless there is an «unused» MV, we must find another MV that is controlling a CV which can be given up, e.g., using a selector

## Slide 5: Switching between active constraint regions (Supervisory control)….
Designing a supervisory control system in a systematic manner requires precomputing and analyzing all possible future scenarios (caused by disturbances and price changes)
Relevant issue also for MPC
  MPC can handle some switches but not all (must anyway define priority for MPC)
Graphical can be useful
  Optimal contraint regions as function of disturbances (max- two disturbances)
  CV values / cost as function of MVs (max two MVs)

## Slide 6: Implementation of optimal operation using simple control elements
Sigurd Skogestad and Krister Forsman

## Slide 7: Basis. Want (close-to) Optimal Operation
MVs should always contribute to optimizing operation (minimize cost J)
Control active constraints
For remaining unconstrained degrees of freedom: Control self-optimizing variables (so that setpoints only need infrequent updates)
Disturbances are the main problem:
Optimal constraint variables may change!
Optimal setpoints change
Question:
How can we implement optimal operation in a simple manner?
Using feedback as our smart tool/trick!

## Slide 8: Rules
Control actice constraints
MV that may saturate should be paired with CV that may be given up
  Alternative interpretation of rule: Avoid using MV that may optimally saturate (steady-state) to control important CV (active constraint)
TPM should be located close to bottleneck
  Reason: Avoid «long loop» (and resulting backoff) when we have max. throughput
  Bottleneck: Last constraint to be reached as we increase throughput
Arrange the inventory control loops (for level, pressures, etc.) around the TPM location according to the radiation rule (Georgakis)
Select “sensitive/drifting” variables as controlled variables CV2 for regulatory control.

## Slide 9: More rules
Never control the cost function J (at fixed value)
  May give infeasibility and certainly non-optimal operation
Never do inventory control across TPM-location
  Corresponds to pairing on zero

## Slide 10: Example: Maximize flow through a cooler
TC
FC
”Traditional” structure:
Cooling water
The operator
gives the setpoint for the flow
The temperature must be kept a a given setpoint, e.g. 45 degrees.
Product
Weakness of this structure: there is no automatic mechanism that guarantees maximum flow.

## Slide 11
TC
FC
Cooling water
Product
qs
T
TCW
2 MVs: q, qcw (both have max-constraints; q<qmax, qcw<qcwmax)
2 CVs (at constraints): T=45C (always),
q = qs (can be given up if infeasible)
Cost J=? (not needed, because solution always at constraints)

## Slide 12: Active constraint regions
qs
TCW
45C
0
qmax
Infeasible region
q=qmax (bottleneck 2)
qcw=qcwmax (bottleneck 1 -> max achievable q)
Feasible region
Three active constraints regions (in all regions T=45C):
  q = qs
  qcw = max (CW valve is bottleneck)
  q = max (product valve is bottleneck)
Need control structure thatr can handle all these regions.

## Slide 13
TC
FC
Cooling water
Product
qs
T
TCW
Three active constraints regions (in all regions T=45C):
  Given setpoint for flow: q = qs
  Bottleneck 1: qcw = max (CW valve) SRC + min.select
  Bottleneck 2: q = max (product valve) No action needed, just give up q
u
u
q
qcw
u
min
SRC
SRC:

## Slide 14
TC
FC
Cooling water
Product
qs (operator)
T
TCW
u
min
Alternative, slightly suboptimal solution, using «valve position control»
VPC
Setpoint valve position for CW = at 95% of max. opening
(so some backoff)
Comment: 1. Has the advantage of not changing the controller for T.
2. With qs large (infeasible setpoint) one can have q=qmax (as long as qCW < max)
3. But cannot quite achieve fully open CW valve (so some loss = backoff)
zs

## Slide 15
TC
FC
Cooling water
Product
qs (operator)
TCW
u
min
Alternative, slightly suboptimal solution, using two temperature controllers
with different setpoints
Comment: 1. Similar to SRC, but avoids the SRC block.
2. Advantage: Two separate controllers
3. Disadvantage: Temperature a bit higher when we reach CW-constraint
Ts=
45C
Ts=
47C
TC

## Slide 16: Distillation example
DOF = Degree Of Freedom
Separate components A (light) and B (heavy)
Cost (J) = - Profit = pF F + pVV – pDD – pBB
Prices: pF=pD=1 $/mol, pB=2 $/mol, Energy pV= 0-0.2 $/mol (varies)
With given feed and pressures: 2 steady-state DOFs.
3 constraints
  Product purities (D,B) > 95%
  capacity constraint on V
xA>95%
xB>95%
Valueable product
V<4 mol/s
«Avoid product give-away» -> Valueable product constraint always active -> xB=95%
Notes: 16

## Slide 17
F
pV
xB
xB and V
Three active constraint regions (+ bottleneck):
Bottleneck!
3 active constraints:
xA, xB and V
Infeasible region
1.45
1.0
xA and xB
Region 1
Region 2
(bottleneck)
LC
LC
PC
xA
TPM
FS
FC
Regulatory control
of levels and pressure
2^2=4

## Slide 18
F
pV
xB
xB and V
Three active constraint regions (+ bottleneck):
Bottleneck!
3 active constraints:
xA, xB and V
Infeasible region
1.45
1.0
xA and xB
Region 1
Region 2
(bottleneck)
LC
LC
PC
xA
xAs=99.1% (self-optimizing; can give up)
TPM
FS
FC
CC
Region 1
CC
xBs=95% (always active!)

## Slide 19
F
pV
xB
xB and V
Three active constraint regions (+ bottleneck):
Bottleneck!
3 active constraints:
xA, xB and V
Infeasible region
1.45
1.0
xA and xB
Region 1
Region 2
(bottleneck)
LC
LC
PC
xA
xAs=99.1%
TPM
FS
FC
CC
Region 2
CC
xBs=95%
SRC
min
u
u
L
V
SRC:

## Slide 20
F
pV
xB
xB and V
Three active constraint regions (+ bottleneck):
Bottleneck!
3 active constraints:
xA, xB and V
Infeasible region
1.45
1.0
xA and xB
Region 1
Region 2
(bottleneck)
LC
LC
PC
xA
xAs=99.1%
FS
FC
CC
Bottleneck
Region (all regions)
CC
xBs=95%
SRC
min
u
u
L
V
min
CC
xAs=95%

## Slide 21
Alternatives
Recerse pairing (pair on negative RGA)
Valve position control (use L to avoid V saturating)
Problem
Price changes (pv). Must be handled by «feed forward» since they do not affect the process
That is, optimal «overpurification» setpoint (which is 99.1% in this example), depends on price pv.
At some point it becomes 95% and we have the «xA xB»-region! So all regions are handled by a single structure

## Slide 22: Operation of Distillation columns in series
DOF = Degree Of Freedom
Ref.: M.G. Jacobsen and S. Skogestad (2011)
> 95% B
pD2=2 $/mol
F ~ 1.2mol/s
pF=1 $/mol
< 4 mol/s
< 2.4 mol/s
> 95% C
pB2=1 $/mol
N=41
αAB=1.33
N=41
αBC=1.5
> 95% A
pD1=1 $/mol
QUIZ: What are the expected active constraints?
1. Always. 2. For low energy prices.
=
=
=
Cost (J) = - Profit = pF F + pV(V1+V2) – pD1D1 – pD2D2 – pB2B2
Prices: pF=pD1=PB2=1 $/mol, pD2=2 $/mol, Energy pV= 0-0.2 $/mol (varies)
With given feed and pressures: 4 steady-state DOFs.
Here: 5 constraints (3 products > 95% + 2 capacity constraints on V)
Notes: 22

## Slide 23: Control of Distillation columns. Cheap energy
Given
LC
LC
LC
LC
PC
PC
Overpurified: To avoid loss of valuable product B
CC
xB
xBS=95%
MAX V1
MAX V2
Example.
Overpurified
Overpurified
A
B
C

## Slide 24
Given
LC
LC
LC
LC
PC
PC
CC
xB
xBS=95%
MAX V1
MAX V2
CC
xAS=2.1%
Control of Distillation columns. Cheap energy
Solution.
Notes: 24

## Slide 25
Given
(TPM)
LC
LC
LC
LC
PC
PC
CC
xB
xBS=95%
MAX V1
MAX V2
CC
xAS=2.1%
What happens if we increase the federate?
Is this control structure still OK??
Notes: 25

## Slide 26
Given
(TPM)
LC
LC
LC
LC
PC
PC
CC
xB
xBS=95%
MAX V1
MAX V2
CC
xA
xAS=95%
Increase federate: Reach xA-constraint
TPM
Notes: 26

## Slide 27
LC
LC
LC
LC
PC
PC
CC
xB
xBS=95%
MAX V1
MAX V2
CC
xA
xAS=95%
Increase federate further: Reach also xC-constraint (Bottleneck)
TPM
CC
xC
xCS=95%
TPM used
as MV
Notes: 27

## Slide 28
LC
LC
LC
LC
PC
PC
CC
xB
xBS=95%
MAX V1
MAX V2
CC
xA
xAS=95%
Move TPM
CC
xC
xCS=95%
TPM (used
as MV)
Move TPM to F2 (closer to bottleneck) and rearrange level loop
Notes: 28

## Slide 29: Active constraint regions for two distillation columns in series
CV = Controlled Variable
3
2
0
1
1
0
2
[mol/s]
[$/mol]
1
Mode 1, Cheap energy: 3 active constraints -> 1 remaining unconstrained DOF (L1) -> Need to find 1 additional CVs (“self-optimizing”)
More expensive energy: Only 1 active constraint (xB) ->3 remaining
unconstrained DOFs -> Need to find 3 additional CVs (“self-optimizing”)
Energy
price
Distillation example: Not so simple
Mode 2: operate at BOTTLENECK. F=1,49
Higher F infeasible because
all 5 constraints reached
Mode 1 (expensive energy)

## Slide 30: How many active constraints regions?
Maximum:
  nc = number of constraints
BUT there are usually fewer in practice
Certain constraints are always active (reduces effective nc)
Only nu can be active at a given time
  nu = number of MVs (inputs)
Certain constraints combinations are not possibe
  For example, max and min on the same variable (e.g. flow)
Certain regions are not reached by the assumed disturbance set
Distillation
nc = 5
  25 = 32
xB always active
2^4 = 16
-1 = 15
In practice = 8

## Slide 31
MV | 1 | 2 | 3 | 4 | Bottleneck (5 constraints)
F | F | « | « | « | xC=0.95 (min.select)
L1 | xA=0.991 | XAb=0.023 (SRC+min.select)* | « | xA=0.95 (max.select) | «
V1 | XAb=0.023 | V1=max | « | « | «
L2 | xB=0.95 | « | « | « | «
V2 | xC=0.993 | « | V2=max | « | «
CV regions with suggested pairings
1
2
3
4
Bottleneck
F
V1
L1
L2
V2
xA
xB
xC
xAb
Blue: unconstrained optimal values (depend on energy price)
*Could avoid with reverse pairing in region 1 (pair on negative RGA)
5
6
7
8

## Slide 32: Constraints: xA, xC, V1, V2 (xB always active)
No constraints (1)
xA (5) (handled OK, happens when energy is expensive so xAopt reaches 95%)
xC (handled OK, happens if column 2 is shorter and energy expensive so xCopt reaches 95%)
V1 (2)
V2 (handled OK, happens if column 2 is shorter)
xA, xC (6) (handled OK)
xA, V1 (8) (NOT handled, two constraints in column 1, so will be bottleneck!)
xA, V2 (handled OK, happens if column 2 is shorter)
xC, V1 (handled OK)
xC, V2 (NOT handled, three constraints in column 2, so must use column 1 to control xC)
V1, V2 (3)
xA, xC, V1 (7) (NOT handled; bottleneck; see region 7)
xA, V1, V2 (4)
xc, V1, V2 (NOT handled, see region 10)
xA, xB, V1, V2 (Bottleneck)

## Slide 33
LC
LC
LC
LC
PC
PC
CC
xBS=95%
xA
xAS=99.1%
Solution for low federate
TPM
FS
FC
CC
CC
xAbS=2.31%
CC
xCS=99.3%
Notes: 33

## Slide 34
LC
LC
LC
LC
PC
PC
CC
xBS=95%
xA
xAS=99.1%
Solution for higher feedrate
TPM
FS
FC
CC
CC
xAbS=2.31%
min
SRC
CC
xCS=99.3%
max
max
Notes: 34

## Slide 35
LC
LC
LC
LC
PC
PC
CC
xBs=95%
CC
xA
xAs=99.1%
Solution for all regions
CC
xCs=95%
TPM
FS
min
FC
CC
CC
xAb,s=2.31%
xAs=95%
max
min
SRC
CC
xCs=99.3%
Notes: 35