## Slide 1
Degrees of Freedom
Module 1.1
ECONOMIC PROCESS DESIGN, OPERATION
& PLANTWIDE CONTROL
An Intensive Industrial Short Course
Economic Process Design, Operation and Plantwide Control 1-5 Jun 2014 IITK

## Slide 2: DOF
What am I free to change
# of variables that can be adjusted (not fixed) INDEPENDENTLY

## Slide 3: Traditional DOF Analysis
DOF =
# of independent variables
- # of independent material / energy balances
- # of equilibrium constraints
Guaranteed to fail !!!
NEED A SIMPLE AND INTUITIVE METHODOLOGY FOR DOF ANALYSIS

## Slide 4: Liquid Flow Through a Pipe
One adjustable flow
DOF = 1
Liquid Flow Rate

## Slide 5: Liquid Flow Networks
DOF = 3
Three split flows
DOF = 4
Three split flows
One mixed flow

## Slide 6: A Simple Surge Tank
2 adjustable flows
FC
FC
LC
1 level controller
(for material balance)
Control DOF = 2
Dynamic DOF = 1 (Level setpoint)
(Has only dynamic impact. No steady state impact)
Steady operation DOF = 1 (Flow setpoint)
(Sets process throughput)

## Slide 7: Tanks in Series
Control DOF = 5
LC
LC
LC
LC
FC
Steady Operation DOF = 1 (FC: Throughput)
Dynamic DOF = 4 (LCs)

## Slide 8: Heated Flash Drum
Control DOF = 4
Throughput
Temperature
Pressure
Level
FC
PC
TC
LC

## Slide 9: Non Isothermal Liquid CSTR
Control DOF = 3
Throughput
Temperature
Level (a SS dof)
FC
TC
LC

## Slide 10: Simple Distillation Column
FC
LC
PC
FC
FC
LC
TC
TC
Control DOF = 6
Throughput
Reboiler Duty or TS
Reflux rate or ratio or TR
Reflux drum level
Bottom Sump Level
Column Pressure

## Slide 11: Packed Bed Reactor
TC
PC
FC
LC
TC
TC
Control DOF = 6
Throughput
Rxr Inlet T
Rxr T
Rxr P
Condensate T
Flash drum level

## Slide 12: A Toy Process
A
B
C
Recycle A, B
A + B → C
TC
LC
FC
LC
PC
TC
LC
X
FC
FC
CC
X
Control DOF = 9
Throughput
Rxr Level
Rxr Temperature
Rxr composition
Column L/F
Column Temperature
Column pressure
Reflux drum level
Sump level

## Slide 13: DOF Exercise: Petlyuk Column

## Slide 14: DOF: Operation vs Design
Operating DOF
  Process already exists
  Equipment size is fixed
Design DOF
  Process does not exist
  Equipment not yet sized ≡ additional DOF
SS Design DOF = SS Operating DOF* + Equipment Size

## Slide 15: Steady State Design DOF Example 1
Throughput Given
Column pressure fixed
UNKNOWN EQUIPMENT SIZES
# of rectifying trays Depends on desired split
# of enriching trays Depends on desired split
Column dia Fixed by flooding
Condenser area Fixed by SS QC
Reboiler area Fixed by SS QR
Reflux drum volume 5-10 min residence time
Bottom sump volume 5-10 min residence time
SS Design DOF = 2 splits + NR+ NE = 4

## Slide 16: Steady State Design DOF Example 2
B
C
Recycle A, B
A + B → C
A
SS Design DOF = SS DOF – 1 + 2 = 7
Rxr Volume
Rxr Temperature
Rxr Composition
2 Column Splits
NR and NS

## Slide 17: The Intuitive DOF Approach
Given a process flowsheet
Show control valve on each adjustable flow
Count # of control valves
Control DOF = # of independent control valves
Steady State
Operation DOF
Control DOF
= - # of non-reactive surge drums
- any other fixed conditions (e.g. column pressure)
Design DOF =
Steady state operation DOF*
+ Major equipment sizes