## Slide 1: MPC i Statoil Stig Strand, spesialist MPC Statoil Forskningssenter 93  SINTEF Reguleringsteknikk 91-93 Dr. ing 1991: Dynamic Optimisation in State Space Predictive Control Schemes

## Slide 2: MPC in Statoil
In-house tool Septic, Statoil Estimation and Prediction Tool for Identification and Control
55 MPC applications with Septic within Statoil
Experimental step response models, built-in functionality for model gain scheduling
Flexible control priority hierarchy
Quality control by inferential models built from laboratory data or on-line analysers
DCS/PCDA interfaces currently in Septic:
  Honeywell TDC3000 (CM50 on Vax computer)
  ABB Bailey via InfoPlus (AspenTech)
  ABB Bailey via ABB OPC server
  ABB Bailey via Matrikon OPC server
  ABB Hartmann&Braun via SysLink
  Kongsberg Simrad AIM1000 (integrated)
Runs on Vax/VMS, Unix, PC (NT)
Supports mechanistic type models, generally non-linear models, for applications with wide operating regimes.

## Slide 3
Applikasjon | MV | CV | DV | Beskrivelse | Applikasjon | MV | CV | DV | Beskrivelse
MpcTordisA | 2 | 2 | 1 | Slug mottak separator | C1C2T200 | 2 | 3 | 1 | Deetaniser
MpcTordisB | 2 | 2 | 1 | Slug mottak separator | C3C4T400 | 2 | 2 | 1 | Depropaniser
LEC02MPC | 4 | 7 | 4 | Debutaniser | C3C4T400 | 2 | 3 | 1 | Debutaniser
LEC03MPC | 5 | 5 | 2 | Nafta splitter (Kondensat) | C3C4T400 | 2 | 2 | 1 | Butansplitter
LEC05MPC | 2 | 4 | 2 | C3/C4 splitter (Kondensat) | MPCPRO | 4 | 4 | 2 | C3/C4 splitter
VBMAXMPC | 3 | 13 | 1 | Fødekontrol | MPCKRA | 11 | 9 | 2 | Reaktor/regenerator seksjon
PLC04MPC | 3 | 5 | 2 | Nafta splitter APS. | MPCDES | 9 | 12 | 7 | Fraksjonering
VBC01MPC | 7 | 13 | 4 | Visbreaker fraktionator | MPCABS | 4 | 7 | 2 | Lette ender (C2-)
PSC01MPC | 7 | 9 | 1 | Atmos. destillasjon | MPCBUT | 4 | 3 | 1 | LPG/Nafta splitter
CFC01MPC | 7 | 12 | 4 | Kondensat fraktionator | MPCT601 | 11 | 7 | 4 | Delayed Coker Fraksjonering
IUC01MPC | 2 | 4 | 3 | Stabilisator, Isomerisering | MPC800 | 5 | 4 | 4 | Delayed Coker Nafta/LGO splitter
IUC52MPC | 3 | 4 | 3 | Raffinat kolonne | MPCFVRM | 7 | 18 | 14 | Råolje forvarming
IUC53MPC | 4 | 5 | 3 | Ekstrakt kolonne | HEXOPT |  |  |  | RTO råolje forvarming
VPC01MPC | 5 | 7 | 2 | Vacuum fraktionator | MPCFVRM | 4 | 4 | 2 | Råolje preflash kolonne
PLC51MPC | 6 | 6 | 1 | Deisopentanizer. | PASBAL | 7 | 9 | 0 | Råoljeovn passbalansering
MPCGASS | 12 | 21 | 2 | HCDP regulering | MPCSPLT | 4 | 5 | 1 | LPG/Nafta splitter (T-108)
MPCdeprop | 2 | 2 | 1 | Depropaniser | MPCSPLT | 2 | 2 | 5 | Lett/Medium Nafta splitter (T-112)
MPCsplitter | 2 | 2 | 1 | iC4/nC4 splitter | MPCSPLT | 2 | 2 | 2 | Lett/Medium Nafta splitter (T-113)
C3C4T100 | 2 | 2 | 1 | Depropaniser | MPCNGL | 7 | 8 | 2 | LPG/Nafta splittere (T-1104/T-1107)
C3C4T100 | 2 | 4 | 1 | Debutaniser | MPCNAF | 3 | 1 | 2 | Medium/Tung Nafta splitter (T-1105)
C3C4T100 | 2 | 2 | 1 | iC4/nC4 splitter | MPCT101 | 13 | 20 | 9 | Atmos. destillasjon
C3C4T200 | 2 | 2 | 1 | Depropaniser | MPCT1406 | 4 | 4 | 2 | Reformat stabiliseringskolonne
C3C4T200 | 2 | 4 | 1 | Debutaniser | MPCR1400 | 6 | 20 | 1 | Reformer reaktor seksjon
C3C4T200 | 2 | 2 | 1 | iC4/nC4 splitter | MPCBBL1 | 9 | 26 | 0 | Gasoline blending
C2T300 | 2 | 4 | 1 | Deetaniser | MPCBBL2 | 9 | 26 | 0 | Gasoline blending
C1C2T100 | 2 | 2 | 1 | Deetaniser | MPCA5200 | 3 | 7 | 2 | Krakkernafta svovelfjerning
 |  |  |  |  | MPCAIM | 14 | 14 | 4 | Snorre trip, SFA oljenivå/komp sugetrykk
 |  |  |  |  | 53 | 244 | 367 | 118 | INKL 1 RTO

## Slide 4: MPC briefly
Prediction horizon
Current
t
Controlled variable, optimized prediction
Manipulated variable, optimized prediction
Set point
MV blocking  size reduction
CV evaluation points  size reduction
CV reference specifications  tuning flexibility set point changes / disturbance rejection
Soft constraints and priority levels  feasibility and tuning flexibility
Process
u
v
y
x
MV
DV
CV
state

## Slide 5: Control priorities
MV rate of change limits
MV high/low Limits
CV hard constraints (”never” used)
CV soft constraints, CV set points, MV ideal values: Priority level 1
CV soft constraints, CV set points, MV ideal values: Priority level 2
CV soft constraints, CV set points, MV ideal values: Priority level n
CV soft constraints, CV set points, MV ideal values: Priority level 99
Sequence of steady-state QP solutions to solve 2 – 7
Then a single dynamic QP to meet the adjusted and feasible steady-state goals

## Slide 6: MPC – Fundamental models (first principles)
Open loop response is predicted by non-linear model
  MV assumption : Interpolation of optimal predictions from last sample
Linearisation by MV step change
  One step for each MV blocking parameter (increased transient accuracy)
QP solver as for experimental models (step response type models)
Closed loop response is predicted by non-linear model
  Compute linearisation error (difference open-loop + QP from simulated non-linear closed-loop response)
    Above threshold ---> closed-loop to "open-loop" and iterate solution
  QP solution ---> defines line search direction with non-linear model
    Possibly closed-loop to "open-loop" and iterate

## Slide 7: Implementation
Operation knowledge – benefit study? or strategy?  MPC project
Site personnel / Statoil R&D joint implementation project
(MPC computer, data interface to DCS, operator interface to MPC)
MPC design  MV/CV/DV
DCS preparation (controller tuning, instrumentation, MV handles, communication logics etc)
Control room operator pre-training and motivation
Product quality control  Data collection (process/lab)  Inferential model
MV/DV step testing  dynamic models
Model judgement/singularity analysis  remove models? change models?
MPC pre-tuning by simulation  MPC activation – step by step and with care – challenging different constraint combinations – adjust models?
Control room operator training
MPC in normal operation, with at least 99% service factor
Benefit evaluation?
Continuous supervision and maintenance
Each project increases the in-house competence  increased efficiency in maintenance and new projects

## Slide 8
GORTO flow sheet

## Slide 9
21
1
5
6
17
20
33
34
39
48
35
40
18
24
TC
1022
LP condensate
LP steam
24
LC
1026
24
PC
1010
24
TI
1018
24
LC
1009
24-HA-103
A/B
24-VA-102
24-PA-102A/B
24
FC
1008
24
TI
1021
24
LC
1010
24
TI
1038
24
TI
1020
24
PC
1020
24
PDC
1021
24
HC
1015
Cooling water
24-VE-107
24
TI
1011
24
TI
1017
24
TI
1012
24
PI
1014
24
PD
1009
24
FC
1009
24
TI
1013
Normally 0 flow, used for start-ups to remove inerts
Propane
Flare
25
FI
1003
24
TI
1005
24
LC
1001
Bottoms from deetaniser
Depropaniser Train 100 – 24-VE-107
24
AR
1005
C = C3
E = nC4
F = C5+
Debutaniser 24-VE-108
24
AR
1008
B = C2
C = C3
D = iC4

## Slide 10
Depropaniser Train 100 – 24-VE-107
21
1
5
6
17
20
33
34
39
48
35
40
18
24
TC
1022
LP condensate
LP steam
24
LC
1026
24
PC
1010
24
TI
1018
24
LC
1009
24-HA-103
A/B
24-VA-102
24-PA-102A/B
24
FC
1008
24
TI
1021
24
LC
1010
24
TI
1038
24
TI
1020
24
PC
1020
24
PDC
1021
24
HC
1015
Kjølevann
24-VE-107
24
TI
1011
24
TI
1017
24
TI
1012
24
PI
1014
24
PD
1009
24
FC
1009
24
TI
1013
Propane
Flare
Bottoms from deetaniser
25
FI
1003
Manipulated variables (MV) = Set points to DCS controllers
24
TI
1005
24
LC
1001
24LC1001.VYA
Disturbance variables (DV) = Feedforward
24
AR
1005
C = C3
E = nC4
F = C5+
Debutaniser 24-VE-108
24
AR
1008
B = C2
C = C3
D = iC4
Controlled variables (CV) = Product qualities, column deltaP ++
Normally 0 flow, used for start-ups to remove inerts

## Slide 11
Depropaniser Train100 step testing
3 days – normal operation during night
Analyser responses are delayed – temperature measurements respond 20 min earlier

## Slide 12
Depropaniser Train100 step testing – inferential models
Combined process measurements  predicts product qualities well
Calculated by 24TI1011 (tray 39)
Calculated by 24TC1022 (t5), 24TI1018 (bottom), 24TI1012 (t17) and 24TI1011 (t39)

## Slide 13
Depropaniser Train100 step testing – CV choice
Product quality predictors, with slow corrections from analyser
  Can control even if the analyser is out of service, automatic analyser fault detection
  Removes a 20 min feedback delay

## Slide 14
Depropaniser Train100 step testing – Dynamic responses/models
The dynamic models (red) are step responses, made from step-test data
  Models from 24FC1008VWA show the 3 CV responses to a reflux set point increase of 1 kg/h
  Models from 24TC1022VWA show the CV responses to a temperature set point increase of 1 degree C
  Models from 24LC1001VYA (DV) show the CV responses to an output increase of 1%.
3 t 20 min etter spranget

## Slide 15
Depropaniser Train100 step testing – Dynamic responses/models
Match between measured CV’s (pink) and modelled step responses (blue) fairly good, green is model error.
  Assumed linear responses, i.e. a reflux change of 1 kg/h gives the same product quality response whether the impurity is 0.1% or 2%. This is not correct, and the application will use logarithmic product quality transformations to compensate for the nonlinearities.

## Slide 16
Depropaniser Train100 MPC – controller activation
Starts with 1 MV and 1 CV – CV set point changes, controller tuning, model verification and corrections
Shifts to another MV/CV pair, same procedure
Interactions verified – controls 2x2 system (2 MV + 2 CV)
Expects 3 – 5 days tuning with set point changes to achieve satisfactory performance

## Slide 17
Depropaniser Train100 MPC – further development
Commissions product quality control January 2004, i.e. MPC manipulates reflux and tray 5 temperature SP to control top and bottoms product quality.
Product quality predictors will be evalutaed and recalibrated if necessary.
If boil-up constraints:
  MV: steam pressure SP 24PC1010.VWA, CV: boiler level SP 24LC1026.VWA with high/low limits.
If limited LP steam (plant-wide):
  Specify max acceptable impurity in both ends (CV SP) (10-15% reduced steam consumption)
  Marginal: MV: column pressure (24PC1020.VWA), CV: pressure controller output (24PC1020.VYA) with high/low limits. Low MV ideal value that decreases pressure against output limitation (1-3% reduced steam consumption)
If Train 100 capacity test gives column flooding:
  CV: column differential pressure, with high limit.
  Specify max acceptable impurity in both ends (10-15% increased capacity compared to normal product purity)
  Adjust feed flow (by adjusting Train 100 feed) against differential pressure high limit (see below)
2005/2006: Capacity control for Train 100 to push feed continuously against one or more processing constraints.
Resources for continuous MPC maintenance important

## Slide 18
Depropaniser Train 100 – 24-VE-107
21
1
5
6
17
20
33
34
39
48
35
40
18
24
TC
1022
LP Kondensat
LP Damp
24
LC
1026
24
PC
1010
24
TI
1018
24
LC
1009
24-HA-103
A/B
24-VA-102
24-PA-102A/B
24
FC
1008
24
TI
1021
24
LC
1010
24
TI
1038
24
TI
1020
24
PC
1020
24
PDC
1021
24
HC
1015
Kjølevann
24-VE-107
24
TI
1011
24
TI
1017
24
TI
1012
24
PI
1014
24
PD
1009
24
FC
1009
24
TI
1013
Propan
Fakkel
Bunn ut deetaniser
25
FI
1003
24
TI
1005
24
LC
1001
24LC1001.VYA
24
AR
1005
C = C3
E = nC4
F = C5+
Debutaniser 24-VE-108
24
AR
1008
B = C2
C = C3
D = iC4
24
AY
1008D
24
AY
1005C
slow update
slow update
24PC1020.VYA
MPCCAP
Train 100
One of the constraints that
MPCCAP must respect
Normally 0 flow, used for start-ups to remove inerts
Manipulated variables (MV) = Set points to DCS controllers
Disturbance variables (DV) = Feedforward
Controlled variables (CV) = Product qualities, column deltaP ++

## Slide 19: MPC Crude Distillation Unit
20 controlled variables (CV) – 18 with high/low limits, 3 with set points
13 manipulated variables (MV) – all with high/low limits, 10 with ideal values
6 measured disturbance variables (DV)
1 minute sample time, 84 samples control horizon, 120 samples prediction horizon
120 step response models, some with gain scheduling, longest models 200 samples
6 optimization variables per MV (piecewise constant, change at samples 0, 4, 12, 28, 52, 84)
8 - 11 evaluation points per CV
1 relaxation parameter per CV limit (constraint relaxation), 24 relaxation parameters in total, appropriate individual CV evaluation dead-time (constraint window)
8 subsequent calls to QP-solver to resolve hierarchy of priorities in steady state
1 call to QP-solver for dynamic control solution
2.4 seconds computation time (data read, pre-calculations, MPC solution, data write, GUI communication), PC with 2 GHz CPU
99% service factor