## Slide 1: Negative feedback amplifier
Sigurd Skogestad
2024

## Slide 2: Linearizing effect of feedback

## Slide 3: The negative feedback amplifier
Amplification was required to send telephone signals across the US in the 1920s and it required 12 amplifications on the way, so they better be fairly accurate.
The original idea of all engineers is to think feedforward (Bell Labs)
Y = BAD y
Harold Black (on a New York ferry, 02 August 1927):

## Slide 4
100
1000
10000
10
Bad amplifier:
Accurate resistance:
Get
Resulting amplification (negative feedback)
Experiment
Proving that Black’s invention worked also initiated the idea of freqyency analysis( Nyquist)

## Slide 5: Linearization of valve using cascade control
LC
y=H
Hs
flow in
flow out
MV=z
valve position
WITHOUT CASCADE
WITH CASCADE (2 controllers)
measured
flow
LC
Hs
flow in
flow out
MV=qs
FC
y2=q
MV2=z
master
slave
measured
level
measured
level
y=H
Benefits: 1. Local distrurbance rejection, 2. Linearization
Does nonlinearity disappear?

## Slide 6: No, it moves to the time constant for slave loop – OK if we we have time scale separation between master and slave
Nonlinear valve with varying gain k2: G2(s)= k2(z) / (s+1)
  Slave (flow) controller K2: PI-controller with gain Kc2 and integral time I= (SIMC-rule). Get
  With slave controller: Transfer function T2 from y2s to y2 (as seen from master loop):
T2 = L2/(1+L2) = 1/(C2 s + 1), where C2 = /(k2 Kc2)
Linearization: Gain for T2 is always 1 (independent of k2) because of intergal action in the inner (slave) loop
But: Gain variation in k2 (inner loop) translates into variation in closed-loop time constant C2. This may effect the master loop
f(z)
0
1
0
1
linear valve
k2(z) = slope = df/dz
G1T2 = «Process» for tuning master controller K1